## Slide 1: Review of EPC Gen2 for Long Range Backscatter
Date: 2025-03-12
Authors:

## Slide 2
Abstract
Why is it important to distinguish long-range Backscatter from EPC-inspired close-range Backscatter?
Discuss the gaps in encapsulating EPC Gen2 at the MAC layer for long-range backscatter.

## Slide 3: Why long-range Backscatter
There are many use-cases with range >1m presented in the Technical report on support of AMP IoT devices in WLAN [1] and many submissions [2-4]

## Slide 4: Advantages of EPC Gen2 protocol
There is a wide consensus on using EPC Gen2 for close range backscatter.
Many proposals to encapsulate the UHF RFID Interrogator commands and Tag replies.[5]
Easy to extend to support AMP + UHF RFID operations

## Slide 5: EPC Gen2 in 2.4GHz for long-range
Direct extension of EPC Gen2 is not straight forward
We should resolve the following issues:
  Presence of multiple independent readers in the range of a tag.
  Implementation of Tag Identification protocol in a single TXOP of a 2.4GHz band.
  Privacy protection in EPC Gen2 is difficult.
  Difficult to implement Slotted Aloha based protocol for a long-range in 2.4GHz band in the presence of competing 802.11 traffic.

## Slide 6: Multiple Independent readers
EPC Gen2 protocol needs coordination between multiple readers working in the near vicinity of each other.
Hard to schedule multiple independent readers in a B2C scenario when the range is not close.
Tag may respond to a non-intended reader with a “Session No”
of high persistence value and moved to ‘B’ state [8].
For example, two different customers in a store with AMP readers on their cell phones. One close to an AMP-Tag, but the other one at a distance reads it first and makes the AMP-Tag go silent.

## Slide 7: Tag Identification protocol in a single TXOP
Others like [5] proposed encapsulating the UHF RFID Interrogator commands and tag replies like the following
But it isn’t easy to do this full sequence in a single TXOP in 2.4 GHz, especially in AC_BK access category.
It will be more difficult to achieve this at longer range.
In addition to the challenges of EH mentioned in [6], it will make it more difficult.

## Slide 8: Privacy protection in EPC Gen2
In long-range privacy requirements may be different
There are use-cases requiring the infrastructure to address each tag with a unique address without an inventory round.
Provisioning and authorization mechanisms would require more than a simple wrapper of AMP over EPC GEN2.

## Slide 9: AMP-tags with other STA in the 2.4GHz band
In 2.4GHz devices communicate on different channels.
AMP + UHF RFID tags are supposed to work without a channelized receiver [7].
This makes it difficult to avoid collisions
In the presence of an interfering PPDU
difficult for the tag to decode the AMP fields

## Slide 10: Conclusion
We need to redesign some part of the EPC inspired AMP-MAC protocol for long-range.
There are some non-trivial challenges in adapting EPC Gen2 for long-range backscatter.
The combined results of these issues can magnify the problem.

## Slide 11: References
[1] Technical Report on support of AMP IoT devices in WLAN, 11-23/2203
[2] Zhisong Zuo et al., Use Cases for AMP IoT Devices, 11-22/0963,
[3] Wei Lin et al., Follow Up on AMP Link Budgets, 11-24/0075
[4] Wei Lin et al., Feasibility study on long range backscatter operation, 11-24/1215
[5] Rojan et al. Thoughts on AMP UHF RFID Tags, 11-24/0836
[6] Dror et al. UL Monostatic and Bistatic Range Extension Considerations, 11-24/0307
[7] Rui et al., Close-range AMP WiFi Reader Feasibility Study Follow up, 11-24/0798
[8] EPC UHF Gen2 Air Interface Protocol | GS1