## Slide 1: Reachability of mmWave Link- Follow Up
Date: 2025-04-08
Authors:
Name | Affiliation | Address | Phone | Email
Insik Jung | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | insik0618.jung@lge.com
Eunsung Park |  |  |  | esung.park@lge.com
Insun Jang |  |  |  | insun.jang@lge.com
Dongju Cha |  |  |  | dongju.cha@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
HanGyu Cho |  |  |  | hg.cho@lge.com
Sang Kim |  | 10680 Treena St 550, San Diego CA 92131 |  | sanggook.kim@lge.com

## Slide 2: Introduction
MmWave reachability estimation in sub-7GHz band can provide following benefits
  It can prevent direct scanning of mmWave link so that STA computation burden can be minimized
  It doesn’t require mmWave beam training procedure for the reachability estimation, which consumes lots of wireless medium
However, estimation in sub-7GHz only can be risky
  mmWave specific characteristics can emerge (e.g., blockage)
Therefore, we propose a two-step reachability estimation for IMMW
  First step is the estimation in sub-7GHz, aiming rough estimation
  Second step is the estimation in mmWave band, using beam training procedure

## Slide 3: Reachability Estimation Structure
Initial Reachability Estimation in Sub-7GHz [1]
  Rough estimation which cannot fully consider mmWave characteristics
  Find STAs which are highly likely to be reachable in mmWave band
Reachability Update in mmWave
  Conduct beam traning only to the STAs which are initially estimated as ‘reachable’
  Based on the RSSI obtained in beam training procedure, reachabilty can be updated
blockage
STA 1
reachable
STA 2
unreachable
STA 3
reachable
Initial reachability estimation in sub-7GHz
Reachability update in mmWave
blockage
STA 1
reachable
STA 2
unreachable
STA 3 (Updated)
Reachable
 Unreachable
Beam training of STA 1 and STA 3
AP
AP

## Slide 4: Initial Reachability Estimation (1/2) [1]
AP side reachability estimation
  APs need the reachability estimation for proper scheduling
  To reduce the STA side computation burden
DL reachability estimation
  For the reachability estimation, an AP needs mmWave RX antenna gain of the STA and pathloss
  For the path-loss estimation, an AP needs EIRP of sub-7 UL transmission
UL reachablity estimation
  For the reachability estimation, an AP needs mmWave EIRP of the STA and pathloss
  For the path-loss estimation, an AP needs EIRP of sub-7 UL transmission

## Slide 5: Initial Reachability Estimation (2/2) [1]
Required parameters for mmWave reachability . estimation
Reachability announcement
sAP
sSTA
Reachability estimation
    Transmit power of the non-AP STA in mmwave link
    Transmit antenna gain of the non-AP STA in mmwave link
    Receive antenna gain at the non-AP STA side in mmwave link
    Transmit power of the non-AP STA in sub-7GHz link
    Transmit antenna gain at the non-AP STA side in sub-7GHz link
EIRP of mmWave
EIRP of sub-7
    DL reachability
    UL reachability
    sAP: AP in a sub-7GHz link
    sSTA: STA in a sub-7GHz link

## Slide 6: Practical Reachability Estimation
Next step of the initial reachability estimate
  For the STAs which are estimated as ‘reachable’, AP conducts beam training procedure to be ready for data transmission
  Not only to align the beam direction, beam training can be utlized to estimate the practical reachability
Best TX beam
Best RX beam
  We can measure the actual RSSI with the best beam directions determined in the beam training procedure
  Based on the actual RSSI, we can estimate the practical reachability

## Slide 7: Practical Reachability Estimation Example (1/2)
Beam Training Methods
  AP announces the beamforming training (BFT) period in a sub-7GHz link
  Multiple STAs may participate in the BFT procedure.
  Detailed beam training schedule/procedure/signaling needs further discussion
mAP
mSTA(s)
Beam training schedule frames
Reachability Response
Medium Busy
Or BFT Trial
sAP
sSTA(s)
Beam Training Procedure
    mAP: AP in a mmWave link
    mSTA: STA in a mmWave link

## Slide 8: Practical Reachability Estimation Example (2/2)
Reachability Response in the Sub-7 GHz link
  We may need a “Reachablilty Response” frame transmitted from STAs for the AP to clearly notice the practical reachability
    AP then can manage those reachable/unreachable STAs properly
  If the BFT was successful, both AP and STA can receive the feedback for BFT in mmWave link and notice that both DL and UL are reachable.
  If the AP couldn’t receive the STA’s feedback, we have some ambiguities
    If STA(s) is dedicated, AP can’t distinguish whether UL was not reachable or the medium was busy during BFT period. Signaling of ‘Medium Busy’ in “Reachability Response” frame may solve this issue
      0: medium was busy, 1: medium was idle
    If STA(s) is not dedicated, AP can’t notice which STA tried the BFT. STA may need to transmit “Reachability Response”frame including the ‘BFT Trial’ field to notify that.
      E.g., 0: BFT tried, 1: reserved

## Slide 9: Conclusion
We have proposed two step reachability estimation method for mmWave band
  First step is a rough estimation in sub-7GHz link
  Second step is a practical estimation in mmWave link using the beam-training procedure

## Slide 10: Reference
[1] 11-24-0805-01, Reachability of mmWave Link, LGE
[2] 11-24-0823-01, IMMW further simplications to promote IMMW adoption, Samsung

## Slide 11: Straw Poll #1
Do you support the following text in TGbq?
  TGbq defines a mechanism to estimate reachability between STAs operating on a link in a mmWave band
    How to estimate the reachability is TBD
Y/N/A: //

## Slide 12: Straw Poll #2
Do you support the following text in TGbq?
  TGbq defines a mechanism to estimate the reachablity of a mmWave link which is conducted in a sub-7GHz link
Y/N/A: //

## Slide 13: Straw Poll #3
Do you support the following text in TGbq?
  TGbq defines a reachability estimation mechanism of a mmWave link which is conducted only by an AP in a sub-7GHz link
Y/N/A: //

## Slide 14: Straw Poll #4
Do you support the following text in TGbq?
  To estimate reachability of a mmWave link, a STA can deliver some information to another STA in the sub-7GHz link
    Detailed information is TBD but we can consider the followings
      Sub-7GHz EIRP
      mmWave EIRP
      mmWave RX antenna gain
Y/N/A: //

## Slide 15: Straw Poll #5
Do you support the following text in TGbq?
  TGbq supports a mechanism for a STA to deliver the estimation result of the mmWave link’s reachablity to another STA through sub-7GHz link
Y/N/A: //

## Slide 16: Straw Poll #6
Do you support the following text in TGbq?
  If some STAs are estimated as unreachable in a initial reachability estimation of a mmWave link conducted in a sub-7GHz link, those STAs are excluded in the following beamforming trainings in the mmWave link
Y/N/A: //

## Slide 17: Straw Poll #7
Do you support the following text in TGbq?
  A STA needs to report some information to resolve the ambiguity in UL reachability of its mmWave link through the sub-7GHz link if the beamforming training in mmWave link is failed.
Y/N/A: //
Notes: UL reachability의 모호성을 해결하기 위한 것이 갈 수 있다

## Slide 18: mmWave Reachability
System Model
AP
MLD
Non-AP MLD
Link 1 (L1) : sub-7GHz link
Link 2 (L2) : mmWave link
We want to estimate link 2’s reachability using frame exchanges in link 1
AP 1
AP 2
STA 1
STA 2

## Slide 19: Reachability Estimation (1/4)
DL reachability
  If estimated received power exceeds given threshold, we can judge that the link is reachable
  =
    : Estimated receive power at the non-AP STA side in a mmwave link
    : Transmit power of AP in a mmwave link
    : Transmit antenna gain of AP in a mmwave link
    : Pathloss of mmwave link
    : Receive antenna gain of non-AP STA in a mmwave link
    : Margin to compensate some impairments or blockage in a mmwave link
  Since AP knows its own parameters (, ), remaining two parameters (, ) need to be given
    Pathloss: It can be estimated based on the pathloss of the sub-7GHz link.
    : It should be delivered from non-AP STA

## Slide 20: Reachability Estimation (2/4)
  mmWave pathloss
    Ideally, mmwave path-loss can be represented as below
        path-loss constant
        : mmWave center frequency
        path-loss exponent
        distance between AP and non-AP STA
      However, in practical environment, additional factors (blockage, shadowing…) need to be considered.
      We need further study to handle those factors
    We can derive the distance between AP and non-AP STA as follows:
    Since AP knows its own parameters (,), remaining two parameters (,) need to be given

## Slide 21: Reachability Estimation (3/4)
  In summary, the parameters below should be delivered from non-AP STA for DL reachability estimation
    : RX antenna gain at the non-AP STA side in mmwave link
    Transmit power of the non-AP STA in sub-7GHz link
    : TX antenna gain at the non-AP STA side in sub-7GHz link

## Slide 22: Reachability Estimation (4/4)
UL reachability
  =
  Since AP knows its own parameters (), remaining three parameters (, , ) need to be given
  Similar to DL reachability case, we need two parameters (,) for the pathloss estimation.
  In summary, the parameters below should be delivered from non-AP STA for UL reachability estimation
    : Transmit power of the non-AP STA in mmwave link
    : Transmit antenna gain of the non-AP STA in mmwave link
    Transmit power of the non-AP STA in sub-7GHz link
    : Transmit antenna gain at the non-AP STA side in sub-7GHz link

## Slide 23: Required Signaling
Required signaling for the DL&UL reachability estimation
  Let us take the union of parameters for DL and UL reachability estimation
  Following parameters need to be delivered from non-AP STA
    : Transmit power of the non-AP STA in mmwave link
    : Transmit antenna gain of the non-AP STA in mmwave link
    : Receive antenna gain at the non-AP STA side in mmwave link
    Transmit power of the non-AP STA in sub-7GHz link
    : Transmit antenna gain at the non-AP STA side in sub-7GHz link
  For overhead reduction, we can also consider following signaling
    Combine tx power and tx antenna gain into EIRP
    Consider delta txpower/EIRP for the mmWave link from sub-7GHz link