## Slide 1: Considerations on NPCA Conditions
Date: 2025-03-03
Authors:

## Slide 2: Introduction
NPCA has been defined in SFD and described in Draft 0.1 [1-3].
In this contribution, we propose methods to improve the NPCA operation further.

## Slide 3: Recap: Non-primary channel access (NPCA)
  In TGbn SFD (24/0209r9), Subclause 3.4
    TGbn defines a mode of operation that enables a STA to access the secondary channel while the primary channel is known to be busy due to OBSS traffic or other TBD conditions.
      The mode of operation shall not assume that the STA is capable to detect or decode a frame and obtain NAV information of the secondary channel concurrently with the primary channel.
      A BSS shall only have a single NPCA primary channel (name TBD) on which the STA contends while the primary channel of the BSS is known to be busy due to OBSS traffic or other TBD conditions.
    [Motion #11, [1] and [21-30]]

## Slide 4: NPCA Operation
AP1 and OBSS STA are hidden to each other. OBSS STA is exposed to STA2.
AP1 exchanges CTS/RTS frames with STA1 with an intra-BSS NAV beginning from T0, followed by transmitting PPDU1 to STA1. STA1 fail to response a BA.
STA2 detects an OBSS transmission on PCH with a Basic NAV set beginning from T1. As such, STA2 performs NPCA by switching from PCH to NPCA PCH.
AP1 sends CF-end to STA2 in PCH and intend to transmit a PPDU2 to STA2. However, since STA2 operates in NPCA PCH during time portion 2, STA fails to receive CF-end in PCH.

## Slide 5: NPCA Solution
AP/STA is configured to disable NPCA during intra-BSS NAV (if the intra-BSS NAV is non-zero).
STA2 remain to operate in PCH during time portion 2 to receive CF-end via PCH, followed by receiving PPDU2 transmitted from AP1.

## Slide 6: Summary
In this contribution, we shared some thoughts of conditions of NPCA operation.
  When an NPCA STA detects an inter-BSS PPDU being received via the PCH, the NPCA STA should not switch to NPCA PCH if an intra-BSS NAV of the STA is non-zero .

## Slide 7: Straw Poll
SP1. Do you support defining an NPCA operation that includes the following?
  An NPCA STA should(/may) not switch to NPCA primary channel if an intra-BSS NAV of the STA is non-zero when the NPCA STA detects an inter-BSS PPDU being received via the PCH.
  Yes
  No
  Abstain

## Slide 8: References
Draft P802.11bn D0.1
24/1762, PDT-MAC-NPCA
24/0209: Specification Framework for TGbn, Ross Jian Yu (Huawei)