## Slide 1: New CCA Schemes for IMMW
Date: 2025-03-04
Authors:

## Slide 2: Introduction
IMMW expands the Multi-link Operation (MLO) defined in the sub-7 GHz band specifications to support non-standalone operation in the mmWave bands (between 42 GHz and 71 GHz).
We consider that each mmWave STA (mSTA)
  can be paired with one other mSTA through the IMMW AP in the sub-7 GHz band.
  can request pairing with another mSTA if it wishes to communicate with it.

## Slide 3: Problem Statement
Paired mSTAs can communicate with each other using directional antenna patterns in the mmWave band. However, two problems arise regarding CCA.
  Omni-directional single antenna CCA might not provide enough link budget. CCA may need to be conducted using directional antenna array.
  The antenna pattern (RX) for CCA does not necessarily align with the antenna pattern for transmission (TX). This misalignment can result in delayed transmissions or interference with other mSTAs.
  An mSTA may detect different transmissions, each with its own NAV duration, from various directions while performing CCA. Determining how to update the NAV timer(s) when multiple transmissions are detected is a complex and implementation dependent problem.
To address these problems, we propose new CCA schemes for IMMW.

## Slide 4: Proposed Scheme 1
Each mSTA’s antenna patterns are calibrated, meaning that the receive antenna pattern (for CCA) aligns with the transmit antenna pattern (for transmission).
  For example, one can use different Antenna Weight Vectors (AWV) for transmitting and receiving. By adjusting these AWVs, the transmit antenna pattern can be made to closely align with the receive antenna pattern.
For scheme 1, we propose that an mSTA performs CCA check only for the direction it wishes to transmit.
  maintains a single NAV timer and backoff counter.
    If multiple transmissions are detected, update the NAV to the longest duration.
  follows Enhanced Distributed Channel Access (EDCA) rules for channel access.
  when allowed to transmit, transmits in the direction in which it performs CCA.

## Slide 5: Proposed Scheme 1
Illustrating scheme 1 with an example.
  mSTA1 is paired with mSTA3. Before transmitting to mSTA3, mSTA1 performs CCA only in direction 2 (assuming mSTA1 uses four antenna patterns to cover CCA direction 1 through 4).
  Meanwhile, mSTA5 starts transmitting to mSTA4. mSTA1 detects mSTA5’s transmission and updates its NAV accordingly.
  Once the NAV clears, mSTA1 performs CCA in direction 2 and follows EDCA rules to transmit to mSTA3. Since mSTA1’s antenna patterns are calibrated, it can perform CCA and transmit in the same direction, i.e., direction 2 in this case.
mSTA2
mSTA5
CCA direction 2
CCA direction 3
CCA direction 4
mSTA4
mSTA3
mSTA1
CCA direction 1

## Slide 6: Proposed Scheme 2
The mSTA’s antenna patterns are not calibrated, meaning that the receive antenna pattern (for CCA ) does not necessarily align with the transmit antenna pattern (for transmission).
For Scheme 2, we propose that an mSTA scans all directions for CCA check using directional antenna patterns.
  maintains a single NAV timer and backoff counter.
    If multiple transmissions are detected, update the NAV to the longest duration among them.
  follows EDCA rules for channel access.
  suspends backoff if CCA is busy during the scanning or NAV is set.
  transmits when the NAV clears and the backoff counter reaches zero.

## Slide 7: Proposed Scheme 2
Illustrating scheme 2 with an example.
  All mSTAs are within the same BSS. mSTA1 is paired with mSTA2. Before transmitting to mSTA2, mSTA1 uses four wide antenna patterns to scan the surroundings for CCA.
  Meanwhile, mSTA4 is transmitting to mSTA3, and mSTA5 is transmitting to mSTA6. mSTA1 detects these two transmissions during CCA scanning and sets its NAV to the longest duration among them.
  Once the NAV clears, mSTA1 performs CCA in all four directions. If CCA indicates a busy channel in any direction, mSTA1 suspends the backoff. Following EDCA rules, mSTA1 can transmit to mSTA2 when the NAV timer clears and the backoff counter reaches zero.
mSTA6
mSTA5
mSTA4
mSTA3
CCA direction 1
CCA direction 2
CCA direction 3
CCA direction 4
mSTA2
mSTA1

## Slide 8: Proposed Scheme 3
The mSTA’s antenna patterns are not calibrated.
For Scheme 3, we propose that an mSTA performs CCA check using omni-directional single antenna. The CCA threshold should be adjusted due to lack of directional gain from single antenna.
  maintains a single NAV timer and backoff counter.
    If multiple transmissions are detected, update the NAV to the longest duration among them.
  follows EDCA rules for channel access.
  suspends backoff if CCA is busy during the scanning or NAV is set.
  transmits when the NAV clears and the backoff counter reaches zero.

## Slide 9: Summary
We proposed new CCA schemes for IMMW.
  Scheme 1: For a calibrated mSTA, it can perform directional CCA.
  Scheme 2: For an uncalibrated mSTA, it uses directional antenna patterns to scan all directions for CCA.
  Scheme 3: For an uncalibrated mSTA, it uses omni-directional single antenna for CCA.

## Slide 10: Straw Poll 1
Do you agree that IMMW allows a calibrated mSTA to perform CCA only in the direction it wishes to transmit?

## Slide 11: Straw Poll 2
Do you agree that IMMW requires an uncalibrated mSTA, if using directional antenna patterns, to scan all directions for CCA?

## Slide 12: Straw Poll 3
Do you agree that when an IMMW mSTA uses an omni-directional single antenna for CCA, the CCA threshold should be adjusted?

## Slide 13: References