## Slide 1: Follow-up on WPT: Protocol, Waveform and PPDU
Date: 2025-03-13
Authors:
Name | Affiliation | Address | Phone | Email
Yinan Qi | OPPO |  |  | v-qiyinan@oppo.com
Weijie Xu |  |  |  | 
Chuangfeng He |  |  |  | 
Doc.: IEEE 802.11-25/0320r1
March 2025

## Slide 2: Abstract
In this contribution, we discuss the following issues:
  WPT protocol between AP and AMP device
  Co-existence of WPT signals
Doc.: IEEE 802.11-25/0320r1

## Slide 3
Recap of Progress
  Agreement: IEEE 802.11bp defines a mechanism that allows an AMP non-AP STA to report its energy harvesting and power related information to AMP AP STA. The parameters that are included in the report and how to report such information is TBD.
  Energizer can potentially transmit other signals, e.g., preamble, wake-up signal, etc.
  Two main challenges
    How does the AMP STA report to the AP?
    What information should be conveyed in this report?
Yinan Qi (OPPO)
Slide 3
Doc.: IEEE 802.11-25/0320r1
March 2025

## Slide 4
WPT Protocol: AMP non-AP STA Reporting
  Long-term/non-periodic v.s. short-term/periodic feedback
    Long-term/non-periodic feedback info
      Less frequent, sometimes only once
      Can be done at the beginning of communication or upon the request of the AP
      Information such as EH related information, energy storage related information, etc.
    Short-term/periodic feedback info
      More frequent and can be real time
      In formation such as power status/requirements
Yinan Qi (OPPO)
Slide 4
Doc.: IEEE 802.11-25/0320r1
March 2025

## Slide 5
WPT Protocol: AMP non-AP STA Reporting
  Joint reporting v.s. individual reporting
    Joint reporting
      Less signalling overhead and less energy consumption
      Power category can jointly indicate the power status of the AMP non-AP STAs [1]
    Individual reporting
      High signalling overhead and high energy consumption
    Joint reporting can be baseline and individual reporting can be optional and only reported when necessary.
Yinan Qi (OPPO)
Slide 5
Doc.: IEEE 802.11-25/0320r1
March 2025

## Slide 6
WPT PPDU: Co-existence Issue
  Two co-existence cases
    Co-existence between WPT signals should be allowed
      No interference issue
      Maybe even beneficial with mutual enhancement
Yinan Qi (OPPO)
Slide 6
Doc.: IEEE 802.11-25/0320r1
March 2025
    Co-existence between WPT signals and other 802.11 systems on S1G, e.g., 802.11ah, or even non-WiFi S1G systems, e.g., Smart Utility Networks, Low Energy, Critical Infrastructure Monitoring, etc.
      May cause heavy interface since the high Tx power of WPT to reach the AMP devices

## Slide 7
WPT Procedure
Yinan Qi (OPPO)
Slide 7
Doc.: IEEE 802.11-25/0320r1
March 2025
    The energizer can do ED first.
    In the case of collision, the energizer needs to keep listening to the channel. If a preamble is detected, the energizer knows the signal is WPT signal and it can transmit its own WPT signal.
    Otherwise, it no preamble is detected, the energizer assumes the signal in the air is communication signal and does backoff.
  Design WPT signal that can be fully or partially understood by the energizer  WPT preamble.
  AP can coordinate the WPT procedure and control the Tx of WPT signal from the energizers.
  Challenge: AP may not be able to reserve S1G channel for WPT
  Energizer needs to do LBT by itself on S1G

## Slide 8: Reference
[1] “AMP Device Power Status,” IEEE 802.11-24/1381r0, Aug. 2024
Doc.: IEEE 802.11-25/0320r1
March 2025

## Slide 9
SP1
  Do you agree to capture the following text to TGbp SFD?
    AMP devices shall support joint reporting of energy and power related information, e.g., power status, to the AP during activation or upon the request of the AP?
      The details on how to define power status are TBD
Yinan Qi (OPPO)
Slide 9
Doc.: IEEE 802.11-25/0320r1
March 2025

## Slide 10
SP2
  Do you agree to capture the following text to TGbp SFD?
    WPT signals are allowed to overlap with each other.
Yinan Qi (OPPO)
Slide 10
Doc.: IEEE 802.11-25/0320r1
March 2025

## Slide 11
SP3
  Do you agree to capture the following text to TGbp SFD?
    11bp specifies, in S1G, WPT PPDU format with at least a preamble and a charging field?
Yinan Qi (OPPO)
Slide 11
Doc.: IEEE 802.11-25/0320r1
March 2025