## Slide 1: Follow-up on sync field for AMP PPDU
Date: 2025-03-10
Authors:
Name | Affiliation | Address | Phone | Email
Wang Ke | OPPO |  |  | wangke6@oppo.com
Jinyu Zhang |  |  |  | xuweijie@oppo.com
Weijie Xu |  |  |  | v-qiyinan@oppo.com
Yinan Qi |  |  |  | 
Sehngjiang Cui |  |  |  | 
Doc.: IEEE 802.11-25/0321r0
March 2025

## Slide 2: Abstract
In our previous contribution[1], we discussed the requirement, design criterion of AMP sync. A candidate sync sequence was proposed and based on it, we do comprehensive simulations to check the synchronization performance and the consequent impact on data channel decoding.
In this contribution, we further update the simulation results. Based on that, we give our proposal.
Doc.: IEEE 802.11-25/0321r0

## Slide 3: Recap:High-level requirements for AMP sync(1)
In [1]. the following requirements for AMP sync are discussed.
  Different sync sequences for DL/UL for indication.
  Support two different AMP DL rate
    e.g. 1Mbps and 250kbps using 2 different sync
    A correlator can distinguish between Sync length 16 and 32.
  The Sync sequence has the same number of 1 and 0.
  Good auto-correlation
  The sequence have 3 consecutive 1/0, which can help distinguish synchronization field and data field with Manchester coding.
Doc.: IEEE 802.11-25/0321r0

## Slide 4: Recap: High-level requirements for AMP sync(2)
During previous meeting, sync field for different receiver type have been discussed.
  For some device type, e.g. close-range dual-mode RFID-like AMP STA, it may not have correlator in the its receiver
Therefore, it needs to consider both receiver types with and without correlator inside.
For the AMP device without correlator, it will use sequence matching for AMP sync field detection.
  False alarm rate is the key metric, which relates to the length of sync sequence
  The sync sequence needs to be decode by the receiver, Manchester coding is necessary to guarantee the decoding performance
Doc.: IEEE 802.11-25/0321r0

## Slide 5: Recap: Auto-Correlation Metrics
For high data rate：[]
For low data rate: [S S]
Local reference sequence:
Doc.: IEEE 802.11-25/0321r0

## Slide 6: Recap: Cross-Correlation Metrics
The Sync sequence will be correlated with other filed of the UL/DL PPDU e.g., random Manchester coding symbols to see the cross-correlation property
  The sync sequence shall maintain low cross-correlation with other filed of UL/DL PPDU
Doc.: IEEE 802.11-25/0321r0

## Slide 7: Recap: Sync sequence length(1)
For length 8, the auto-correlation is not so good and cross-correlation with random Manchester symbols become unacceptable.
  One sequence after computer searching is '10001101'
Doc.: IEEE 802.11-25/0321r0
AC_H: -4 AC_L: 2
Cross-correlation with Random Manchester symbols

## Slide 8: Recap：Sync sequence length(2)
For length 16, the auto-correlation is better and cross-correlation with random Manchester symbols is good
  One candidate sequence after computer searching is '1100100101011100'
Doc.: IEEE 802.11-25/0321r0
AC_H: -4 AC_L: 4
Cross-correlation with Random Manchester symbols

## Slide 9: Simulation assumptions for sync performance evaluation
  Note: For ED receiver, it directly receiver the RF signal and derive its envelope, then it samples the OOK envelope and perform correlation detection. For IF receiver, RF signal is converted to baseband signal and then it samples the baseband OOK signal and perform correlation detection.
Doc.: IEEE 802.11-25/0321r0
Parameters | Values
Sync sequence | 1100100101011100
Waveform | DSSS-OOK
Channel model | Channel B/Channel D
Chip duration | 0.5/1/2µs
Sampling rate at AMP device | 2MHz/8MHz
Receiver type | ED/IF receiver (Note)

## Slide 10: Synchronization performance(1)
  Case 1-1: 2MHz sampling rate at AMP STA & Chanel B@ED receiver.
  Note that the sync error is represented as the number of sampling points.
Doc.: IEEE 802.11-25/0321r0
Table 1: Sync performance when chip duration is 0.5 µs
Table 2: Sync performance when chip duration is 1 µs
Table 3: Sync performance when chip duration is 2 µs
SNR vs Sync error | -10 | -8 | -6 | -4 | -2 | 0 | 2 | 4 | 6 | 8 | 10
0 | 0.0526 | 0.0963 | 0.2086 | 0.4283 | 0.7276 | 0.9313 | 0.9879 | 0.996 | 0.9978 | 0.9986 | 0.999
1 | 0.1074 | 0.1157 | 0.111 | 0.0909 | 0.0499 | 0.0124 | 0.0025 | 0.001 | 0.0006 | 0.0003 | 0.0001
2 | 0.2423 | 0.2474 | 0.2383 | 0.197 | 0.1134 | 0.0343 | 4.90E-03 | 0.0012 | 0.0005 | 0.0005 | 0.0006
>=3 | 0.5977 | 0.5406 | 0.4421 | 0.2838 | 0.1091 | 0.022 | 4.70E-03 | 1.80E-03 | 1.10E-03 | 0.0006 | 0.0003
SNR vs Sync error | -10 | -8 | -6 | -4 | -2 | 0 | 2 | 4 | 6 | 8 | 10
0 | 0.0263 | 0.0597 | 0.168 | 0.4246 | 0.7812 | 0.9688 | 0.9955 | 0.9977 | 0.9985 | 0.999 | 0.9995
1 | 0.0148 | 0.0174 | 0.0196 | 0.0199 | 0.01 | 0.0017 | 0.0003 | 0.0001 | 0 | 0 | 0
2 | 0.0554 | 0.0647 | 0.0665 | 0.0525 | 0.0238 | 0.003 | 3.00E-04 | 0.0003 | 0.0002 | 0 | 0
>=3 | 0.9035 | 0.8582 | 0.7459 | 0.503 | 0.185 | 0.0265 | 3.90E-03 | 1.90E-03 | 1.30E-03 | 1.00E-03 | 5.00E-04
SNR vs Sync error | -10 | -8 | -6 | -4 | -2 | 0 | 2 | 4 | 6 | 8 | 10
0 | 0.0067 | 0.028 | 0.1123 | 0.4117 | 0.8378 | 0.9891 | 0.998 | 0.9991 | 0.9994 | 0.9994 | 0.9998
1 | 0.0046 | 0.0086 | 0.019 | 0.0339 | 0.0239 | 0.0029 | 0.0003 | 0 | 0 | 0 | 0
2 | 0.0011 | 0.0013 | 0.0025 | 0.0025 | 0.0009 | 0 | 0.00E+00 | 0 | 0 | 0 | 0
>=3 | 0.9876 | 0.9621 | 0.8662 | 0.5519 | 0.1374 | 0.008 | 1.70E-03 | 9.00E-04 | 6.00E-04 | 6.00E-04 | 2.00E-04

## Slide 11: Synchronization performance(2)
  Case 1-2: 2MHz sampling rate at AMP STA & Chanel B@ IF receiver.
  Note that the sync error is represented as the number of sampling points.
Doc.: IEEE 802.11-25/0321r0
Table 4: Sync performance when chip duration is 0.5 µs
Table 5: Sync performance when chip duration is 1 µs
Table 6: Sync performance when chip duration is 2 µs
SNR vs Sync error | -10 | -8 | -6 | -4 | -2 | 0 | 2 | 4 | 6 | 8 | 10
0 | 0.2923 | 0.4519 | 0.6621 | 0.8669 | 0.973 | 0.996 | 0.998 | 0.9982 | 0.9984 | 0.9985 | 0.9986
1 | 0.0522 | 0.0446 | 0.0307 | 0.0158 | 0.0053 | 0.0025 | 0.0018 | 0.0018 | 0.0016 | 0.0015 | 0.0014
2 | 0.0481 | 0.0403 | 0.0264 | 0.0124 | 0.0032 | 0.0007 | 2.00E-04 | 0 | 0 | 0 | 0
>=3 | 0.6074 | 0.4632 | 0.2808 | 0.1049 | 0.0185 | 0.0008 | ####### | 0.00E+00 | 0 | 0.00E+00 | 0
SNR vs Sync error | -10 | -8 | -6 | -4 | -2 | 0 | 2 | 4 | 6 | 8 | 10
0 | 0.3828 | 0.5733 | 0.7939 | 0.9433 | 0.9931 | 0.9983 | 0.9988 | 0.9987 | 0.9986 | 0.9986 | 0.9986
1 | 0.0628 | 0.0555 | 0.0363 | 0.0147 | 0.0033 | 0.0016 | 0.0012 | 0.0013 | 0.0014 | 0.0014 | 0.0014
2 | 0.0352 | 0.0261 | 0.0136 | 0.0042 | 0.0005 | 0 | 0.00E+00 | 0 | 0 | 0 | 0
>=3 | 0.5192 | 0.3451 | 0.1562 | 0.0378 | 0.0031 | 1.00E-04 | 0.00E+00 | 0.00E+00 | 0 | 0 | 0
SNR vs Sync error | -10 | -8 | -6 | -4 | -2 | 0 | 2 | 4 | 6 | 8 | 10
0 | 0.4862 | 0.7057 | 0.8797 | 0.9664 | 0.993 | 0.9982 | 0.9986 | 0.9989 | 0.9989 | 0.9988 | 0.9988
1 | 0.1336 | 0.1165 | 0.0737 | 0.0288 | 0.0067 | 0.0015 | 0.0014 | 0.0011 | 0.0011 | 0.0012 | 0.0012
2 | 0.0324 | 0.0207 | 0.0084 | 0.001 | 0 | 0 | 0.00E+00 | 0 | 0 | 0 | 0
>=3 | 0.3478 | 0.1571 | 0.0382 | 0.0038 | 0.0003 | 3.00E-04 | 0.00E+00 | 0.00E+00 | 0 | 0 | 0

## Slide 12: Synchronization performance(3)
  Case 1-3: 2MHz sampling rate at AMP STA & Chanel D@ ED receiver.
  Note that the sync error is represented as the number of sampling points.
Doc.: IEEE 802.11-25/0321r0
Table 7: Sync performance when chip duration is 0.5 µs
Table 8: Sync performance when chip duration is 1 µs
Table 9: Sync performance when chip duration is 2 µs
SNR vs Sync error | -10 | -8 | -6 | -4 | -2 | 0 | 2 | 4 | 6 | 8 | 10
0 | 0.0495 | 0.0922 | 0.1898 | 0.3863 | 0.6609 | 0.8765 | 0.9553 | 0.9758 | 0.9836 | 0.9878 | 0.99
1 | 0.1061 | 0.113 | 0.1127 | 0.1005 | 0.0619 | 0.024 | 0.0093 | 0.007 | 0.0065 | 0.0062 | 0.0063
2 | 0.2386 | 0.2439 | 0.2407 | 0.2053 | 0.1315 | 0.0526 | 1.72E-02 | 0.007 | 0.0032 | 0.0014 | 0.0007
>=3 | 0.6058 | 0.5509 | 0.4568 | 0.3079 | 0.1457 | 0.0469 | 1.82E-02 | 1.02E-02 | 6.70E-03 | 0.0046 | 0.003
SNR vs Sync error | -10 | -8 | -6 | -4 | -2 | 0 | 2 | 4 | 6 | 8 | 10
0 | 0.0266 | 0.0601 | 0.1563 | 0.3955 | 0.7386 | 0.9352 | 0.9793 | 0.9863 | 0.99 | 0.9912 | 0.9923
1 | 0.0168 | 0.0169 | 0.021 | 0.023 | 0.0149 | 0.0079 | 0.006 | 0.0058 | 0.0051 | 0.0055 | 0.0055
2 | 0.0566 | 0.0643 | 0.0684 | 0.0539 | 0.0223 | 0.0049 | 1.20E-03 | 0.0009 | 0.0009 | 0.0008 | 0.0005
>=3 | 0.9 | 0.8587 | 0.7543 | 0.5276 | 0.2242 | 0.052 | 1.35E-02 | 7.00E-03 | 4.00E-03 | 2.50E-03 | 1.70E-03
SNR vs Sync error | -10 | -8 | -6 | -4 | -2 | 0 | 2 | 4 | 6 | 8 | 10
0 | 0.0062 | 0.0247 | 0.1081 | 0.3931 | 0.8076 | 0.9698 | 0.9875 | 0.9904 | 0.9922 | 0.993 | 0.9937
1 | 0.0037 | 0.0071 | 0.017 | 0.0338 | 0.0285 | 0.0116 | 0.0061 | 0.0056 | 0.0053 | 0.0056 | 0.0052
2 | 0.002 | 0.0021 | 0.0026 | 0.0027 | 0.0013 | 0 | 1.00E-04 | 0.0002 | 0 | 0 | 0
>=3 | 0.9881 | 0.9661 | 0.8723 | 0.5704 | 0.1626 | 0.0186 | 6.30E-03 | 3.80E-03 | 2.50E-03 | 1.40E-03 | 1.10E-03

## Slide 13: Synchronization performance(4)
  Case 1-4: 2MHz sampling rate at AMP STA & Chanel D@ IF receiver.
  Note that the sync error is represented as the number of sampling points.
Doc.: IEEE 802.11-25/0321r0
Table 10: Sync performance when chip duration is 0.5 µs
Table 11: Sync performance when chip duration is 1 µs
Table 12: Sync performance when chip duration is 2 µs
SNR vs Sync error | -10 | -8 | -6 | -4 | -2 | 0 | 2 | 4 | 6 | 8 | 10
0 | 0.2738 | 0.4207 | 0.6201 | 0.8154 | 0.9341 | 0.9707 | 0.9772 | 0.9787 | 0.9798 | 0.98 | 0.9805
1 | 0.0644 | 0.0642 | 0.0608 | 0.0481 | 0.0328 | 0.0265 | 0.0226 | 0.0212 | 0.0202 | 0.02 | 0.0195
2 | 0.0493 | 0.0401 | 0.028 | 0.014 | 0.0044 | 0.0006 | 1.00E-04 | 0.0001 | 0 | 0 | 0
>=3 | 0.6125 | 0.475 | 0.2911 | 0.1225 | 0.0287 | 0.0022 | 1.00E-04 | ####### | 0 | 0.00E+00 | 0
SNR vs Sync error | -10 | -8 | -6 | -4 | -2 | 0 | 2 | 4 | 6 | 8 | 10
0 | 0.3562 | 0.5444 | 0.7562 | 0.908 | 0.9636 | 0.9761 | 0.9782 | 0.9799 | 0.9804 | 0.9811 | 0.9811
1 | 0.0827 | 0.083 | 0.0716 | 0.0492 | 0.0328 | 0.0238 | 0.0218 | 0.0201 | 0.0196 | 0.0189 | 0.0189
2 | 0.0379 | 0.0271 | 0.0139 | 0.0051 | 0.0008 | 0 | 0.00E+00 | 0 | 0 | 0 | 0
>=3 | 0.5232 | 0.3455 | 0.1583 | 0.0377 | 0.0028 | 1.00E-04 | 0.00E+00 | 0.00E+00 | 0 | 0 | 0
SNR vs Sync error | -10 | -8 | -6 | -4 | -2 | 0 | 2 | 4 | 6 | 8 | 10
0 | 0.4576 | 0.67 | 0.8458 | 0.9344 | 0.9674 | 0.977 | 0.9814 | 0.9835 | 0.9847 | 0.9847 | 0.9849
1 | 0.1468 | 0.1432 | 0.1046 | 0.0599 | 0.0323 | 0.0229 | 0.0185 | 0.0164 | 0.0152 | 0.0153 | 0.0151
2 | 0.0338 | 0.0218 | 0.0078 | 0.0015 | 0.0001 | 0 | 0.00E+00 | 0 | 0 | 0 | 0
>=3 | 0.3618 | 0.165 | 0.0418 | 0.0042 | 0.0002 | 1.00E-04 | 1.00E-04 | 1.00E-04 | 1.00E-04 | 0 | 0

## Slide 14: Synchronization performance(5)
  Case 2-1: 8MHz sampling rate at AMP STA & Chanel B@ED receiver.
  Note that the sync error is represented as the number of sampling points.
Doc.: IEEE 802.11-25/0321r0
Table 13: Sync performance when chip duration is 0.5 µs
Table 14: Sync performance when chip duration is 1 µs
Table 15: Sync performance when chip duration is 2 µs
SNR vs Sync error | -10 | -8 | -6 | -4 | -2 | 0 | 2 | 4 | 6 | 8 | 10
0 | 0.0067 | 0.0261 | 0.1055 | 0.3653 | 0.7883 | 0.9566 | 0.9807 | 0.9856 | 0.9883 | 0.9884 | 0.9883
1 | 0.0033 | 0.008 | 0.0199 | 0.0371 | 0.0366 | 0.0205 | 0.0116 | 0.0111 | 0.0094 | 0.0099 | 0.0108
2 | 0.0025 | 0.0023 | 0.0028 | 0.0033 | 0.0013 | 0 | 2.00E-04 | 0.0001 | 0 | 0 | 0
>=3 | 0.9875 | 0.9636 | 0.8718 | 0.5943 | 0.1738 | 0.0229 | 7.50E-03 | 3.20E-03 | 0.0023 | 0.0017 | 0.0009
SNR vs Sync error | -10 | -8 | -6 | -4 | -2 | 0 | 2 | 4 | 6 | 8 | 10
0 | 0.0007 | 0.0067 | 0.0652 | 0.398 | 0.8684 | 0.967 | 0.9842 | 0.9871 | 0.9881 | 0.9877 | 0.9879
1 | 0.0001 | 0.0017 | 0.0146 | 0.0533 | 0.0483 | 0.0247 | 0.0128 | 0.0113 | 0.0108 | 0.0116 | 0.0115
2 | 0.0003 | 0.0008 | 0.0032 | 0.0059 | 0.0041 | 0.0004 | 2.00E-04 | 0.0001 | 0 | 0 | 0
>=3 | 0.9989 | 0.9908 | 0.917 | 0.5428 | 0.0792 | 0.0079 | 2.80E-03 | 1.50E-03 | 1.10E-03 | 7.00E-04 | 6.00E-04
SNR vs Sync error | -10 | -8 | -6 | -4 | -2 | 0 | 2 | 4 | 6 | 8 | 10
0 | 0 | 0.0005 | 0.0299 | 0.4406 | 0.9109 | 0.972 | 0.9838 | 0.9877 | 0.9885 | 0.9888 | 0.9883
1 | 0 | 0.0004 | 0.0085 | 0.0693 | 0.0626 | 0.0246 | 0.0148 | 0.0112 | 0.011 | 0.0106 | 0.0113
2 | 0 | 0 | 0.0013 | 0.01 | 0.0053 | 0.0005 | 0.00E+00 | 0 | 0 | 0 | 0
>=3 | 1 | 0.9991 | 0.9603 | 0.4801 | 0.0212 | 0.0029 | 1.40E-03 | 1.10E-03 | 5.00E-04 | 6.00E-04 | 4.00E-04

## Slide 15: Synchronization performance(6)
  Case 2-2: 8MHz sampling rate at AMP STA & Chanel B@ IF receiver.
  Note that the sync error is represented as the number of sampling points.
Doc.: IEEE 802.11-25/0321r0
Table 16: Sync performance when chip duration is 0.5 µs
Table 17: Sync performance when chip duration is 1 µs
Table 18: Sync performance when chip duration is 2 µs
SNR vs Sync error | -10 | -8 | -6 | -4 | -2 | 0 | 2 | 4 | 6 | 8 | 10
0 | 0.4584 | 0.6667 | 0.831 | 0.9174 | 0.9538 | 0.9692 | 0.9754 | 0.9779 | 0.9781 | 0.9798 | 0.9791
1 | 0.1612 | 0.1491 | 0.1192 | 0.0756 | 0.0459 | 0.0305 | 0.0244 | 0.0221 | 0.0219 | 0.0202 | 0.0209
2 | 0.0335 | 0.0191 | 0.0074 | 0.0016 | 0 | 0 | 0.00E+00 | 0 | 0 | 0 | 0
>=3 | 0.3469 | 0.1651 | 0.0424 | 0.0054 | 3.00E-04 | 3.00E-04 | 2.00E-04 | 0.00E+00 | 0.00E+00 | 0.00E+00 | 0.00E+00
SNR vs Sync error | -10 | -8 | -6 | -4 | -2 | 0 | 2 | 4 | 6 | 8 | 10
0 | 0.5577 | 0.7313 | 0.8448 | 0.9111 | 0.9504 | 0.9696 | 0.9732 | 0.9778 | 0.9795 | 0.981 | 0.9808
1 | 0.2181 | 0.1963 | 0.1382 | 0.0861 | 0.0489 | 0.0304 | 0.0267 | 0.0222 | 0.0204 | 0.019 | 0.0192
2 | 0.0616 | 0.0355 | 0.0117 | 0.0026 | 0.0003 | 0 | 0.00E+00 | 0 | 0 | 0 | 0
>=3 | 0.1626 | 0.0369 | 0.0053 | 2.00E-04 | 4.00E-04 | 0.00E+00 | 1.00E-04 | 0.00E+00 | 1.00E-04 | 0.00E+00 | 0.00E+00
SNR vs Sync error | -10 | -8 | -6 | -4 | -2 | 0 | 2 | 4 | 6 | 8 | 10
0 | 0.6042 | 0.7362 | 0.8375 | 0.906 | 0.95 | 0.9653 | 0.9738 | 0.9784 | 0.9806 | 0.9812 | 0.9818
1 | 0.2493 | 0.2029 | 0.1413 | 0.0903 | 0.0495 | 0.0347 | 0.0262 | 0.0216 | 0.0194 | 0.0188 | 0.0182
2 | 0.0776 | 0.0399 | 0.0158 | 0.0032 | 0.0005 | 0 | 0.00E+00 | 0 | 0 | 0 | 0
>=3 | 0.0689 | 0.021 | 0.0054 | 5.00E-04 | 5.59E-17 | 0.00E+00 | 0.00E+00 | 0.00E+00 | 0.00E+00 | 0.00E+00 | 0.00E+00

## Slide 16: Synchronization performance(7)
  Case 2-3: 8MHz sampling rate at AMP STA & Chanel D@ ED receiver.
  Note that the sync error is represented as the number of sampling points.
Doc.: IEEE 802.11-25/0321r0
Table 19: Sync performance when chip duration is 0.5 µs
Table 20: Sync performance when chip duration is 1 µs
Table 21: Sync performance when chip duration is 2 µs
SNR vs Sync error | -10 | -8 | -6 | -4 | -2 | 0 | 2 | 4 | 6 | 8 | 10
0 | 0.0038 | 0.0193 | 0.0731 | 0.2427 | 0.554 | 0.7155 | 0.7488 | 0.7659 | 0.7725 | 0.7807 | 0.7839
1 | 0.0045 | 0.0102 | 0.0349 | 0.0907 | 0.1758 | 0.2077 | 0.2122 | 0.2059 | 0.205 | 0.1977 | 0.197
2 | 0.0047 | 0.0038 | 0.0053 | 0.0119 | 0.0107 | 0.0099 | 1.06E-02 | 0.0119 | 0.0102 | 0.0131 | 0.0121
>=3 | 0.987 | 0.9667 | 0.8867 | 0.6547 | 0.2595 | 0.0669 | 2.84E-02 | 1.63E-02 | 0.0123 | 0.0085 | 0.007
SNR vs Sync error | -10 | -8 | -6 | -4 | -2 | 0 | 2 | 4 | 6 | 8 | 10
0 | 0.0004 | 0.0044 | 0.0469 | 0.2782 | 0.6338 | 0.7353 | 0.7577 | 0.7677 | 0.7728 | 0.7778 | 0.7835
1 | 0.0004 | 0.0028 | 0.0203 | 0.1093 | 0.2182 | 0.222 | 0.2162 | 0.2114 | 0.2079 | 0.2051 | 0.1981
2 | 0.0002 | 0.0011 | 0.0066 | 0.0163 | 0.0196 | 0.0163 | 1.38E-02 | 0.013 | 0.0142 | 0.0124 | 0.0147
>=3 | 0.999 | 0.9917 | 0.9262 | 0.5962 | 0.1284 | 0.0264 | 1.23E-02 | 7.90E-03 | 5.10E-03 | 4.70E-03 | 3.70E-03
SNR vs Sync error | -10 | -8 | -6 | -4 | -2 | 0 | 2 | 4 | 6 | 8 | 10
0 | 0 | 0.0003 | 0.0231 | 0.3119 | 0.6814 | 0.7407 | 0.7564 | 0.7719 | 0.778 | 0.7803 | 0.7804
1 | 0 | 0.0004 | 0.0114 | 0.1371 | 0.2473 | 0.2308 | 0.2219 | 0.2098 | 0.2046 | 0.2023 | 0.2017
2 | 0 | 0 | 0.0016 | 0.0242 | 0.0267 | 0.0178 | 1.53E-02 | 0.0141 | 0.0139 | 0.0149 | 0.0156
>=3 | 1 | 0.9993 | 0.9639 | 0.5268 | 0.0446 | 0.0107 | 6.40E-03 | 4.20E-03 | 3.50E-03 | 2.50E-03 | 2.30E-03

## Slide 17: Synchronization performance(8)
  Case 2-4: 8MHz sampling rate at AMP STA & Chanel D@ IF receiver.
  Note that the sync error is represented as the number of sampling points.
Doc.: IEEE 802.11-25/0321r0
Table 22: Sync performance when chip duration is 0.5 µs
Table 23: Sync performance when chip duration is 1 µs
Table 24: Sync performance when chip duration is 2 µs
SNR vs Sync error | -10 | -8 | -6 | -4 | -2 | 0 | 2 | 4 | 6 | 8 | 10
0 | 0.3628 | 0.5196 | 0.651 | 0.724 | 0.7519 | 0.7771 | 0.7884 | 0.7989 | 0.8075 | 0.806 | 0.8113
1 | 0.2183 | 0.244 | 0.2615 | 0.2449 | 0.2295 | 0.208 | 0.2008 | 0.1891 | 0.1817 | 0.1843 | 0.1787
2 | 0.0519 | 0.0401 | 0.0336 | 0.0191 | 0.015 | 0.0122 | 9.30E-03 | 0.0106 | 0.0095 | 0.0085 | 0.009
>=3 | 0.367 | 0.1963 | 0.0539 | 0.012 | 3.60E-03 | 2.70E-03 | 1.50E-03 | 1.40E-03 | 1.30E-03 | 1.20E-03 | 1.00E-03
SNR vs Sync error | -10 | -8 | -6 | -4 | -2 | 0 | 2 | 4 | 6 | 8 | 10
0 | 0.4602 | 0.5896 | 0.6767 | 0.7232 | 0.7516 | 0.7731 | 0.7843 | 0.7948 | 0.8007 | 0.8044 | 0.8059
1 | 0.2827 | 0.2966 | 0.2765 | 0.2498 | 0.2315 | 0.212 | 0.2037 | 0.1944 | 0.1883 | 0.1846 | 0.1842
2 | 0.078 | 0.0601 | 0.0362 | 0.0227 | 0.0143 | 0.0127 | 1.04E-02 | 0.0098 | 0.0098 | 0.0098 | 0.0089
>=3 | 0.1791 | 0.0537 | 0.0106 | 4.30E-03 | 2.60E-03 | 2.20E-03 | 1.60E-03 | 1.00E-03 | 1.20E-03 | 1.20E-03 | 1.00E-03
SNR vs Sync error | -10 | -8 | -6 | -4 | -2 | 0 | 2 | 4 | 6 | 8 | 10
0 | 0.4972 | 0.5973 | 0.6554 | 0.7218 | 0.7498 | 0.7731 | 0.7859 | 0.7959 | 0.8013 | 0.8065 | 0.8082
1 | 0.3214 | 0.3007 | 0.2929 | 0.2505 | 0.2345 | 0.2143 | 0.2037 | 0.1922 | 0.1885 | 0.1837 | 0.182
2 | 0.0929 | 0.0666 | 0.0389 | 0.0237 | 0.014 | 0.011 | 9.70E-03 | 0.0111 | 0.0095 | 0.0089 | 0.0089
>=3 | 0.0885 | 0.0354 | 0.0128 | 4.00E-03 | 1.70E-03 | 1.60E-03 | 7.00E-04 | 8.00E-04 | 7.00E-04 | 9.00E-04 | 9.00E-04

## Slide 18: Summary of Sync performance
Doc.: IEEE 802.11-25/0321r0
 | Sync error =0 @90% Probability |  |  |  | Sync error =0 and 1 @90% Probability |  |  | 
Sampling rate | 2MHz |  |  |  | 8MHz |  |  | 
Channel Model | Channel B |  | Channel D |  | Channel B |  | Channel D | 
Receiver Type | ED | IF | ED | IF | ED | IF | ED | IF
Chip duration =0.5µs | ~-0.3 | -3.3 | 0.6 | -2.5 | -0.95 | -6.7 | -0.3 | -6.1
Chip duration =1µs | ~-0.7 | -4.5 | -0.3 | -4 | -2 | -8.4 | -1 | -7.5
Chip duration =2µs | ~-1.2 | -5.5 | -0.9 | -4.7 | -2.3 | -8.5 | -2.1 | -7.8

## Slide 19: Impact on decoding performance(1)
  When there is synchronization error, the impact on data decoding performance is evaluated with the following assumptions:
Doc.: IEEE 802.11-25/0321r0
Parameters | Values
Date Rate | 250kpbs/1MHz
Waveform | DSSS-OOK
Channel model | Channel B/D
Chip duration | 2µs/0.5µs
Sampling rate at AMP device | 2MHz/8MHz
Coding | Manchester
Receiver type | ED receiver
synchronization error | 1 Sampling point

## Slide 20: Impact on decoding performance(2)
  Simulation results for data rate of 250kbps in channel B
Doc.: IEEE 802.11-25/0321r0
Figure 1: DL PPDU decoding performance @sampling rate of 2MHz
Figure 2: DL PPDU decoding performance @sampling rate of 8MHz

## Slide 21: Impact on decoding performance(3)
  Simulation results for data rate of 1Mbps and sampling rate of 8MHz
Doc.: IEEE 802.11-25/0321r0
Figure 3: DL PPDU decoding performance （Channel B）

## Slide 22: Impact on decoding performance(2)
  Simulation results for data rate of 250kbps in channel D
Doc.: IEEE 802.11-25/0321r0
Figure 1: DL PPDU decoding performance @sampling rate of 2MHz
Figure 2: DL PPDU decoding performance @sampling rate of 8MHz

## Slide 23: Impact on decoding performance(3)
  Simulation results for data rate of 1Mbps and sampling rate of 8MHz
Doc.: IEEE 802.11-25/0321r0
Figure 3: DL PPDU decoding performance （Channel D）

## Slide 24: Observation
Under both channel B and channel D, for sampling rate = 2MHz at AMP STA’s receiver, the required SNR is ~1dB for DL data rate of 250kbps.
Under both channel B and channel D, for sampling rate = 8MHz at AMP STA’s receiver, the required SNR is ~-2dB for DL data rate of 250kbps.
  For AMP sync of length 16, the sync performance for chip duration of 2µs is acceptable.
Doc.: IEEE 802.11-25/0321r0

## Slide 25: Summary
In this submission, sync sequence for AMP is discussed. Based on the discussion, the following is proposed.
  Basic sync length is 16, one proposed sequence is
    S1= '1100100101011100’
  Chip duration of sync field is 2 µs .
Doc.: IEEE 802.11-25/0321r0

## Slide 26
Straw Poll #1
Weijie Xu (OPPO)
Slide 26
Doc.: IEEE 802.11-25/0321r0
March 2025
Do you agree with the following text:
  Basic AMP sync length is 16, one proposed sequence is
    S1= '1100100101011100’
  Chip duration of sync field is 2 µs .
Yes
No
Abstain

## Slide 27: Reference
IEEE 802.11-25/0034r2 Sync field for AMP PPDU
Doc.: IEEE 802.11-25/0321r0
March 2025