## Slide 1: Information exchange in SMD
Date: 2025-3-10
Authors:

## Slide 2: Introduction
TGbn agreed to define an SMD that covers multiple AP MLDs, where a non-AP MLD can use the UHR seamless roaming procedure to roam between the AP MLDs of the SMD.
TGbn also agreed to include a roaming preparation procedure for setting up link(s) with a target AP MLD.
Currently, multiple candidate target AP MLDs selection is TBD.
In this contribution, we show that some information exchange between AP MLDs can help in selecting an appropriate target AP MLD

## Slide 3: Roaming preparation procedure
A non-AP MLD can initiate a roaming preparation procedure with a target AP MLD by sending a TBD request frame to its current AP MLD.
Before executing the seamless roaming procedure, the non-AP MLD needs to know target AP MLD or candidate target AP MLDs to roam.
For target AP selection, the current AP can provide information about candidate APs of an SMD that are recommended for the non-AP MLD[1].
Current AP
Target AP(s)
STA
TBD preparation request
Setup link(s)
transferable context transfer
(context renegotiation)
TBD preparation response
Roaming
Preparation

## Slide 4: Information exchange within SMD
For making recommendations, it is preferable for the current AP to consider status/parameter/condition of other APs in its SMD as much as possible.
  For example,
    QoS management such as SCS [2]
    number of links, supported BW[3]
    data forwarding capability
Without this information, roaming may fail, or the non-AP MLD may experience low-quality communication.
  Without SCS information, target AP may reject the setup of SCS.
  Without data forwarding capability, the current AP needs to send all buffered DL to the STA, and the initiation of data exchange with the target AP may be delayed(especially for single-link STAs).
Therefore, it is preferred to have information exchange between AP MLDs in SMD to select appropriate target AP MLD.

## Slide 5: Target AP selection procedure
BTM framework can be reused for target AP selection procedure for seamless roaming.
STA may send BTM Query to its current AP to select appropriate target AP.
  STA may include candidate target AP list in BTM Query.
Current AP collects information of other candidate APs in SMD.
  This information collection can be done before BTM Query.
Current AP decides preference of target AP to roam by considering the gathered information and notifies it to STA by BTM Request.
Based on the preference notified by current AP, STA may select target AP to roam.
Current AP
candidate APs
STA
May send BTM query
Information exchange
Target AP preference decision
BTM Request
TBD preparation request
Setup link(s)
transferable context transfer
(context renegotiation)
TBD preparation response
Roaming
Preparation

## Slide 6: Conclusion
As a part of seamless roaming procedure, non-AP MLD choose a target AP MLD to roam before roaming preparation/execution procedure.
We see that some information exchange between AP MLDs can help to select appropriate target AP MLD in some cases.

## Slide 7: SP1
Do you agree to include the following text to the 11bn SFD?
  Add extra bits within the Neighbor Report element to indicate operational parameters for SCS/MSCS.
    How many bits to be added is TBD.
    Which operational parameters to be indicated is TBD.

## Slide 8: SP2
Do you agree to include the following text to the 11bn SFD?
  Add one bit within the Neighbor Report element to indicate whether the data forwarding from the reporting AP to the reported AP is capable?

## Slide 9: SP3
Do you agree to include the following text to the 11bn SFD?
  If the field in the Neighbor Report element which indicates the capability of data forwarding from the reporting AP to the reported AP is set to 1, the Neighbor Report element can include extra bits to indicate information about the data forwarding?
    How many bits to be included is TBD.
    What information to be indicated is TBD.

## Slide 10: References
[1] 24/1884r0, “Signaling considerations for seamless roaming,” Abhishek Patil (Qualcomm)
[2] 24/1425r0, “Considerations for Context Transfer in 11bn,” Peshal Nayak (Samsung)
[3] 24/1882r1, “Link Setup for Seamless Roaming,” Chitto Ghosh (Apple)