## Slide 1: Simple UL Access for AMP Clients
Authors:
Date: 2025-03-03
Name | Affiliations | Address | Phone | email
Sanket Kalamkar | Qualcomm Technologies Inc. |  |  | sankal@qti.qualcomm.com
George Cherian |  |  |  | 
Alfred Asterjadhi |  |  |  | 

## Slide 2: Proposal
This contribution proposes a simple channel access scheme that:
  Considers the limitations of AMP clients (Active Tx, Backscatter clients)
    Limited energy availability
    Minimal to no persistent memory
    High clock drift
  Supports both unicast and multicast/broadcast cases
Simple protocol for UL channel access
  Assumes no timing synchronization

## Slide 3: Recap: E2E View of AMP Operation
Offline Onboarding
  E.g., password setting
  Optional: May be outside IEEE scope
Initial Info Exchange (Discovery)
  AP and AMP clients exchange basic information, e.g., MAC addresses
    May happen post-onboarding or when the AP needs to verify if the client remains within its range
  AP uses this mode to determine the presence of active AMP clients
AMP Operation Mode Information Exchange
  AP requests the client’s operation capabilities
  The client provides capability and schedule-related information to the AP
    E.g., schedule information, power budget, energy harvesting capabilities
  AP uses this mode to determine the Tx/Rx parameters to reach AMP clients
AMP Poll (Trigger)/UL Response
  AP requests client for uplink (UL) transmissions; client sends UL transmissions
  Happens Per schedule/On-demand
Initial Info Exchange
AMP Trigger/ UL Response
AMP Operation Mode Information Exchange
Offline Onboarding
Once
Once in a while
Once in a while
Per Schedule/ On Demand

## Slide 4: Steps for UL Access
When AP wants to solicit an UL AMP PPDU from a client:
From AP side:
  Sends energizing/excitation signal towards the client
  Sends Trigger frame to solicit UL access that is addressed to the client
From Client side:
  If the client accumulates sufficient energy to wake up and perform an UL transmission, the client wakes up
  The client looks for the Trigger frame addressed to it
  If the Trigger frame is addressed to the client:
    The client performs UL access
  If the Trigger frame is NOT addressed to the client:
    The client goes back to sleep

## Slide 5: Remarks
The proposed UL access assumes no timing synchronization between the AP and the client
  E.g., Need not rely on duty-cycled operation
    The client can specify how often it expects the AP to solicit UL PPDUs
      E.g., during AMP Operation Mode Information Exchange
    The AP charges the client accordingly to ensure sufficient energy for UL access
      The AP sends an energizing/excitation signal only when it intends to solicit UL access from the client
  When the client performs UL access, it uses the Trigger frame’s receive time as a reference for that TXOP

## Slide 6: Summary
Proposed a simple protocol for AMP clients for UL access
  Does not need to timing synchronization between the AP and the clients
  Honors AMP clients’ limitations
    Limited energy availability
    Minimal to no persistent memory
    High clock drift

## Slide 7: SP
Do you agree that an 802.11bp client may use the receive time of the AMP Trigger frame, which solicits UL AMP PPDUs from the client, to determine the timing for transmitting UL AMP PPDUs?