## Slide 1: Considerations for AP Dynamic Power Save
Date: 2025-03-03
Authors:

## Slide 2: Introduction
The key objective of AP Power Save is to reduce power consumption for APs without impacting the latency or throughput requirements of non-AP STAs
There are limited number of options available for AP power save
  Reduction of bandwidth
  Reduction of number of Spatial Streams
  Disable links (if MLO available)
    The current standard allows the AP to change these parameters
AP power management has two modes: Active mode and power save mode
  In power save mode, the AP is either in doze state or awake state
    For example, in doze state AP disables its radio interface, and it does not transmit, receive, or listen
    In awake state the AP operates with its full capabilities, and it can transmit, or receive
Dynamic power save i.e. listen state using minimum capabilities has been introduced for non-AP STAs and mobile APs[1]
  This is envisioned to reduce power in both listen and receive modes
  However, a similar mechanism tailored to the specific operations of AP is not a part of SFD yet
Dynamic AP power save allows APs to save power dynamically by switching capabilities
  Impactful power saving potential for UHR APs
  Legacy STAs may experience significant impact
In this contribution, we provide considerations on Dynamic AP Power Save
Notes: AP Power save is a feature that has not gained enough momentum in the TG despite several related contributions

## Slide 3: Related Work
Several contributions discuss Dynamic Power Save (DPS) for an AP:
  [1] discusses candidate power save protocols describing the requirements, target power saving that can be achieved as well as issues that need careful considerations
  [2] provide thoughts on details of DPS operation for an AP. Presents solutions to prevent loss of medium synchronization during transition in different modes
  [3] proposes consideration of different power save modes based on the scenario and the STAs present
  [4] describes the information element options available to specify an AP’s schedule, power state, capability, and management info. to the non-AP STAs for power save mode

## Slide 4: AP Power Save Summary
In DPS, an AP can transmit beacons and management frames, listen to the channel; and communicate with legacy STAs, as well as with DPS-capable STAs which can be served without increasing the AP’s capabilities
  AP is capable of exchanging non-HT dup format PPDUs
AP PS Mechanism | Signaling | Energy saving | Schedule Duration | Compatibility
Scheduled | Use TWT signaling | High | Long | Does not work with Legacy devices
*Dynamic | ICF with intermediate FCS and padding, ICR | Medium | Short | Limited due to the backward compatibility issues related with legacy
Cross Link | Cross link wake-up frame (Reuse AP Assistance Request control info. field) | High | Short | High due to the presence of at least one active link
* Not a part of SFD yet
Notes: Ynamic Ynamic

## Slide 5: Motivation
In general, the AP is always expected to be ON, always operating in its full capability state
  As most APs are wall-powered, the need to save power at APs is often overlooked
  However, the introduction of MLO makes power save a crucial issue for APs
There are scenarios e.g.
  In enterprise / managed Wi-Fi setups where the service provider is expected to be, via contractual obligations, responsible for cost of utilities (e.g., power).
  In outdoor deployment of Wi-Fi APs where APs may not use constant-power source e.g., when mounted on DOCSIS- strands
  Scheduled PS can work well in network traffic predictable cases, such as office buildings where low/no traffic is expected at night-time and weekends. However, if the managed network covers an area such as downtown where the AP is on a strand applying a scheduled power save may not work due to the dynamic nature of its usage
In such cases, we need AP power saving methods that can dynamically change capabilities to save power and ensure uninterrupted services

## Slide 6: Motivation(cont.)
TWT based scheduled AP PS allows AP to be in doze state outside the TWT SPs. However, there are several considerations such as
  The AP cannot go in doze state in presence of legacy devices
  The doze state must consider QoS requirements of the associated STAs
  After negotiating the schedule, the devices don’t always wake up accurately
  In presence of multiple STAs, an AP does not get many opportunities to be in doze state as it is responsible for sending out the beacon and management frames
Dynamic PS with AP operating in minimum capability state allows the AP to serve legacy devices while maintaining minimum Tx/Rx operation and the possibility to transition to higher capability state when triggered by a non-AP STA
  Frames that need to be exchanged for transition to higher capability state need to be designed such that they do not interfere with the operation of legacy devices
Dynamic power save could provide significant improvement for power saving in scenarios where, the network traffic is unpredictable and traditional power saving schemes such as scheduled PS are not applicable

## Slide 7: Summary
Brief discussion on the available AP power save techniques
We describe scenarios in which AP power save is critical either due to the AP not being wall-powered or the expenses incurred by the operator
Scheduled power save can help reduce power consumption during down time, however, there are scenarios where it may not be applicable due to dynamic utilization of the network
  Therefore, a technique such as dynamic power save in which the AP is essentially in listen sate with some limited Tx/Rx capabilities can provide some significant power reduction
Highlights the need for dynamic power save in APs

## Slide 8: References
[1] 24/2016, PDT MAC Power Save
[2] 23/0010, Considerations for enabling AP Power Save
[2] 24/0451, AP state transitions in DPS mode
[3] 24/0833, Dynamic Power Saving for AP
[4] 24/0097, AP Power Management– Follow-up