## Slide 1: PPDU Format for IMMW
Date: 2025-03-12
Authors:
Name | Affiliation | Address | Phone | Email
Eunsung Park | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | esung.park@lge.com
Insun Jang |  |  |  | insun.jang@lge.com
Insik Jung |  |  |  | insik0618.jung@lge.com
Dongju Cha |  |  |  | dongju.cha@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
HanGyu Cho |  |  |  | hg.cho@lge.com
Sanggook Kim |  | 10680 Treena St 550, San Diego CA 92131 |  | sanggook.kim@lge.com

## Slide 2: Introduction
Many contributions discussed high level design ways and technical scope for IMMW during the SG phase [1-6]
  Although some details are slightly different, all of them have almost identical views
    Leverage the sub-7 GHz PHY design and 11be MLO architecture
In this contribution, we discuss PPDU formats for IMMW
  We consider two options for a basic PPDU format
  We also introduce two additional PPDU formats which can be considered in IMMW

## Slide 3: Basic PPDU Format (1/4)
We propose the following two PPDU formats
  Option 1: 11a like PPDU
  Option 2: 11ac/ax like PPDU
STF and STF1 need to have a structure which can perform packet detection, CFO measure as well as AGC
  E.g, 10 times repetition of a 0.8/N us signal (N times upclocking applied)
LTF and LTF1 need to have a structure which can perform CFO measure as well as channel estimation
  E.g., GI2 + LTS + LTS
STF | LTF | SIG | Data
STF1 | LTF1 | SIG | STF2 | LTF2 | Data

## Slide 4: Basic PPDU Format (2/4)
Option 1: 11a like PPDU
  11bq is the first version leveraging the sub-7 GHz PHY design in a mmWave band, and thus, we don’t have to consider a legacy preamble part
    This option has an advantage in terms of the overhead
    While we can consider forward compatibility and the SIG part can include version ID information
  If IMMW supports multi-bandwidth and multi-stream, these information should be exchanged in sub-7 GHz prior to a mmWave PPDU transmission with this format
    In order to decode the Data part, bandwidth and the number of streams / LTF symbols should be known before receiving the PPDU for the AGC and channel estimation performed in the STF and LTF, respectively
    Estimated channel state can be used to decode both SIG and Data parts
  Each field design depends on a tone plan and we can consider two approaches
    For implementation simplicity, the tone plan can be defined for the smallest bandwidth and it can be duplicated in a wide bandwidth, i.e., all of the fields have a duplicated structure
    For throughput enhancement, the tone plan can be independently defined in each bandwidth and STF, LTF and SIG design can also follow the tone plan, i.e., the structure of these fields is not duplicated in each channel

## Slide 5: Basic PPDU Format (3/4)
Option 2: 11ac/ax like PPDU
  We can simply use an 11ac/ax PPDU with a slight modification for consistent implementation between sub-7 GHz and mmWave bands
  If MIMO is supported in IMMW, this structure may be more efficient for MIMO AGC and MIMO channel estimation
    For future extension, this structure, especially 11ax like PPDU which can also support OFDMA, may have benefits
  Bandwidth and the number of streams / LTF symbols may not have to be exchanged in sub-7 GHz prior to a mmWave PPDU transmission with this format
    We can just include these information in SIG of the mmWave PPDU to decode the Data part and a flexible use of bandwidth and spatial stream may be possible
  Similar to option 1, we can consider two approaches for a tone plan design
    For implementation simplicity, the tone plan can be defined for the smallest bandwidth and it can be duplicated in a wide bandwidth, i.e., all of the fields have a duplicated structure
    For throughput enhancement, the tone plan can be independently defined in each bandwidth and STF2 and LTF2 can follow them while STF1, LTF1 and SIG can still have a duplicated structure similar to the pre-VHT/HEW modulated part in a sub-7 GHz PPDU. In this case, estimated channel state obtained from LTF1 and LTF2 can be used to decode SIG and Data part, respectively.

## Slide 6: Basic PPDU Format (4/4)
If most of the mmWave PPDU transmissions use one spatial stream in the smallest bandwidth to reduce implementation complexity and beamforming training overhead, option 1 may be reasonable
  When using option 2 in this case, STF2 and LTF2 can be just overhead
However, considering supporting a variety of use cases including high throughput and low latency in IMMW, it would be good to define multiple bandwidths and/or support MIMO
  In this case, option 2 may be more reasonable
  We can still use option 1 by indicating the information about the bandwidth and the number of spatial streams in sub-7 GHz prior to a mmWave PPDU transmission
We are open for both PPDU formats for now and need further discussion
Meanwhile, when it comes to the tone plan design, we propose to duplicate a tone plan of the smallest bandwidth
  The allowed bandwidths may be already enough for high data rate and we don’t think we need to further optimize the tone plan according to the bandwidth
  This approach allows separate PHYs to process each frequency subblock

## Slide 7: Consideration on Additional PPDU formats
In 11bn, there are some additional PPDUs for specific functions
  EHT sounding NDP for sounding and beamforming
  Enhanced long range PPDU to overcome coverage difference between DL and UL
In IMMW, we can also consider several additional PPDUs
  NDP like PPDU
    It can be formed based on the basic PPDU format by excluding the Data part and used for (fast / simplified) beam training
    Required information for beam training can be exchanged in the sub-7 GHz band and/or included in the SIG field of the PPDU
  Enhanced long range PPDU
    It can be used to overcome coverage limit caused by a beamforming gain difference between STAs, roughly trained beamforming or an omnidirectional transmission/reception
    As a result, it can help to prevent a frequent transition to a sub-7 GHz band caused by beamforming issues
    To this end, several approaches such as power boosting, lower MCS and signal repetition can be applied to the basic PPDU format

## Slide 8: Summary
We have discussed two basic PPDU formats
  There are pros and cons in each option and we are open for now
We have also proposed how to design a tone plan for a wide bandwidth
  We prefer to duplicate a tone plan of the smallest bandwidth
Finally, we have introduced two additional PPDU formats
  The purpose of them can be beamforming training and coverage extension

## Slide 9: References
[1] 11-23-1819-01-immw-integrated-mmwave-design-considerations
[2] 11-23-1878-01-immw-high-level-design-considerations-of-immw
[3] 11-23-1905-00-immw-high-level-thoughts-on-immw
[4] 11-23-1968-00-immw-discussion-on-general-direction-of-integrated-mmwave
[5] 11-23-2004-00-immw-technical-scope-proposal
[6] 11-24-0066-00-immw-discussion-on-target-objectives-for-immw