## Slide 1: MLO assisted beam training protocols in IMMW
Date: 2025-03-10
Authors:

## Slide 2: Introduction
The PAR of the Integrated Millimeter Wave (IMMW) wireless LAN amendment [1] defines the scope of unlicensed millimeter wave (mmWave) band (between 42GHz to 71GHz) to be non-standalone operation with the support of sub-7.25GHz multi-link operation (MLO)
The analog/hybrid beamforming is an important mechanism to compensate the high pathloss in mmWave band with the tradeoff of performance and complexity. The beam training protocols are required but can be further simplified under the MLO scheme compared to 11ad/ay [2].
In this contribution, we will discuss the MLO assisted beam training protocols

## Slide 3: MLO assisted beam training protocols
The 11ad/ay [3] defined a control mode PPDU format which can have 15dB processing gain compared to the lowest data MCS
  The control mode PPDU is essential for beam training protocols in the standalone mmWave band operation, especially when the receiver uses the quasi-omni antenna pattern such that the Rx beam gain is not utilized, e.g., used as the training PPDU during the transmit sector sweep in initial sector level sweep, etc.
The MLO assisted beam training protocols can be simplified by either without special control mode training PPDU design, or a simpler training PPDU format design with much relaxed dB gain requirements, considering the following beam training schemes
  Sector level sweep (SLS) with directional receive
  Beam refinement with multi-phase trainings
  Beam failure detection and recovery
Notes: As the Tx/Rx beam training already closes the gap between SLS and link with optimal Tx/Rx beam

## Slide 4: Sector level sweep with directional receive
The MLO assisted SLS is initiated from the non-mmWave link (or sub-7.25GHz link) by an announcement (or setup) frame exchange, when the mmWave link is yet to be established or a beam/link failure is detected which requires the retraining of the Tx and/or Rx beam/antenna weight vector (AWV) pair, etc.
  Training PPDU format: can be a null-data packet (NDP) format, if the preamble can contain all the essential training related parameters
  Training PPDU Tx/Rx beams: one Tx beam per training PPDU, and the receiver can use directional receive antenna pattern, as the receive beam information can be conveyed via the non-mmWave link
  Training PPDU bandwidth (BW): can use smaller BW than that of the data PPDU/device BW
    The extended range type of preamble enhancement can also be applied in the SLS training PPDU

## Slide 5: Sector level sweep with directional receive
Example: the SLS with directional Rx for DL direction (e.g., AP-MLD is the initiator, and non-AP STA MLD is the responder), with assumptions
  The training PPDU is NDP format, and NDP announcement (NDPA) is initiated at the non-mmWave link to negotiate the training parameters, including the directional Rx beam index at the responder
  The initiator conducts up to N (negotiated or capability setting) round of the transmit sector sweep (TXSS) with the same set of Tx Beams for each round
  The feedback exchange is at non-mmWave link, and the feedback is solicited by the initiator via BF poll for each TXSS round
    Once the initiator receives a valid feedback with Tx Beam ranking info, it may decide if it will continue to finish up all the N rounds, e.g., the initiator stops the SLS after M (<=N) rounds of TXSS
Notes: The delay could be a pre-defined IFS or including BO time (uncertainty)
The feedback can be:
    Initiated by the responder for each TXSS round it receives training PPDU or at the end of N rounds
    Or solicited by the initiator via BF poll for each TXSS round or at the end of N rounds

## Slide 6: Beam refinement with multi-phase trainings
The beam refinement procedure (BRP) is used to train the fine beam or track the beam change in response to the channel changes. It can be conducted right after the SLS and then initiated periodically, or initiated by request, e.g., triggered by the receiver when the beam failure is detected (beam failure discussion later)
  Training PPDU: additional training (TRN) fields will be added to each BRP training PPDU to evaluate multiple Tx or Rx beams, or both
  Training PPDU Tx/Rx beams: the non-TRN fields are applied with the best available Tx/Rx beam pair, while the TRN fields could be applied with different Tx/Rx beams
    The best available Tx/Rx beam pair can be negotiated by either the announcement frame exchange or other control frame exchange before it at the non-mmWave link
  Training PPDU BW: the non-TRN fields of the BRP training PPDU can have the same BW and preamble format as the SLS training PPDU (e.g., NDP), while the TRN fields can have the same BW as the data PPDU/device BW
Notes: Although it’s called SLS training PPDU or BRP training PPDU, it can use a unified PPDU format

## Slide 7: Beam refinement with multi-phase trainings
The execution overhead of BRP training can be simplified with hierarchical beam design, i.e., defining multiple training phases with specific purposes. For example,
  Phase 1. Joint training for both Tx and Rx beams, e.g., with Rx/Tx BRP training PPDU: beam tracking upon channel change (may use coarse and/or fine beams)
  Phase 2. Tx beam refinement (use Tx fine beams) with the best available Rx beam applied at the receiver, e.g., with Tx only BRP training PPDU
  Phase 3. Rx beam refinement (use Rx fine beams) with the best available Tx beam applied at the transmitter, e.g., with Rx only BRP training PPDU
These training phases can be conducted with different training periods
  Need a beam indication method to differentiate the beam index obtained from Phase 1 and Phase 2 feedback, while Phase 3 doesn’t require the feedback of best Rx beam info
  Phases 2 and 3 may be optional if Phase 1 already includes the fine beams

## Slide 8: Beam refinement with multi-phase trainings
Example diagram: BRP training phases with different training periods
  Each dashed box indicates a BRP training sequence, including announcement frame exchange for training parameter negotiation, training PPDU(s) transmission, and feedback transmission (not required in Phase 3)

## Slide 9: Beam failure detection and recovery
The mmWave link is established after a good Tx/Rx (fine) beam pair is selected through the beam training procedures, e.g., SLS and BRP. But the mmWave link may suffer from a beam failure when there is a sudden channel condition change, e.g., caused by moving, blockage, etc.
  Option 1. The data transfer switches to a more robust non-mmWave link when the mmWave link failure happens, and the transmitter initiates a full round of SLS and BRP to retrain a new Tx/Rx beam pair for the mmWave link
  Option 2. A beam failure detection and recovery procedure is conducted to obtain another good Tx/Rx beam pair before the link failure, and to keep the mmWave link less disrupted
The beam failure detection can be conducted at the receiver based on RSSI measurement or its variant, and then the receiver informs the transmitter via a request frame sent at the non-mmWave link for a beam recovery procedure

## Slide 10: Beam failure detection and recovery
Once confirmed, the transmitter can conduct a beam recovery procedure making use of SLS/BRP or similar procedure with limited candidate Tx/Rx beams (from previous trainings), to obtain a better new Tx/Rx beam pair
  The new Tx/Rx beam pair may not necessarily be an optimal Tx/Rx beam pair, but keeps relatively good link quality with speedy recovery and will be further refined by the continued BRP procedure

## Slide 11: Summary
We discussed the MLO assisted beam training protocols, which can include
  Sector level sweep with directional receive for the initial beam acquisition in the mmWave link establishment
    The SLS training PPDU can use smaller BW than that of data PPDU/device BW for power gain
  Beam refinement procedure with multi-phase trainings to track or further refine the Tx/Rx beams efficiently
    Each training phase can use a different BRP training PPDU type with different period
  A beam failure detection and recovery scheme
    The receiver detects the potential beam failure and requests a limited beam training procedure for a speedy beam failure recovery
    The recovery procedure can reuse SLS/BRP or similar procedure with limited candidate beams

## Slide 12: Straw Poll 1
Do you agree to define the IMMW beam training procedure using a training PPDU format which has same or limited dB sensitivity gain compared to the range of the SU PPDU preamble
  The limited dB gain is, e.g., up to 6dB

## Slide 13: Straw Poll 2
Do you agree to define the directional receive for the mmWave link sector level sweep (or initial beam acquisition) procedure in IMMW

## Slide 14: Straw Poll 3
Do you agree to define a beam failure detection and recovery procedure in IMMW

## Slide 15: References
[1] 11-24-0116-07-immw-immw-draft-proposed-par
[2] 11-22-1595-01-0uhr-some-questions-to-answer-in-the-sg
[3] Draft P802.11REVme_D7.0