## Slide 1: Considerations on UHR Sounding Operation
Date: 2025-03-11
Authors:

## Slide 2: Introduction
There are two possible sounding sequences for COBF in UHR
Sequential NDP based sounding
Joint NDP based sounding
In both sounding sequences, 2 APs initiate sounding sequences until all necessary CSI feedback are obtained.
total four sequences for sequential NDP based sounding
total two sequences for joint NDP based sounding
In this contribution, we discuss 2 possible issues that may occur during the CoBF channel sounding and propose solutions.

## Slide 3: UHR Sounding Protocol sequences (1/2)
UHR defines two sounding sequences to support DL CoBF. The first is a sequential NDP sounding sequence and the second is a joint NDP sounding sequence.
UHR NDP Announcement
BFRP
Trigger
Compressed Beamforming/CQI
AP 1
AP 2
STA 1
EHT Sounding NDP
UHR NDP Announcement
BFRP
Trigger
Compressed Beamforming/CQI
EHT Sounding NDP
UHR NDP Announcement
BFRP
Trigger
Compressed Beamforming/CQI
AP 1
AP 2
STA 1
EHT Sounding NDP
EHT Sounding NDP
UHR TB Sequential NDP sounding sequence initiated by AP 1
UHR TB Joint NDP sounding sequence initiated by AP 1

## Slide 4: UHR Sounding Protocol sequences (2/2)
To collect the channel state for CoBF transmission, each AP needs to initiate a sounding sequence. Only after both APs successfully perform sounding can CoBF transmission can start.
AP 1
AP 2
STA 1
STA 2
AP1 initiated sounding sequence(s)
AP2 initiated sounding sequence(s)
CoBF Trigger
total sounding duration
CoBF PPDU
CoBF PPDU
sounding interval
CoBF Trigger
CoBF PPDU
CoBF PPDU
AP1 initiated sounding sequence
AP2 initiated sounding sequence

## Slide 5: Problem 1
In some scenarios, the total sounding duration for CoBF sounding may be prohibitively long. For example, if the other AP is not able to obtain a TXOP due to channel being busy. This may lead to insufficient during CoBF as the channel may have changed since the start of the sounding.
AP 1
AP 2
STA 1
STA 2
AP1 initiated sounding sequence(s)
AP2 initiated sounding sequence(s)
total sounding duration
Channel busy

## Slide 6: Proposal
To prevent the problem, we propose to define a mechanism for truncating the CoBF sounding operation by either AP. Truncating the UHR sounding protocol allows AP1 to re-use existing CSI feedback in a non-CoBF PPDU before the CSI expires.
AP 1
AP 2
STA 1
STA 2
AP1 initiated sounding sequence(s)
AP2 initiated sounding sequence(s)
total sounding duration
Channel busy
Sounding termination notification
Option 1: Either of the APs transmit a sounding termination notification frame to the other AP.
Option 2: Sounding is terminated automatically after a timeout interval (e.g., starting from the end of the AP1 initiated sounding sequence(s))
Timeout interval
(1)
(2)

## Slide 7: Problem 2
During UHR TB joint NDP sounding or cross-BSS UHR TB sounding, the responding AP is expected to overhear the CSI feedback solicited by the initiating AP. In case of reception error by the overhearing AP (e.g., incorrect link parameters), CoBF can not be performed until the next sounding interval.
UHR NDP Announcement
BFRP
Trigger
Compressed Beamforming/CQI
AP 1
AP 2
STA 1
EHT Sounding NDP
Non-COBF
PPDU
Fail
CoBF PPDU
AP2 initiated sounding sequence(s)
EHT Sounding NDP
STA 2
AP1 initiated sounding sequence(s)
Success
Success
Success
Invite
Response
No

## Slide 8: Proposal
To solve the problem, we propose a CSI reception report mechanism for the responding AP.
The report may be transmitted by the responding AP on its own using its own TXOP. Or may be solicited by the initiating AP (e.g. using a trigger frame).
If the CSI reception report indicates failure, the initiating AP can perform one of the following
Retransmit the BFRP trigger frame
Reinitiate the sounding sequence that contains error.
Forward the CSI feedback to the responding AP (if available).
UHR NDP Announcement
BFRP
Trigger
Compressed Beamforming/CQI
AP 1
AP 2
STA 1
EHT Sounding NDP
Fail
EHT Sounding NDP
STA 2
AP1 initiated sounding sequence(s)
Success
CSI reception report (error)
BFRP
Trigger
Compressed Beamforming/CQI
Success

## Slide 9: Conclusion
Errors may occur when two APs perform CoBF sounding sequences. Due to the inherent time constraints involved with the CSI feedback during CoBF sounding, we proposed to define mechanisms to
Truncate the CoBF sounding procedure.
Report CSI feedback reception error by the responding AP.

## Slide 10: Strawpoll 1
Do you agree to add in the 11bn specification:
11bn defines a mechanism to truncate the UHR sounding protocol sequences initiated by an AP. The detailed mechanism is TBD.

## Slide 11: Strawpoll 2
Do you agree to add in the 11bn specification:
11bn defines a mechanism for an AP to report its CSI feedback reception status after a UHR TB sounding sequence initiated by another AP. The detailed mechanism is TBD.