## Slide 1: Transferred Context Indication for Seamless Roaming
Date: 2024-12-01
Authors:

## Slide 2: Abstract
Near-static context transfer is one of the key aspects of seamless roaming procedure:
  Enables a non-AP MLD to prepare the target AP MLD with necessary setups prior to roam
In this contribution we discuss some information items which can benefit the device side if included in context transfer signaling:
  Context transfer indication: Indication of which near static contexts have been successfully transferred and which ones failed.

## Slide 3: Context Transfer Background
A device may have set up more than one feature with the current AP.
Setting up each of the features one by one with the target AP can take multiple frame exchanges which is not desired.
As the device roams to a target AP, it is important that the features setup by STA with the current AP are also setup on the target AP.
Two types of context:
  Near static: setups which do not change on a short time scale.
    Limit to a few features
  Dynamic: which can keep changing on a short time scale.
Context | Type
Seq Number (SN) | Dynamic
Packet Number (PN) | Dynamic
BA context | Dynamic
BA setup | Near Static
SCS/MSCS | Near Static
EPCS | Near Static
TWT and variants (bTWT, rTWT, etc.) | Near Static
P2P TWT/CoEx session | Near Static
Example features that can benefit from context transfer

## Slide 4: Near Static Context Transfer
Near static context transfer procedure can enable a non-AP MLD to prepare a target AP MLD with necessary setups for its operation upon roam.
In this contribution, we discuss some information items whose inclusion in the context transfer signaling is critical or beneficial for the non-AP MLD.

## Slide 5: Transferred/Failed Context Indication
The context transfer response frame must contain an indication of either:
  Transferred context: contexts which were successfully transferred from the current AP MLD to the target AP MLD
  Failed context: alternatively an indication of which contexts were not transferred from the current AP MLD to the target AP MLD can be provided.
This information enables a non-AP MLD to determine which features need to be re-setup upon roam
Non-AP MLD
Current AP MLD
Target AP MLD
Context transfer req
Near static context transfer
Context transfer resp<…, transferred/failed context indication,…>

## Slide 6: Conclusion
In this contribution, we discussed signaling details for near static context transfer.
  Transferred/failed context indication