## Slide 1: IM pilot indices for OFDMA transmissions
Date: 2025-03-09
Authors:

## Slide 2: Introduction
Interference mitigation (IM) has been proposed and approved for 11bn [1-4]
  Main idea is to be able to detected, track and suppress interference when receiving a PPDU
  On January 2025 Interim session it was agreed to support…
    IM with LDPC only (Motion 245)
    Fixed IM pilots per BW (Motion 246)
    IM pilots occupy same subcarriers for all data symbols (Motion 247)
This contributions addresses the following TBDs
    IM pilot locations
    Support for IM with DRU
Propose IM pilot location design for …
  MU-PPDUs and TB-PPDUs that is compatible with OFDMA and non-OFDMA transmissions
  OFDMA TB-PPDUs with DRUs

## Slide 3: Considerations for IM pilot support and PPDU formats
Interference mitigation is advantageous to increase reliability of any PPDU transmission
  Receiver non-AP STAs with small number of antennas can apply adaptive equalization and phase compensation in the presence of narrow-band interference
  IM pilots in TB-PPDUs can help AP improve reliability of reception
    Especially important for DRU transmissions that seek range enhancements
Case 1: Non-DRU transmissions
  Propose IM pilot locations fixed per PPDU bandwidth and compatible with OFDMA and non-OFDMA transmissions
    Consistent number of IM pilots across RUs of equal size
  Only one IM enabled/disabled indication is required
Case 2: TB-PPDU with DRU
  Propose to use the fact that DRUs are distributed and define one per DBW to carry IM pilots
  Only one IM enabled indication is required

## Slide 4: Design criteria for IM pilot locations (non DRU case)
IM pilots should not affect regular pilots
  Regular pilots are used for phase tracking and should not be moved.
IM pilots should be spread evenly across PPDU bandwidth
  To better detect and suppress narrow-band or partial-band interference
  To better track frequency changes on interference channel
The number of IM pilots per RU size should be constant
  Every RU of specific size should always have same number of IM pilots regardless of its frequency location
  This maintains same NSD after inserting IM pilots
The overhead of IM pilots should be limited
  ~10% overhead is good compromise between reliability performance and overhead

## Slide 5: Proposed IM pilot locations (non DRU case) (1/2)
Define IM pilots in blocks with fixed tone distance equal to 9 tones
  (Quasi-)Symmetric structure and even distribution
    For 20MHz and 40MHz define two mirroring blocks of IM pilots with a fixed tone distance
    For 80MHz define 4 blocks (2 pairs mirroring each other) of IM pilots with fixed tone distance
  Insert additional IM pilots
    To make sure all RU sizes have same number of IM pilots regardless of Bandwidth and RU allocation
    To fill gaps in the IM pilot locations to maintain a minimum tone distance
BW | IM pilot indices (x) means optional | Total number of IM pilots |  | Overhead w.r.t. Full BW RU size |  | (Min., max) tone distance |  | Distance towards edge Sc.
20MHz | [[-119:9:-11], (-3), 4 , [11:9:119]] | 27 | 28 | 11.2% | 11.6% | (7,15) | (7,9) | 3
40MHz | [[-241:9:-7],(-3),(3),[7:9:241]] | 54 | 56 | 11.2% | 11.6% | (9,14) | (4,9) | 3
80MHz | = [4, (12), [15:9:249],(256),(259),[263:9:497]] [ , ] | 110 or 112 | 114 | 11% or 11.2% | 11.4% | (8,14), or (7,11) | (3,10) | 3
BW | IM pilot indices (x) means optional | Total number of IM pilots |  | Overhead w.r.t. Full BW RU size |  | (Min., max) tone distance |  | Distance towards edge Sc.
20MHz | [[-119:9:-11], (-3), 4 , [11:9:119]] | 27 | 28 | 11.2% | 11.6% | (7,15) | (7,9) | 3
40MHz | [[-241:9:-7],(-3),(3),[7:9:241]] | 54 | 56 | 11.2% | 11.6% | (9,14) | (4,9) | 3
80MHz |  | 110 or 112 | 114 | 11% or 11.2% | 11.4% | (8,14), or (7,11) | (3,10) | 3

## Slide 6: Proposed IM pilot locations (non DRU case) (2/2)
Minimum PHY parameters modification
  Need to modify NSD with IM pilots as NSD_IM = NSD - #IM pilots in RU
  Need to modify LDPC DTM only for RUs larger than 242-tones
RU size | NSD | Number of IM pilot tones | NSD_IM | NSD_IM_short (equal to 11be) | DTM_IM
26 | 24 | 3 | 21 | 6 | 1
52 | 48 | 6 | 42 | 12 | 3
106 | 102 | 12 | 90 | 24 | 6
242 | 234 | 27 | 207 | 60 | 9
 |  | 28 | 206 | 60 | 2
484 | 468 | 54 | 414 | 120 | 9
 |  | 56 | 412 | 120 | 4
996 | 980 | 110 | 870 | 240 | 15
 |  | 112 | 868 | 240 | 14
 |  | 114 | 866 | 240 | 2
New
DTM

## Slide 7: IM pilots for OFDMA TB-PPDU with DRUs (1/2)
Defining separate IM pilot locations for DRU case would increase complexity
However, DRUs can satisfy most IM pilot design criteria with minimum changes
Propose to use a fixed DRU per distribution bandwidth (DBW) for IM pilots
  Utilize full DRU to carry IM pilots
    No need to change NSD since DRU with IM pilots would not contain data
  DRUs are spread across bandwidth by design
  Regular pilots in DRU can be left unchanged
  A small size DRU can be selected to carry IM pilots and maintain low overhead w.r.t. DBW
  No need to have IM pilots spreading over several RUs

## Slide 8: IM pilots for OFDMA TB-PPDU with DRUs (2/2)
Definition of one fixed DRU per DBW and frequency block for IM pilots
  Option 1: Zero-energy IM pilots
    Specific set of DRUs (RU allocation indices) shall be left unallocated (AID12 = 2046) if IM is enabled
  Option 2: Active IM pilots
    IM pilots shall be transmitted on specific set DRUs (RU allocation indices)
      User allocated to such DRUs shall transmit IM pilots if IM is enabled
    Optionally, another specific DRU can be allocated to same user for parallel data transmission
      Power boost will be lower due to parallel IM pilot transmission
      User allocation is left up to implementation although it would be useful for STAs with lower pathloss
DBW | RU allocation subfield for IM pilots | DRU Index for IM pilot | RU allocation subfield for parallel IM pilot and data transmission | DRU index for IM pilot parallel data
20MHz | {7, 16, 26, 35} | 26-tone DRU8 | {8, 17, 27, 36} | 26-tone DRU9
40MHz | {43, 50} | 52-tone DRU7 | {44, 51} | 52-tone DRU8
80MHz | {58} | 106-tone DRU6 | {57} | 106-tone DRU5
RU allocation index for DRUs used to transmit IM pilots |  |  |  | 

## Slide 9: Signaling aspects
In all proposed cases only one IM enabled/disabled indication is needed
  Non-OFDMA MU-PPDU
    Already exists one bit (B13) in common info field of UHR-SIG to indicate IM enabled/disabled
  OFDMA MU-PPDU
    Can use same bit (B13) in common info field of UHR-SIG to indicate IM enabled/disabled
  TB-PPDU (without DRUs)
    Can use one UHR reserved bit in the TF common info field
  OFDMA TB-PPDU with DRUs
    Include IM enabled indication in UHR variant user info field in case of DRU
      Use one of the reserved bits of the SS allocation subfield, Or,
      Use one value of UL UHR-MCS subfield

## Slide 10: Conclusion
Fixed IM pilot locations can support MU-PPDUs and TB-PPDUs
  Non-OFDMA and OFDMA cases can also be supported including cases with DRUs
Proposed IM pilot locations with blocks of fixed tone distances
  Evenly spread IM pilots
  Same number of IM pilots for RUs of same size regardless of their frequency location
  Around 11% pilot overhead
  Only require one bit IM enable signaling
Proposed to support IM pilots for OFDMA with DRUs
  Select one fixed DRU per DBW and frequency block to carry IM pilots if IM is enabled
  IM enable indication in UHR variant user info field in case of DRU

## Slide 11: References
[1] 11-24/2008r2 PDT PHY Interference Mitigation
[2] 11-24/1785r2 Interference mitigation pilots definitions
[3] 11-24/1264r0 Supporting rx interference mitigation in TGbn
[4] 11-22/1649r0 MIMO interference suppression for enhanced reliability