## Slide 1: Information Exchange in the COBF Transmission Phase
Date: 2025-03-06
Authors:
Name | Affiliations | Address | Phone | email
Alice Chen | Qualcomm Technologies Inc. |  |  | alicel@qti.qualcomm.com
Sameer Vermani |  |  |  | svverman@qti.qualcomm.com
Bin Tian |  |  |  | btian@qti.qualcomm.com
Youhan Kim |  |  |  | youhank@qti.qualcomm.com
Ahmed Elsherif |  |  |  | 

## Slide 2: Introduction
Per MAC sequence, conceptually there will be three frames, i.e., the CoBF Invite, Response and Sync frames [1] for information exchange between the sharing and shared APs in the CoBF transmission phase
  CoBF Invite/Sync: sent from the sharing AP to the shared AP
  CoBF Response: sent from the shared AP to the sharing AP
Information exchange between two APs through these three frames to negotiate parameters and form the common preamble in CoBF transmission should be self-contained
In this presentation, we discuss the information exchange in the transmission phase, with the focus on PHY information

## Slide 3: Two Types of Information
Two types of information will be signaled
  Subfields in the common preamble (also called “PHY info”)
    Essential info: Parameters which are essential to pre-transmission negotiation
    Non-essential info: Parameters which are either pre-defined or derived from essential info
    Focus our discussion mostly on the essential info
  Basic control information
    Each frame needs to indicate what it is (‘CoBF Invite’/‘CoBF Acceptance’/‘CoBF Rejection’/‘CoBF Sync’)
      How to indicate this info is TBD

## Slide 4: Time/Frequency Resource
Bandwidth and Punctured Channel Information should be indicated in the Invite frame
  Shared AP needs BW info for scheduling users of different BW capabilities
  To be self-contained, also include the Punctured Channel Information
  No bandwidth or punctured pattern negotiation allowed
Range of data field indication and negotiation, as discussed in [1]
  Range of data field should be indicated in the Invite frame
    Minimum Number of Data OFDM Symbols (9 bits)
    Maximum Number of Data OFDM Symbols (9 bits)
  Suggested data field duration should be indicated in the Response frame
    Suggested Number of Data OFDM Symbols (9 bits)
  Suggest to fix the LDPC Extra Symbol Segment to 1 (for lower puncturing ratio) and fix the common pre-FEC padding factor to 4 (for largest payload for a given number of Data OFDM Symbols)

## Slide 5: Number of UHR-LTF Symbols
Number of UHR-LTF Symbols
  In the Invite frame, the sharing AP indicates the per-user Nss in the sharing BSS and the Maximum Total Nss Allowed for shared AP (2 bits)
  In the Response frame, the shared AP indicates the per-user Nss in the shared BSS and Extra LTF Allowed or not in the shared BSS
  In the Sync frame, the sharing AP determines the final Number of UHR-LTF Symbols and indicates it
  The following table shows all possible cases
    BSS1 or BSS2 may be sharing or shared BSS
Total Nss in BSS1 | Total Nss in BSS2 | Nss,total | Minimum N_LTF | N_LTF with Extra LTF
1 | 1 | 2 | 2 | 4
1 | 2 | 3 | 4 | 8
1 | 3 | 4 | 4 | 8
2 | 2 | 4 | 4 | 8

## Slide 6: User Info
Per-user MCS
  Sharing AP can’t determine the per-user MCS for its users at the time of the Invite frame, without knowing the number of spatial streams from the shared AP
  Shared AP determines and indicates the per-user MCS for its users in the Response frame, with the full knowledge of STA selection and per-user Nss across two BSSs
  Sharing AP finally determines the per-user MCS for its users after the Response frame and indicates the info in the Sync frame
Per-user 2xLDPC: Suggest to let each AP decides for its users
  A local rate adaptation decision at each AP
  Shared AP indicates the 2xLDPC bit for its users in the Response frame
  Sharing AP indicates the 2xLDPC bit for its users in the Sync frame

## Slide 7: User Field Ordering
User field ordering
  In each of the Invite/Response frame:
    If there is information for more than one users, suggest to order the users according to Nss in non-increasing order
  In the Sync frame:
    For ease of ‘copy and paste’, suggest to include the information of all users across two BSSs
    Suggest to order the users in the same order as in the UHR-SIG field in the CoBF transmission
      Note that the final user field ordering is according to Nss in non-increasing order (due to the design of the Spatial Configuration subfield) while keeping the user fields belong to the same BSS contiguous [2]
      In the case where the user fields of either BSS may go first, suggest that the user fields of the sharing BSS go first

## Slide 8: Info with Fixed Values
UHR-SIG MCS: Suggest to fix it to MCS0
Spatial Reuse (SR): Suggest to fix it to ‘PSR_AND_NON_SRG_OBSS_PD_PROHIBITED’
Interference Mitigation (IM): Suggest to fix it to ‘Disable’
PE Disambiguity
  As in [4, 5], with a fixed T_PE=20us, the PE Disambiguity becomes a fixed value of 1 according to the following

## Slide 9: Other Discussion
Non-essential info that uses fixed values doesn’t need to be signaled
  UL/DL, PPDU Type And Compression Mode, CoBF/CoSR Indication, UHR-SIG MCS, SR, IM, LDPC Extra Symbol Segment, Pre-FEC Padding Factor, PE Disambiguity
Suggest to signal the following TXOP dependent info (including both essential and non-essential but derivable info) in the Sync frame for ease of direct ‘copy and paste’
  BSS Colors, TXOP, Number of UHR-SIG Symbols, Number of CoBF Users
  Bandwidth, Punctured Channel Information, GI+LTF Size (indicated in the Invite [1])
  Info for all users

## Slide 10: Summary of Info Exchange – Part 1
Preamble Field/Control Info | Information / Subfield | Category | Carried in CoBF Invite | Carried in CoBF Response | Carried in CoBF Sync
Control Info | Information Flag | Essential | (‘CoBF Invite') | (‘CoBF Acceptance') | (‘CoBF Sync')
L-SIG | Length (12 bits) | Essential | Minimum Number of Data OFDM Symbols (9 bits), Maximum Number of Data OFDM Symbols (9 bits) | Suggested Number of Data OFDM Symbols (9 bits) | Yes
U-SIG | PHY Version Identifier (3 bits) | Essential | Yes | Yes | Yes
 | Bandwidth (3 bits) | Essential | Yes |  | Yes
 | UL/DL (1 bit) | Non-Essential (fixed to 0) |  |  | 
 | BSS Colors (6 bits each) | Non-Essential |  |  | Yes
 | TXOP (7 bits) | Non-Essential |  |  | Yes
 | PPDU Type And Compression Mode (2 bits) | Non-Essential (fixed to 2) |  |  | 
 | CoBF/CoSR Indication (1 bit) | Non-Essential (fixed to 0) |  |  | 
 | Punctured Channel Information (5 bits) | Essential | Yes |  | Yes
 | UHR-SIG MCS (2 bits) | Non-Essential (fixed to MCS0) |  |  | 
 | Number of UHR-SIG Symbols (5 bits) | Non-Essential |  |  | Yes

## Slide 11: Summary of Info Exchange – Part 2
Preamble Field/Control Info | Information / Subfield | Category | Carried in CoBF Invite | Carried in CoBF Response | Carried in CoBF Sync
UHR-SIG Common | Spatial Reuse (4 bits) | Non-Essential (‘Disabled’) |  |  | 
 | GI+LTF Size (2 bits) | Essential | Yes |  | Yes
 | Number Of UHR-LTF Symbols (3 bits) | Essential | Maximum Total Nss at shared AP (2 bits) | Extra LTF Allowed (1 bit) | Yes
 | LDPC Extra Symbol Segment (1 bit) | Non-Essential (fixed to 1) |  |  | 
 | Pre-FEC Padding Factor (2 bits) | Non-Essential (fixed to 4) |  |  | 
 | PE Disambiguity (1 bit) | Non-Essential (fixed to 1) |  |  | 
 | Interference Mitigation (1 bit) | Non-Essential (‘Disabled’) |  |  | 
 | Number of CoBF Users (i.e., Number of Non-OFDMA Users, 3 bits) | Non-Essential | Number of CoBF Users served by the sharing AP (2 bits) | Number of CoBF Users served by the shared AP (2 bits) | Yes
UHR-SIG User Field | STA ID (11 bits) | Essential | Yes (for users in sharing BSS) | Yes (for users in shared BSS) | Yes (for all users)
 | MCS (5 bits) | Essential |  | Yes (for users in shared BSS) | Yes (for all users)
 | Spatial Configuration (4 bits) | Essential | Nss (1 bit) (for users in sharing BSS) | Nss (1 bit) (for users in shared BSS) | Yes (for all users)
 | BSS Color Indication (1 bit) | Non-Essential |  |  | Yes (for all users)
 | 2xLDPC (1 bit) | Essential |  | Yes (for users in shared BSS) | Yes (for all users)

## Slide 12: Reference
11-25/381r0, Some open issues on COBF, Sameer Vermani, et al. (Qualcomm)
11-24/1822r4, COBF Design for UHR, Sameer Vermani, et al. (Qualcomm)
11-25/87r0, Co-Triggering Frame Design for CoBF, Insik Jung, et al. (LGE)
11-25/399r0, COBF/COSR Design Follow-up, You-Wei Chen (MediaTek)
11-25/401r0, CoBF PHY design consideration, Juan Fang, et al. (Intel)
11-25/397r0, Spatial Streams Indication for CoBF TF and PPDU, Junghoon Suh, et al. (Huawei)

## Slide 13: SP1
Do you agree to add the following to the 11bn SFD?
  The CoBF Invite frame carries the following information?
    How to indicate the information is TBD
  Supporting doc: 11-25/389r1, 11-25/399r0
Category | 
Control | ‘CoBF Invite’
PHY Common Info | Minimum Number of Data OFDM Symbols
 | Maximum Number of Data OFDM Symbols
 | PHY Version Identifier
 | Bandwidth
 | Punctured Channel Information
 | GI+LTF Size
 | Maximum Total Nss Allowed for shared AP
 | Number of CoBF Users in sharing BSS
Per-User Info in Sharing BSS | STA ID
 | Nss

## Slide 14: SP2
Do you agree to add the following to the 11bn SFD?
  The CoBF Response frame carries the following information?
    How to indicate the information is TBD
  Supporting doc: 11-25/389r1, 11-25/399r0
Category | 
Control | ‘CoBF Acceptance’
PHY Common Info | Suggested Number of Data OFDM Symbols
 | PHY Version Identifier
 | Extra LTF Allowed
 | Number of CoBF Users in shared BSS
Per-User Info in Shared BSS | STA ID
 | MCS
 | Nss
 | 2xLDPC

## Slide 15: SP3
Do you agree to add the following to the 11bn SFD?
  The CoBF Sync frame carries the following information?
    How to indicate the information is TBD
  Supporting doc: 11-25/389r1, 11-25/399r0, 11-25/401r0
Category | 
Control | ‘CoBF Sync’
PHY Common Info | Length
 | PHY Version Identifier
 | Bandwidth
 | Punctured Channel Information
 | BSS Color 1, BSS Color 2
 | TXOP
 | Number of UHR-SIG Symbols
 | GI+LTF Size
 | Number Of UHR-LTF Symbols
 | Number of CoBF Users
Per-User Info in Both BSS | STA ID
 | BSS Color Indication
 | MCS
 | Spatial Configuration
 | 2xLDPC

## Slide 16: SP4
Do you agree to add the following to the 11bn SFD?
  In each of the CoBF Invite, Response and Sync frames, if there is information for more than one users, the users are ordered according to Nss in non-increasing order?
    The order of users in the sharing BSS in the Sync frame is aligned with that in the Invite frame.
    The order of users in the shared BSS in the Sync frame is aligned with that in the Response frame.
  Supporting doc: 11-25/389r1, 11-25/381r0, 11-25/397r0

## Slide 17: appendix

## Slide 18: Conceptual Level Sequence for CoBF Transmission Phase
Concept level sequence in the transmission phase with 3-way handshaking
  COBF Invite: Sharing AP (TXOP holder) shares needed common preamble info in addition to which clients it will serve
  COBF Response: Shared AP acknowledges it can null its signal at sharing AP’s client and declares which clients it will serve
  COBF Sync: Sharing AP acknowledges it can null its signal at shared AP’s client
    Can be used as synchronization message as well
DL PPDU
Sharing AP
DL PPDU
Shared AP
COBF
Invite
SIFS
COBF
Response
SIFS
Shared TXOP
COBF
Sync
SIFS