## Slide 1: Link Reconfiguration Signaling Design for Next Generation WLANs
Date: 2024-08-06
Authors:

## Slide 2: Abstract
In this contribution, we discuss link reconfiguration framework based design for seamless roaming in next generation WLANs
  Signaling design and frame contents
  Examples based on the signaling for different use cases discussed in 11bn

## Slide 3: Seamless Roaming Procedural Overview
Phase | Purpose
Enh. Discovery | Domain AP info gathering
Recommendation | Info gathering for candidate AP assessment considering: Context Load, etc.
Preparation | Prepare 1 target AP MLD for roaming (more than one is TBD) Near static context transfer
Execution | Initiate transition procedures: Dynamic context transfer DS remapping
Buffered data handling | Handling buffered data at current AP Can be considered a part of the above stage
TGbn has agreed to define procedures that enable a non-AP MLD to roam from current AP MLD to target AP MLD while remaining in state 4.
A number of contributions have discussed various procedures for seamless roaming (summarized in the table)
A number of target use cases/scenarios have also been discussed so far:
  Preparation of target AP MLD links through current AP MLD prior to roaming
  Preparation (context transfer) done through target AP MLD
  …

## Slide 4: Signaling Details for Preparation and Execution
In our last contribution [1], we proposed an enhancement to 11be link reconfiguration request and response frames to perform preparation and execution.
In this contribution, we provide further details on the signaling
Further, we provide some examples of how the signaling can be used in:
  Preparation and execution phases when both are done
  Preparation and execution done with an SN reset
  Preparation done through target AP MLD

## Slide 5: Signaling details: Reconfiguration Request frame
Order | Meaning
1 | Category
2 | Protected UHR Action
3 | Dialog token
4 | Target AP MLD identifier
5 | Action indicator field
6 | Context to be transferred
7 | Reconfiguration Multi-link element
8 | OCI element
Modified Reconfiguration request frame format
Target AP MLD to roam to. Must be in the same SMD as current AP MLD.
 | Near static | Dynamic reset | Context pull | Roam | Reserved/TBD
Bits: | 1 | 1 | 1 | 1 | 4
Compilation of individual bits for each feature/context set to 1/0 values
Indicate per-STA profile of target AP that needs to be added. Missing in execution phase if preparation phase is completed.

## Slide 6: Signaling Details: Reconfiguration Response Frame
Modified Reconfiguration response frame format
Order | Meaning
1 | Category
2 | Protected UHR Action
3 | Dialog Token
4 | AID (optional)
5 | Transferred context indication
6 | Operation parameters
7 | Deadline/Timeout
8 | Suggested parameters
9 | Count
10 | Reconfiguration Status List
11 | Group Key Data (optional)
12 | OCI element (optional)
13 | Basic Multi-link element (optional)
Ideally AID should not change. But this can cause some complications. So a simple option is to include AID in response when response is for roam execution phase.
Compilation of individual bits for each feature/context set to 1/0 values successfully transferred to target AP MLD
Operation parameters needed for each feature if transferred.
Examples: SCS: SCS descriptor element that carries only SCS ID, service start time, service start time link ID (remaining optional fields skipped), EPCS: priority access ML element.
Deadline to roam after preparation phase is completed/timeout after execution phase is completed.
If context is rejected at target AP MLD, then suggested value to help non-AP MLD to renegotiate and converge faster at target AP MLD. E.g., suggested delay bound values for SCS setup

## Slide 7: Example 1: preparation phase + execution phase
PREP Req: Modified Reconfiguration request frame format
PREP Resp: Modified Reconfiguration response frame format
Order | Meaning
1 | Category
2 | Protected UHR Action
3 | Dialog token
4 | Target AP MLD identifier
5 | Action indicator field: NS
6 | Context to be transferred
7 | Reconfiguration Multi-link element
8 | OCI element
Order | Meaning
1 | Category
2 | Protected UHR Action
3 | Dialog Token
4 | AID (optional)
5 | Transferred context indication
6 | Operation parameters
7 | Roam Deadline
8 | Suggested parameters
10 | Count
11 | Reconfiguration Status List
12 | Group Key Data (optional)
13 | OCI element (optional)
14 | Basic Multi-link element (optional)
STA
Current AP
Prep req
Interaction with target
Prep resp
EXE Req: Modified Reconfiguration request frame format
EXE Resp: Modified Reconfiguration response frame format
Order | Meaning
1 | Category
2 | Protected UHR Action
3 | Dialog Token
4 | AID (Not present if provided in prep phase)
5 | Timeout
Order | Meaning
1 | Category
2 | Protected UHR Action
3 | Dialog token
4 | Target AP MLD identifier
5 | Action indicator field: R
Exe req
Exe resp
Interaction with target

## Slide 8: Example 2: Preparation phase + execution phase with SN reset
PREP Req: Modified Reconfiguration request frame format
STA
Current AP
Prep req
Interaction with target
Prep resp
EXE Req: Modified Reconfiguration request frame format
Exe req
Exe resp
Interaction with target
PREP Req: Modified Reconfiguration request frame format
Order | Meaning
1 | Category
2 | Protected UHR Action
3 | Dialog token
4 | Target AP MLD identifier
5 | Action indicator field: NS + DR
6 | Context to be transferred
7 | Reconfiguration Multi-link element
8 | OCI element
EXE Req: Modified Reconfiguration request frame format
Order | Meaning
1 | Category
2 | Protected UHR Action
3 | Dialog token
4 | Target AP MLD identifier
5 | Action indicator field: R
PREP Resp: Modified Reconfiguration response frame format
Order | Meaning
1 | Category
2 | Protected UHR Action
3 | Dialog Token
4 | AID (optional)
5 | Transferred context indication
6 | Operation parameters
7 | Roam Deadline
8 | Suggested parameters
10 | Count
11 | Reconfiguration Status List
12 | Group Key Data (optional)
13 | OCI element (optional)
14 | Basic Multi-link element (optional)
EXE Resp: Modified Reconfiguration response frame format
Order | Meaning
1 | Category
2 | Protected UHR Action
3 | Dialog Token
4 | AID (optional)
5 | Timeout

## Slide 9: Example 3: preparation through target AP
STA
Target AP
Exe(+prep) req
Exe(+prep) resp
Interaction with previous AP MLD
Prep req: Modified Reconfiguration request frame format
Prep req: Modified Reconfiguration response frame format
Order | Meaning
1 | Category
2 | Protected UHR Action
3 | Dialog Token
4 | AID (optional)
5 | Transferred context indication
6 | Operation parameters
8 | Suggested parameters
10 | Count
12 | Reconfiguration Status List
12 | Group Key Data (optional)
13 | OCI element (optional)
14 | Basic Multi-link element (optional)
Order | Meaning
1 | Category
2 | Protected UHR Action
3 | Dialog token
4 | Target AP MLD identifier – old AP
5 | Action indicator field: CP + R
6 | Context to be transferred
7 | Reconfiguration Multi-link element
8 | OCI element

## Slide 10: Conclusion
In this contribution we discuss the signaling for seamless roaming based on link reconfiguration framework
We further discuss the example use cases and how the signaling can be used in those use cases

## Slide 11: References
[1] IEEE 802.11-25/388, “Link Reconfiguration Framework for Preparation and Execution Phases of Seamless Roaming”