## Slide 1: Renegotiation based on Link Reconfiguration Framework for Next Generation WLANs
Date: 2024-08-06
Authors:

## Slide 2: Abstract
In this contribution, we discuss signaling for performing renegotiation during seamless roaming procedure
We also provide example signaling and example operation based on the signaling

## Slide 3: Seamless Roaming Procedural Overview
Phase | Purpose
Enh. Discovery | Domain AP info gathering
Recommendation | Info gathering for candidate AP assessment considering: Context Load, etc.
Preparation | Prepare 1 target AP MLD for roaming (more than one is TBD) Near static context transfer
Execution | Initiate transition procedures: Dynamic context transfer DS remapping
Buffered data handling | Handling buffered data at current AP Can be considered a part of the above stage
TGbn has agreed to define procedures that enable a non-AP MLD to roam from current AP MLD to target AP MLD while remaining in state 4.
A number of contributions have discussed various procedures for seamless roaming (summarized in the table)
A number of target use cases/scenarios have also been discussed so far:
  Preparation of target AP MLD links through current AP MLD prior to roaming
  Preparation and execution in a single step through current AP MLD
  Preparation (context transfer) done through target AP MLD
  Renegotiation of context during roaming
  …

## Slide 4: Signaling Details for Renegotiation Procedure
In this contribution, we discuss the signaling for performing renegotiation during the seamless roaming procedure
We provide example operation based on the signaling

## Slide 5: Signaling details: Reconfiguration Request frame
Order | Meaning
1 | Category
2 | Protected UHR Action
3 | Dialog token
4 | Target AP MLD identifier
5 | Action indicator field
6 | Context to be transferred
7 | Context to renegotiate
8 | Renegotiation parameters
9 | Reconfiguration Multi-link element
10 | OCI element
Modified Reconfiguration request frame format
Context that needs to be renegotiated along with the parameter values.
This can be a little tricky and we need to decide how to handle rejection cases.
One option can be to allow a single renegotiation chance and handle everything else using baseline with target AP MLD.

## Slide 6: Signaling Details: Reconfiguration Response Frame
Modified Reconfiguration response frame format
Order | Meaning
1 | Category
2 | Protected UHR Action
3 | Dialog Token
4 | AID (optional)
5 | Transferred context indication
6 | Operation parameters
7 | Roam Deadline
8 | Suggested parameters
9 | Renegotiation response
10 | Count
11 | Reconfiguration Status List
12 | Group Key Data (optional)
13 | OCI element (optional)
14 | Basic Multi-link element (optional)
Indication of accept/reject for new parameters.

## Slide 7: Example Operation: Renegotiation of Context
STA
Current AP
Prep req(..,SCS renegotiate, new delay bound = 20ms, ..)
Prep resp(…, reject, …)
Interaction with target
Prep req: Modified Reconfiguration request frame format
Order | Meaning
1 | Category
2 | Protected UHR Action
3 | Dialog token
4 | Target AP MLD identifier
5 | Action indicator field: R
7 | Context to renegotiate
8 | Renegotiation parameters
7 | Reconfiguration Multi-link element
8 | OCI element
Prep req: Modified Reconfiguration response frame format
Order | Meaning
1 | Category
2 | Protected UHR Action
3 | Dialog Token
4 | AID (optional)
7 | Roam Deadline
8 | Suggested parameters
9 | Renegotiation response
10 | Count
12 | Reconfiguration Status List
12 | Group Key Data (optional)
13 | OCI element (optional)
14 | Basic Multi-link element (optional)
Target AP
SCS with delay bound of 40 ms
SCS req(…,delay bound = 30ms, ..)
SCS resp
STA roams to target AP
…

## Slide 8: Conclusion
In this contribution we discuss the renegotiation of near static context based on the link reconfiguration framework
We provide information items that can be added to the link reconfiguration request and response frames
We also provide example operation based on the signaling