## Slide 1: New MCS Capability Follow Up
Date: 2025-03-08
Authors:
Name | Affiliations | Address | Phone | email
Ross Jian Yu | Huawei |  |  | ross.yujian@huawei.com

## Slide 2: Background
The following motion has passed:
  Mandatory support MCSs of QPSK with code rate 2/3; 16QAM with code rate 2/3; 16QAM with code rate 5/6; 256QAM with code rate 2/3.
    Support for 256QAM with code rate 2/3 for 20MHz only devices is TBD.
  [Motion #216, [264] and [274, 275]]
Support of 256-QAM in 802.11ax and 802.11be is optional for 20 MHz only devices:
  An EHT STA may support the following features:
    EHT-MCSs 8 to 13 (transmit and receive) if the STA is a 20 MHz-only non-AP STA and EHT-MCSs 10 to 13 (transmit and receive) if the STA is not a 20 MHz-only non-AP STA.

## Slide 3: New MCS Capability follow-up
Propose that the support of 256QAM with code rate 2/3 for 20MHz only devices is optional.
  aligns with the support of 256QAM (MCS 8 and 9) in 802.11ax and 802.11be.

## Slide 4: SP1
Do you agree to make the following changes to the 802.11bn SFD?
  Mandatory support MCSs of QPSK with code rate 2/3; 16QAM with code rate 2/3; 16QAM with code rate 5/6; 256QAM with code rate 2/3.
    Support for 256QAM with code rate 2/3 for 20MHz only devices is TBD optional.
  [Motion #216, [264] and [274, 275]]

## Slide 5
11-24-0209-09-00bn-specification-framework-for-tgbn, Ross Jian Yu (Huawei)
IEEE P802.11be D7.0
References