## Slide 1: Supporting EMLSR STAs under CBF
Date: 2024-10-25
Authors:

## Slide 2: Background
For the CBF data transmission sequence, we expect that the overall sequence will look as below after accounting for cases (e.g., EMLSR) where ICF/ICR will occur between sharing/shared AP and their associated STAs.
CBF-invite
CBF-response
AP1
AP2
ICF to assoc STAs
AP1-STAs
AP2-STAs
ICR
ICF to assoc STAs
ICR
CBF-Trigger
CBF PPDU
CBF PPDU
MU-BAR
BA
MU-BAR
BA

## Slide 3: Problem
A STA following baseline EMLSR rules will go back to listen mode shortly after detecting no frame for itself.
Multiple places in the CBF sequence where the STAs associated to sharing AP or shared AP will go back to listen mode before completing their data+BA exchange.
CBF-invite
CBF-response
AP1
AP2
ICF to assoc STAs
AP1-STAs
AP2-STAs
ICR
ICF to assoc STAs
ICR
CBF-Trigger
CBF PPDU
CBF PPDU
MU-BAR
BA
MU-BAR
BA
AP1-STAs go to
listen mode
AP2-STAs go to
listen mode
AP2-STAs go to
listen mode

## Slide 4: Proposed resolution
So, after sending the ICRs, non-AP STAs need to remain in the link in which CBF frame exchange is taking place to cover all possible inactivity periods caused by the CBF sequence i.e.,
  After sending their respective ICR frames, the EMLSR STAs associated to AP-1 and AP-2 need to wait till at least the CBF Data PPDU before going back to listen mode.
  After receiving the CBF DL PPDU, the STAs associated to AP-2 waits till at least the BAR transmission from AP-2 before going back to listen mode
Proposal: only during the CBF frame exchange sequence, relax the baseline EMLSR conditions regarding when to go back to listen mode to cover extended periods of inactivity.
  The signaling (including whether the extended timeout period duration is simply fixed in spec) is TBD.

## Slide 5: Straw Poll-1
Do you agree:
if an eMLSR non-AP MLD that receives an ICF addressed to one of its affiliated STAs during CoBF sequences and if the affiliated STA responds with an ICR, then the eMLSR non-AP MLD shall follow the eMLSR procedure defined in 35.3.17, except that the STA shall use an extended time-out period prior to switching back upon inactivity:
  The duration of the extended time-out period shall be sufficient to cover any inactivity period within the COBF sequence, e.g. (but not limited to), from the end of the ICR to the beginning of the data PPDU, or from the DL PPDU until the beginning of the MU-BAR frame from the shared AP for STAs associated with the shared AP
  The signaling and derivation of these timeout periods to the STA are TBD.
  Once the eMLSR STA(s) switch back to listen mode, they start using the default time-out period (aSIFSTime + aSlotTime + aRxPHYStartDelay) in future TXOPs unless otherwise indicated in the ICF.
  This is applicable to CoBF transmission sequence

## Slide 6: Straw Poll-2
Do you agree that an AP MLD that receives an ICR from a STA affiliated with an EMLSR non-AP MLD during CBF data frame exchange does not attempt to transmit to the eMLSR non-AP MLD on another link during the extended time-out periods, per baseline behavior ?