## Slide 1: Dynamic power save – ICF required
Date: 2025-03-08
Authors:

## Slide 2: ICF prior to frame exchange
We are defining Dynamic Power Save (DPS) for non-AP STAs, a mechanism that allows to transition from a low capability mode to a high capability mode thanks to the ICF-ICR exchange, in order to save power during the listening period
We need to decide if the DPS assisting AP needs:
  A) to transmit ICF prior to any frame exchange with a DPS STA, similarly to eMLSR operation
  or B) to transmit ICF only prior to the frame exchanges that are intended to be transmitted in high capability mode
    Which means that in that case the DPS assisting AP can transmit frames other than ICF to the DPS STA in low capability mode

## Slide 3: ICF prior to frame exchange
There are pros and cons for the 2 modes
  A) allows to reuse eMLSR implementation and save extra power
  B) allows to not always need to have the overhead of the ICF-ICR transmission for short packets for instance
And a clear majority is not emerging to allow to select only one mode.
We therefore propose to define the 2 modes under DPS and allow the non-AP STA to select the mode that it will use when it enables DPS

## Slide 4: Proposal
Define 2 modes under DPS for a non-AP STA
  One mode where the DPS Assisting AP shall initiate frame exchanges with a DPS STA by sending an ICF if it intends to transmit to the DPS STA in HC mode
    In that case, the DPS Assisting AP may exchange frames with the DPS STA without being required to send an ICF as long as the frames use parameters consistent with the STAs’ LC mode
    The mode is not allowed if the DPS STA is operating on an eMLSR link
  One mode where the DPS Assisting AP shall initiate any frame exchange with a DPS STA by sending an ICF (i.e., the DPS Assisting AP can not exchange any frames with the DPS STA unless they are preceded with an ICF)
Define a field, called ICF-required, in the frame sent by the non-AP STA to enable DPS in order to select the mode with which the STA will operate once DPS is enabled
  A DPS Assisting AP shall support operation with a DPS STA for both modes

## Slide 5: Straw Poll
Do you agree to add the following to the 11bn SFD:
define a procedure for a DPS non-AP STA to indicate, during the DPS enablement procedure, an ICF-required field, where:
  If ICF-required is set to 0, the DPS Assisting AP shall initiate frame exchanges with a DPS STA by sending an ICF if it intends to transmit to the DPS STA in HC mode (i.e. the DPS Assisting AP may exchange frames with the DPS STA without being required to send an ICF as long as the frames use parameters consistent with the STAs’ LC mode)
    ICF-required set to 0 is only allowed if the DPS STA is not operating on an eMLSR link
  If ICF-required is set to 1, the DPS Assisting AP shall initiate any frame exchange with a DPS STA by sending an ICF (i.e., the DPS Assisting AP can not exchange any frames with the DPS STA unless they are preceded with an ICF)
A DPS Assisting AP shall support operation with a DPS STA that has set ICF-Required to 0 or 1