## Slide 1: Low Latency Indication
Date: 2025-03-09
Authors:
Name | Affiliations | Address | Phone | email
Liwen Chu Huizhao Wang Hongyuan Zhang Rui Cao Sudhir Srinivasa Hui-Ling Lou | NXP |  |  | 

## Slide 2: Recap: Location Indication
The group agreed the following low latency indication
  TGbn defines or improves an existing mechanism so that a non-AP STA that is a TXOP responder can indicate its buffered low latencyLL traffic needs (for traffic from the TxOP TXOP responder to the TxOP TXOP Holder) in a control response frame. The TXOP holder should consider the indication in determining subsequent actions. Subsequent actions related to this indication are out of the scope of the standard.
    Note: whether an AP can Indicate indicate its low latency needs is TBD
  [Motion #273, [264] and [288-300]]

## Slide 3: ICF/ICR in 11bn
11bn decided to repurpose BSRP Trigger and Multi-STA BA for various features since BSRP Trigger and Multi-STA BA are flexible enough to carry the additional information
  Solicited unavailable time report for in-device coexistence.
    The Multi-STA BA is the response to carry the unavailable time in special Per AID TID Information field.
  unsolicited unavailable time report for in-device coexistence.
    The Multi-STA BA is the acknowledgement to BSRP Trigger carrying the unavailable time.
      No special Per AID TID Info field is needed.
  Responding frame for NPCA when non-HT duplicate PPDU needs to be used for the AP to carry the response.

## Slide 4: Multi-STA BA Format For Unavailable Time Report
The following special Per AID TID Indo field is used to carry the unavailable time:
  AID11 field equal to the same special value as the special Per AID TID Info field carrying unavailable information (Feedback Per AID TID Info field).
  The Low Latency Indication is included in the Feedback field of the Feedback Per AID TID Info field (the one that carries control feedback)
  The Feedback Type field (Located in B12 to B15 of the Block Ack Starting Sequence Control) is set to 1
    Note: Feedback Type field set to 0 is used for DUO feedback.
  TBD bits in the Feedback field is defined to provide the low latency need.

## Slide 5: Summary
We proposed Multi-STA BA being used to carry LL need:
  AID11 field equal to the same special value as the AID11 field of Feedback Per AID TID Info field.
  The Low Latency Indication is included in the Feedback field of the Feedback Per AID TID Info field.
  The Type field is defined in Sequence Number field to differentiate the information being carried.

## Slide 6: SP1
Do you agree to amend Motion #273 as following?
  TGbn defines or improves an existing mechanism so that a non-AP STA that is a TXOP responder can indicate its buffered low latencyLL traffic needs (for traffic from the TxOP TXOP responder to the TxOP TXOP Holder) in a control response frame. The TXOP holder should consider the indication in determining subsequent actions. Subsequent actions related to this indication are out of the scope of the standard.
    Note: whether an AP can Indicate indicate its low latency needs is TBD
    The Low Latency Indication is included in the Feedback field of the Feedback Per AID TID Info field (the one that carries control feedback).
    The Feedback Type field (Located in B12 to B15 of the Block Ack Starting Sequence Control) is set to 1
      Note: Feedback Type field set to 0 is used for DUO feedback
    TBD bits in the Feedback field is defined to provide the low latency need.