## Slide 1: ICF and NAV Operation
Date: 2025-03-09
Authors:
Name | Affiliations | Address | Phone | email
Liwen Chu Huizhao Wang Hongyuan Zhang Rui Cao Sudhir Srinivasa Hui-Ling Lou | NXP |  |  | 

## Slide 2: Recap: RTS, MU-RTS and NAV Operation
A NAVTimeout is defined as
  (2 × aSIFSTime) + (CTS_Time) + aRxPHYStartDelay + (2 × aSlotTime).
The NAV timer can be reset if the detected frame exchange solicited by RTS or MU-RTS fails
  When the following conditions are true
    a STA receives RTS or MU-RTS sets its NAV timer
    The STA doesn’t detect PHY-RXEARLYSIG.indication or PHYRXSTART. indication primitive is received within NAVTimeout period related to the end of the PPDU carrying the RTS or MU-RTS
  Then the STA can reset is NAV timer.

## Slide 3: BSRP Trigger
In 11bn, MU-RTS is replaced by BSRP in some use cases
  In DSO, BSRP Trigger is the ICF.
  In DUO of in-device coexistence, BSRP is the ICF.
  In NPCA, BSRP is the ICF being transmitted by a non-AP STA to its associated AP.
In some other features, such replacement is also required.
This is a requirement to reset NAV timer when BSRP is detected.

## Slide 4: BSRP and NAV Operation
A NAVTimeout is defined as
  (2 × aSIFSTime) + T_PREAMBLE + T_SIGNAL + UL_Length + aRxPHYStartDelay + (2 × aSlotTime)
  (see Table 17-5—Timing-related parameters).
The NAV timer can be reset if the detected frame exchange solicited by BSRP fails
  When the following conditions are true
    a STA receives BSRP sets its NAV timer
    The STA doesn’t detect PHY-RXEARLYSIG.indication or PHYRXSTART. indication primitive is received within NAVTimeout period related to the end of the PPDU carrying the BSRP
  Then the STA can reset is NAV timer.

## Slide 5: Summary
We proposed BSRP and NAV operation:
  The NAVTimeout is defined related to UL TB PPDU length.
  A STA detects frame exchange with BSRP as the soliciting frame fails and its NAV timer is set be BSRP can reset its NAV timer.

## Slide 6: SP1
Do you support that an UHR STA that sets its NAV timer per the BSRP Trigger frame may reset its NAV timer if the following condition is true
  no PHY-RXEARLYSIG.indication or PHYRXSTART.indication primitive is received from the PHY during a NAVTimeout period.
    The NAVTimeout period is equal to (2 × aSIFSTime) + T_PREAMBLE + T_SIGNAL + UL_Length + aRxPHYStartDelay + (2 × aSlotTime).
(see Table 17-5—Timing-related parameters)