## Slide 1: A Third Equation for Long-Term Slot Sync in Greenfield Spectrum
Mar 2025
Authors:
Name | Affiliation | Phone | email
Brian Hart | Cisco Systems |  | brianh@cisco.com
Binita Gupta | Cisco Systems |  | 
Malcolm Smith | Cisco Systems |  | 
Juan Carlos Zuniga | Cisco Systems |  | 
Stephen Orr | Cisco Systems |  | 
Javier Contreras | Cisco Systems |  | 

## Slide 2: Situation Slotted Access is regarded as a Good Thing in Wireless Channel Access
And certain technologies, like HiP EDCA, really lean into slot alignment [1]
Ditto, Multi-AP Coordination would also benefit from slot alignment
ALOHA
Slotted ALOHA
CSMA/CA (built on slots)

## Slide 3: Problem: For 802.11 at 2.4/5/6 GHz, slot synchronization is quickly lost in OBSS environments with out-of-range nodes
Many simulations have most/all APs and STAs in range of each other, so don’t encounter this slot asynchronism

## Slide 4: Solution (1/3): For 802.11 at 2.4/5/6 GHz, slot synchronization can be retained for appreciably longer via a simple PPDU Extension with 1μsec granularity

## Slide 5: Solution (2/3): The solution is a third design equation (but it is too hard to introduce at 2.4/5/6 GHz due to legacy PPDUs and products)
Currently the MAC design rules (10.3.7 DCF timing relations, 10.23.2.4 Obtaining an EDCA TXOP) are based on two equations:
  aSlotTime, based on aCCATime, aMACProcessingDelay, aRxTxTurnaroundTime, aAirPropagationTime
  aSIFSTime, based on aRxPHYDelay, aMACProcessingDelay, aRxTxTurnaroundTime
CSMA/CA powered by wide-area slot synchronization access needs a third equation: e.g.,
  Option A (TXOP-level alignment):
    Duration(TXOP) needs to be an integer multiple of aSlotTime
    Minimizes padding, but slot sync is typically lost if PIFS or EIFS recovery is invoked (fail)
  Option B (PPDU-level alignment):
    TXTIME(TXOP) + aSIFSTime needs to be an integer multiple of aSlotTime
    EIFS becomes an integer multiple of aSlotTime too
    Adds extra padding, but this come in handy if PIFS or EIFS recovery need to be invoked
    Given the OFDM symbol duration is not an integer (sub)multiple of aSlotTime, this padding is most easily and robustly achieved by the PPDU Extension at the end of each PPDU having suitable granularity

## Slide 6: Solution (3/3) Since IMMW only needs to coexist with legacy, IMMW spectrum can be considered as greenfield, where the third constraint can be introduced
Assume 8x overclocking is applied, to both PPDU clock and MAC clock
Then we additionally want to achieve:
  TXTIME(TXOP) + aSIFSTime needs to be an integer multiple of aSlotTime
For PPDUs, calculate TXTIME as usual, then append an extra Slot-Sync PE of duration:
  aSlotTime * ceil((TXTIME+aSIFSTime)/aSlotTime) - (TXTIME+aSIFSTime)
  This Slot Sync PE is globally applied to all PPDUs sent by IMMW STAs, so no additional SIG signaling is required
  Desirable spectral characteristics if constructed as a cyclic extension of the final OFDM symbol
  Required padding resolution is 1μsec / upclocking rate, or 0.125μsec for 8x overclocking

## Slide 7: Summary
Slot synchronization is desirable to reduce collisions
802.11 CSMA/CA is not designed to preserve slot synchronization for out-of-range BSSs
Many simulations have most/all APs and STAs in range of each other, so don’t encounter this slot asynchronism
We can provide for slot synchronism that is sustained and retained across multiple hops if we introduce a third design constraint
  TXTIME(TXOP) + aSIFSTime needs to be an integer multiple of aSlotTime
This design constraint is readily achieved in greenfield bands, such as IMMW, by appending every PPDU with a Slot-Sync PE of duration:
  aSlotTime * ceil((TXTIME+aSIFSTime)/aSlotTime) - (TXTIME+aSIFSTime)
Likely resolution is 0.125μsec

## Slide 8: References
[1] 11-23/1065r0, 11-23/2126r0, 11-24/0467r1, 11-24/0840r0, 24/1144, Dmitry Akhmetov (Intel) et al