## Slide 1: Further details on UHR low latency
Authors:
Name | Affiliations | Address | Phone | Email
Reza Hedayat | Apple Inc. |  |  | 
Mohamed Abolsoud |  |  |  | 
Yong Liu |  |  |  | 
Anuj Batra |  |  |  | 

## Slide 2
During a TXOP, a TXOP-responder sends low latency (LL) indication to the TXOP-owner
LL request signaling:
  May be carried in a CRF, e.g. BA
  May be carried in an ICR, e.g. M-BA
Types of LL indication [1,2]:
  Request to transmit data to the TXOP-holder
  Request to opt out of the TXOP
LL session
  During a LL session, AP/non-AP STA TXOP-owners expect to receive LL indication
Background: Overview of LL proposals

## Slide 3
LL signaling in CRF
BA: using currently available bits (5 reserved bits)
  However, these reserved bits may not be suitable to be used for LLI
M-BA: use M-BA instead of BA to carry LLI
  Currently M-BA can be used for acknowledging MPDUs carried in multi-TID single-STA A-MPDUs.
    9.3.1.8.6: “The Multi-STA BlockAck frame is supported if either UL MU or multi-TID A-MPDU operation is 5 supported and acknowledges MPDUs carried in an HE TB PPDU or multi-STA multi-TID, multi-STA single-TID, or single-STA multi-TID A-MPDUs.”
    Spec change: need to allow the use of M-BA for single-TID A-MPDUs
  The goal is to accommodate the LL signaling indication in M-BA regardless if the M-BA acts a control response frame (i.e. a block acknowledgment to an A-MPDU) or as ICR (as a response to an ICF)
Signalling for LL indication — 1

## Slide 4
Proposal: LL signaling carried in ICR/M-BA
  The LL signaling is always present, during a LL session, regardless if the STA has a request for LL transmission
  In other words, the LL request indicates no-request or indicates a request for reverse direction
  As a result, the provided feedback is a fixed-size feedback whose length is known to the receiving STA
A feedback Per AID TID Info field carries LL signaling
  The Starting Sequence Control and Block Ack Bitmap to carry the type and the LL request and its attributes.
  The Feedback Type field (located in B12 to B15 of the Block Ack Starting Sequence Control) is set to 1
  Two or more bits in Block Ack Bitmap field is defined to provide the low latency need
Signalling for LL indication — 2

## Slide 5
Once the TXOP-owner receives the LL signaling in an ICR, it should consider the request in subsequent actions
An AP TXOP-owner may consider the received LL signaling in triggering the requesting STA
A TXOP-owner may provide reverse direction grant to the requesting STA, per baseline RD procedure
An AP TXOP-owner may share the TXOP with the the requesting STA, via the baseline TXS procedure
Subsequent actions by the TXOP-owner

## Slide 6
This contribution proposes to carry low latency indication in an ICR
Given the use of M-BA as ICR, we propose to use M-BA to carry the low latency indication
Summary

## Slide 7
Define or improve an existing mechanism so that a non-AP STA that is a TXOP responder can indicate its low latency needs (for traffic between the TXOP responder and the TXOP Holder) in a control response frame that is an M-BA frame. The TXOP holder should consider the indication in determining subsequent actions. Subsequent actions related to this indication are out of the scope of the standard.
  Note: whether an AP can Indicate its Low latency needs is TBD
  The Low Latency Indication is included in the Feedback field of the Feedback Per AID TID Info field (the one that carries control feedback).
The Feedback Type field (Located in B12 to B15 of the Block Ack Starting Sequence Control) is set to 1
Note: Feedback Type field set to 0 is used for DUO feedback.
TBD bits in Block Ack Bitmap field is defined to provide the low latency need
Strawpoll

## Slide 8
[1] 24-389r0, Preemption for Low Latency, Mohamed Abouelseoud
[2] 24-168r0, TXOP Preemption in 11bn, Kiseon Ryu
References