## Slide 1: IFCS Discussion
Date: March 10th, 2025
Authors:
Name | Affiliation | Address | Phone | Email
Avner Epstein | MaxLinear |  |  | aepstein@maxlinear.com
Ido Shemer |  |  |  | ishemer@maxlinear.com
Elad Ben Yosef |  |  |  | ebenyosef@maxlinear.com
Oren Kedem |  |  |  | okedem@maxlinear.com
Sigurd Schelstraete |  |  |  | sschelstraete@maxlinear.com

## Slide 2: Introduction
  UHR Trigger Frame Format added iFCS to enable frame validation up to but excluding the padding field.
  The motivation for iFCS is to enable a STA that uses the Trigger Frame as a trigger for switching functionality (e.g. an EMLSR Non-AP STA that needs to switch to its main radio) to validate the Trigger Frame before the beginning of the padding field; otherwise, the padding field does not fulfil its purpose, or the STA is performing the switch without being able to validate the Trigger Frame.

## Slide 3: Problem Description
  In order to maintain backwards compatibility with Non-AP HE STAs it is required to keep the format of user-info and not to exceed the 5 octets allocated for user-info.
  Therefore, according to SFD, the iFCS field is split into two parts in two consecutive user-info fields:
  Splitting the iFCS into two sub-fields adds non-negligible complexity on the CRC calculation hardware (in both transmit and receive paths).

## Slide 4: Solution – Option A
  Since the Trigger Frame is intended for UHR STAs, they are able to identify the format of the iFCS field, hence it may be increased to 6 octets, thus allowing the iFCS to be contiguous.
    Note: the user-info with AID12=2011 (for the iFCS) should be the last user-info before that with AID12=4095 (for the padding).
  Backwards compatibility:
    When HE STAs are addressed via Trigger Frame using the HE Variant (first row in the table) there is no backwards compatibility issue.
    EHT & UHR STAs are not mixed together in the same Trigger Frame, and the EHT STAs are able to identify this is not an EHT Variant based on the Phy Version field in the Special User Info.
    The only limitation is with the mixed UHR-HE variant (last two rows in the table) – in this case an HE STA may be fooled to find its AID in the IFCS3 field; however, mixed UHR-HE variant is currently not part of 11bn SFD (relies on A-PPDU which is currently out-of-scope).

## Slide 5: Solution – Option B
  According to 11be, the Padding field, if present, is at least two octets in length and is set to all 1s. If the Padding field is present in a Trigger frame, its length is computed as described in 26.5.2.2.3 (Padding for a triggering frame) and 35.5.2.2.3 (Padding for a Trigger frame).
  The padding field is identified by AID12=4095 as part of the first two octets that are all 1s.
  The iFCS field could be defined to overlap the padding (after the first two octets); hence only the first two octets shall be all 1s (and not the entire padding field).
  The risk for backwards compatibility issues is low, since STAs that require padding use this time for processing and/or switching time (e.g. EMLSR) and do not (cannot) verify that the remaining bits in the padding field are all 1s.
  If an AP calculates the required padding length as N octets it should increase the padding field by 4 octets to account for the iFCS and the total field length should be at least 6 octets (rather than 2, as it is now).

## Slide 6: Solution – Option C
  Still use CRC32, but only provide the highest 28bits (omit the lower nibble of the FCS).
  This option has no backwards compatibility issues
  Since the Trigger Frame is significantly shorter than a QoS data frame, then we argue that 28bits are sufficient, as shown in the next slide.
  Alternatively, we may use only the highest 3 octets of the FCS (effectively CRC24), while relying on a constant value in the first two octets of the user-info (AID12=2011 and four bits of 1) for increased robustness.
  Note, the CRC calculation shall remain CRC32, but the lowest 4 bits shall be omitted.

## Slide 7: Solution – Option C (continue)
N_users | Trigger Frame size | Miss-Detect Probability with CRC28 | QoS data frame size with equivalent miss-detect probability using CRC32
8 | 552 bit | 2.06e-6 | 1104 Bytes
16 | 872 bit | 3.25e-6 | 1744 Bytes
32 | 1512 bit | 5.63e-6 | 3024 Bytes
  BSRP Trigger Frame:
    Header = 16 Bytes
    Common-Info = 8 Bytes
    Special User-Info = 5 Bytes
    User-Info = 5 Bytes
    Total = 16+8+5+N_users*5
  Miss detect probability:
    The probability of a single bit undetected error: Pk= ~2^(-k), where k is the CRC size.
    The probability of miss-detect of at least 1 bit in an n-bit frame is: 1-(1-Pk)^n

## Slide 8: Conclusions
  The proposed format of iFCS field in UHR Variant of the Trigger Frame adds non-negligible complexity on the CRC calculation hardware (also in receive path).
  Three solutions have been proposed for working around this problem:
    Solution A – may have backwards compatibility issues with HE STAs; however mixed Trigger Frame is relying on the definition of A-PPDU, which is currently not present neither in 11be nor in 11bn
    Solution B – Low risk for backwards compatibility issues (STAs do not verify that remaining bits in the padding field are all 1s).
    Solution C – no backwards compatibility concern. The simplest solution, relying on the fact that a Trigger Frame is much shorter than data frame and usually transmitted with lower MCS.
  Note, similar considerations might apply also to the MIC field in protected Trigger Frame

## Slide 9: SP1
  Do you agree to change the format of the iFCS field in UHR Variant of the Trigger Frame via Option A?
  Yes / No / Abstain

## Slide 10: SP2
  Do you agree to change the format of the iFCS field in UHR Variant of the Trigger Frame via Option B?
  Yes / No / Abstain

## Slide 11: SP3
  Do you agree to change the format of the iFCS field in UHR Variant of the Trigger Frame via Option C?
  Yes / No / Abstain

## Slide 12: References