## Slide 1: Discussion on NPCA switch back
Date: 2025-03-26
Authors:
Name | Affiliations | Address | Phone | email
Chaoming Luo | OPPO |  |  | luochaoming@oppo.com
Liuming Lu | OPPO |  |  | 
Ning Gao | OPPO |  |  | 
Yapu Li | OPPO |  |  | 
Liangxiao Xin | OPPO |  |  | 

## Slide 2: Abstract
Proposes a mechanism to resolve CID 1783.
CID | Clause | Comment
1780 | 37.10 | The NPCA duration time is limited, STA is better to switch back to BSS P-channel early, instead of continue contending the NPCA P-channel incase the NPCA P-channel is busy

## Slide 3: Discussion
The time a STA/AP stays on the NPCA primary channel is limited. Ideally, the STA/AP needs to switch back to BSS primary channel before basic NAV expires.
  If there are STAs (e.g., legacy STAs) do not switch to NPCA primary channel, it’s more fair for an AP to switch back as early as possible considering about possible OBSS TXOP truncation.
  If a STA/AP switches back late more than 72 us, the STA/AP loses the medium synchronization on the BSS primary channel. [2]
Then, what if the STA/AP does not gain channel access on the NPCA primary channel?
  Should it keeps retrying? There may be no enough time left to finish even a single MSDU transmission after it gain the channel access.
  Should it switch back to BSS primary channel immediately? When the basic NAV is long, there is possibility that it can retry and obtain a TXOP to finish data transmission.
  So, we need a balance!

## Slide 4: Proposal
A simple solution: if the time left is less than a NPCA Transmission Threshold, the STA/AP switches back; otherwise, the STA/AP may keep retrying.
The NPCA Transmission Threshold is a minimum time required to finish at least a single MSDU transmission on the NPCA primary channel:
  At least one EDCA backoff, consumes a minimum of PIFS, i.e., 25 us.
  At least one ICF + SIFS + ICR + SIFS sequence, consumes a minimum around 232 us.
    Assume ICF takes around 128 us (using non-HT PPDU or non-HT duplicate PPDU format using a rate of 6 Mb/s, 12 Mb/s, or 24 Mb/s), ICR takes around 72 us.
  At least one Data + SIFS + Ack/BA sequence, consumes a minimum around 160 us.
    Assume Data takes no less than 72 us, ICR takes around 72 us.
  At least a NPCA Switch Back Delay of the AP
The NPCA Transmission Threshold is greater than or equal to the NPCA Switch Back Delay of the AP plus 417 us.
  We may use an arbitrary value to replace the NPCA Switch Back Delay of the AP, e.g., 252 us.
  The exact numbers could be discussed further.

## Slide 5: Straw Poll
Do you support to add the following into the latest TGbn draft ?
  A NPCA Transmission Threshold field is added into the NPCA Operation Information field.
  The NPCA Transmission Threshold is a minimum time required to finish at least a single MSDU transmission on the NPCA primary channel.
  The NPCA Transmission Threshold is greater than or equal to the NPCA Switch Back Delay of the AP plus 417 us.

## Slide 6: References
[1] Draft P802.11bn_D0.1
[2] 11-24-0496-01-00bn-secondary-channel-usage-follow-up
[3] 11-24-0070-02-00bn-some-details-about-non-primary-channel-access
[4] 11-23-1891-00-00bn-nonprimary-channel-access-follow-up