## Slide 1: NPCA Announcement
Date: 2025-03-26
Authors:
Name | Affiliations | Address | Phone | email
Chaoming Luo | OPPO |  |  | luochaoming@oppo.com
Liuming Lu | OPPO |  |  | 
Ning Gao | OPPO |  |  | 
Yapu Li | OPPO |  |  | 
Liangxiao Xin | OPPO |  |  | 

## Slide 2: Abstract
Proposes a mechanism to resolve CID 1773.
CID | Clause | Comment
1773 | 37.10 | In order to solve different view problem when observing OBSS transmission in NPCA procedure, the AP observing the OBSS transmission would be better to send a short signal during the SIFS to inform STAs in the BSS to switch to NPCA P-channel.

## Slide 3: Proposal
As proposed in the comment, when AP1 detects AP2’s transmission of a control frame exchange on the BSS primary channel, AP1 may send a short signal during the SIFS to announce NPCA switch
Non-AP STAs associated with AP1 may switch to NPCA primary channel upon the receipt of this short signal.

## Slide 4: Design of The Short Signal
Option 1: The short signal may be a 2x LTF symbol (6.4 us) with 1.6 us GI which takes 8 us
  It should be more than or equal to 4 us considering minimum receiver detecting time. [1]
  It should be less than a SIFS (e.g., 16 us) to minimize the impact to the ongoing OBSS transmission
    As stated in baseline clause 10.3.2.11: If an RTS/CTS exchange is used, the PPDU containing an individually addressed Data or Management frame shall be transmitted starting one SIFS after the end of the CTS frame. No regard is given to the busy or idle status of the medium when transmitting this PSDU.
  The transmission of the short signal obeys the regulatory. ([2], Short Control Signalling Transmissions)
  The short signal may be transmitted on a dedicated RU
    AP1 and AP2 use different RUs to identify themselves to their associated STAs.
    AP1 and AP2 can negotiate the RUs to avoid conflict.
  Further random phase rotation could be applied to the LTF symbol
    Alternate way to reduce conflict between APs
    To mitigate the possible replay attack.
Option 2: The short signal may be a orthogonal code division multiplexing (CDM) sequence, e.g., Zadoff-Chu sequence. Detail design TBD

## Slide 5: Summary
The method can alleviate the different view problem of NPCA procedure.
Detail design can be further discussed.

## Slide 6: Straw Poll
Do you support to include the following text into the 11bn SFD?
  An NPCA AP may send a short signal during the SIFS after the OBSS control frame exchange on the BSS primary channel to announce its switching to NPCA primary channel?
    Detailed design of the short signal is TBD

## Slide 7: References
[1] 11-24-0284-02-00bn-low-latency-low-collision-low-power-uhr-medium-access
[2] EN 301 893v2.1.1