## Slide 1: Cross Link Indication for NPCA
Date: 2025-03-26
Authors:
Name | Affiliations | Address | Phone | email
Chaoming Luo | OPPO |  |  | luochaoming@oppo.com
Liuming Lu | OPPO |  |  | 
Ning Gao | OPPO |  |  | 
Yapu Li | OPPO |  |  | 
Liangxiao Xin | OPPO |  |  | 

## Slide 2: Abstract
Proposes a mechanism to resolve CID 1781 and 1782.
CID | Clause | Comment
1781 | 37.10 | To mitigate the different view problem, when an affiliated AP of link 1 switches to NPCA P-channel, the affiliated AP of link 2 which obtains an TXOP can inform the non-AP MLDs to switch to NPCA P-channel of link 1.
1782 | 37.10 | To mitigate the medium sync loss problem, when an affiliated AP of link 1 switches to BSS P-channel from NPCA P-channel, the affiliated AP of link 2 which obtains an TXOP can solicit the non-AP MLDs to report NAV of link 1.

## Slide 3: Proposal 1
When AP1 switches to NPCA P-channel, AP2 which holds an TXOP may notify the non-AP MLDs that have affiliated STAs on link 1 (e.g., STA1, STA3, STA5) to switch to NPCA P-channel.
It is an opportunistic optimization. It works only if AP2 just holds an TXOP when AP1 switches to NPCA P-channel.

## Slide 4: Proposal 2
Before AP1 switches back to BSS P-channel from NPCA P-channel, AP2 which holds an TXOP may solicit NAV information of link 1 from the non-AP MLDs that have affiliated STAs staying on the BSS P-channel (e.g., STA5 does not do NPCA operation), so AP1 could restore the medium busy/idle status quickly.

## Slide 5: Summary
The proposed methods can alleviate the different view problem and medium sync loss problem of NPCA procedure.
Detail design can be further discussed.

## Slide 6: Straw Poll 1
Do you support to include the following text into the 11bn SFD?
  When an AP affiliated with an AP MLD operating on link 1 switches to NPCA primary channel, another affiliated AP of the AP MLD which holds an TXOP may notify the associated non-AP MLDs that have affiliated STAs operating on link 1 to switch to NPCA primary channel.
    Detailed design is TBD

## Slide 7: Straw Poll 2
Do you support to include the following text into the 11bn SFD?
  Before an AP affiliated with an AP MLD operating on link 1 switches back to BSS primary channel from NPCA primary channel, another affiliated AP of the AP MLD which holds an TXOP may solicit NAV information of link 1 from the associated non-AP MLDs that have affiliated STAs operating on link 1 staying on the BSS primary channel.
    Detailed design is TBD

## Slide 8: References
[1] Draft P802.11bn_D0.1