## Slide 1: Early reception termination when I-FCS is present in a Trigger frame
Date: 2024-12-11
Authors:

## Slide 2: Abstract
This document discusses the use of intermediate FCS in trigger frames for early termination of the frame reception.

## Slide 3: Introduction
Group has agreed to carry an intermediate FCS field in a trigger frame when one or more recipient UHR STA(s) operating in DSO, EMLSR or DPS modes require it.
The I-FCS can be located in dedicated User Info field(s) of the Trigger frame.
In this presentation, we discuss the option for early termination of reception of the trigger frame at a receiver when I-FCS is present.
Ctrl frame | Duration | RA | TA | Common Info | User Info of group1 | I-FCS | User Info of group2 | padding | FCS
Effective padding time for group 1

## Slide 4: Early termination of reception
When an I-FCS field is present within a Trigger frame, non-AP UHR (or beyond) STAs may use the I-FCS value to early terminate the decoding process of the frame.
  STAs expected to receive the frame may terminate reception if I-FCS CRC check fails.
  STAs not expected to receive frame, e.g., OBSS STA, may terminate reception after I-FCS CRC check.
  When I-FCS CRC check passes, a receiving STA gets valid NAV information.
This has multiple benefits:
  It can save power at the receiving STAs (both intended and unintended recipient STAs).
    All STAs save power by terminating reception when I-FCS check fails.
    OBSS STAs can save power by going to doze for TXOP duration when I-FCS check passes.
  It increases chance of successful frame reception at unintended recipient, since the frame segment before I-FCS is of a smaller length.
  It increases the opportunity for NPCA operation in an overlapping BSS.
The benefit of early termination is more if the I-FCS can be carried early within the trigger frame.
Frame Control | Duration | RA | TA | Common Info | User Info List | Padding | FCS
Special User Info | Some User Info fields | I-FCS | Some User Info fields
Some STAs may perform early receive termination

## Slide 5: Conclusions
An I-FCS when present in a trigger frame can be used by a receiving STA for early termination of frame reception process. This can:
  Reduce power consumption.
  Increase chance of successful reception of the frame.
  Increase opportunity for NPCA, etc.
Correspondingly, even if I-FCS is not needed by any recipient STA, there is benefit in including it within the trigger frame.
The benefit is higher if I-FCS is present early within the trigger frame.

## Slide 6: Strawpoll
SP1: Do you support to allow a UHR STA to set the NAV from a received trigger frame based on a successful CRC check on the intermediate FCS, if present, within the frame.
  Yes
  No
  Abstain
Note1: Whether the mechanism is applicable to all trigger frames is TBD.
Note2:Other necessary conditions for NAV update may still be applicable.

## Slide 7: Strawpoll
SP2: Do you support to allow a UHR non-AP STA to perform early termination of the reception of a trigger frame, based on failure of the CRC check on the intermediate FCS, if present, within the frame.
  Yes
  No
  Abstain

## Slide 8: References
11-23-1873-01-00bn-post-fcs-mac-padding
11-23-2003-01-00bn-client-power-save
11-24-0544-01-00bn-power-save-protocols-for-uhr-follow-up
11-24-1227-01-00bn-some-usage-of-intermediate-fcs
11-24-1129-01-00bn-discussion-on-intermediate-fcs-signaling

## Slide 9: Backup slides