## Slide 1: NFRP mechanism for NPCA
Date: 2025-04-17
Authors:
Name | Affiliation | Address | Phone | Email
Junbin Chen | TP-Link Systems Inc. |  |  | chenjunbin@tp-link.com.hk
Yunpeng Yang |  |  |  | yangyunpeng@tp-link.com.hk
Renfang Zhou |  |  |  | zhourenfang@tp-link.com.hk
Yaoshen Cui |  |  |  | cuiyaoshen@tp-link.com.hk
Haozheng Li |  |  |  | lihaozheng@tp-link.com.hk
Qingwei Fu |  |  |  | fuqingwei@tp-link.com.hk
Shuyu Shi |  |  |  | shishuyu@tp-link.com.hk
Yu Zhu |  |  |  | zhuyu@tp-link.com.hk

## Slide 2: Abstract
Currently, we have define that the NPCA STA may switch to the NPCA primary channel when the primary channel is occupied by OBSS transmissions [1-2]:
However, the hidden node may lead to mismatch problem of the parking channel between AP and STAs [3-4].
      The AP hears OBSS PPDU and switch to NPCH, but STA stays on the PCH; and vice versa.
  Besides, many previous contributions [4-6] suggest to disable the untriggered UL transmission in NPCH.
      Thus, we shall define a mechanism for non-AP STAs to report their buffer status of UL low-latency traffic.
In this presentation, we’d like to mitigate the problems mentioned above by extending the NFRP mechanism for NPCA.

## Slide 3: Recap: hidden node issues in NPCA
A general solution:
The AP send an ICF soliciting ICR in order to query for the channel status of STAs.
The non-AP STA reports that it stays on PCH or it has switched to NPCH.
PCH
NPCH
ICF
ICF
ICF
ICF
ICR(STA1/3)
ICR(STA1/3)
OBSS
for STA1
PCH
NPCH
ICF
ICF
ICR(STA1/3)
ICR(STA1/3)
OBSS for AP
AP
STA1
OBSS AP
STA2
AP
STA3
OBSS AP
STA2
P40
P40
S40
S40
STA2 stays on PCH and do not respond ICR
ICR(STA2/3)
ICR(STA2/3)
STA1
Case 1
OBSS activity is hidden to AP
STA3
Bandwidth assumption:
STA1: 80MHz or 40MHz
STA2: 40MHz
STA3: 80MHz
All STAs are NPCA STAs
Case 2
OBSS activity is hidden to non-AP STA

## Slide 4: Why not to reuse the (MU-)RTS/CTS as the ICF/ICR?
Frame control
duration
RA
FCS
Frame control
duration
RA
FCS
Frame control
duration
RA
FCS
Frame control
duration
RA
FCS
Frame control
duration
RA
FCS
Frame control
duration
RA
FCS
Frame control
duration
RA
FCS
The RTS/CTS works only for SU in the aforementioned scenarios.
To query for the channel status of multi-user:
  The AP shall transmit an MU-RTS, which contains multiple user info field, causing overhead.
  The indicated STAs respond the MU-RTS with CTS in 20MHz non-HT DUP PPDU.
  Most importantly, the CTS frame only contains RA but not TA.
    Therefore, the AP can not distinguish the sender of CTS.
MU-RTS(20MHz non-HT DUP)
CTS(20MHz non-HT DUP)
20M STA
40M STA
80M STA
Mac header
Common info
user info
user info
user info
…
padding
FCS
Mac header
Common info
user info
user info
user info
…
padding
FCS
Mac header
Common info
user info
user info
user info
…
padding
FCS
Mac header
Common info
user info
user info
user info
…
padding
FCS

## Slide 5: Why not to reuse the BQRP?
In 11ax, the BQR is used to report the availability of each 20MHz subchannel.
Advantages:
  The non-AP STAs can report the detailed availability of each 20MHz subchannel.
Disadvantages:
  As an ICF, the BQRP contains multiple user info field, which brings further overhead.
  As an ICR, the BQR report shall be transmitted through different RUs as indicated in the BQRP frame from AP.
  However, the AP is trying to query the channel status so as it can make a proper RU assignment.
Frame control
duration
RA
FCS
HT Control
Frame body
…
BQRP
BQR in HT control
STA 1
STA 2
STA 3
Mac header
Common info
user info
user info
user info
…
padding
FCS
Mac header
Common info
user info
user info
user info
…
padding
FCS
Mac header
Common info
user info
user info
user info
…
padding
FCS
Mac header
Common info
user info
user info
user info
…
padding
FCS
Frame control
duration
RA
FCS
HT Control
Frame body
…
Frame control
duration
RA
FCS
HT Control
Frame body
…
Frame control
duration
RA
FCS
HT Control
Frame body
…
STA 4

## Slide 6: Recap: NFRP and NDP feedback report
The NFRP allows AP to trigger multiple STA for a short feedback.
There is only one user info field in NFRP indicating multiple STAs.
  Query up to 72 users in one NFRP with 80MHz bandwidth (in absence of UL mu-mimo).
Phy header
Mac header
Common info
user info
PE
NFRP(20MHz non-HT DUP)
L-STF/L-LTF/L-SIG/RL-SIG
HE-SIG-A
HE-LTF
PE
NDP(HE TB PPDU)
L-STF/L-LTF/L-SIG/RL-SIG
HE-SIG-A
HE-LTF
PE
L-STF/L-LTF/L-SIG/RL-SIG
HE-SIG-A
HE-LTF
PE
L-STF/L-LTF/L-SIG/RL-SIG
HE-SIG-A
HE-LTF
PE
Phy header
L-STF/L-LTF/L-SIG/RL-SIG
HE-SIG-A
HE-LTF
PE
L-STF/L-LTF/L-SIG/RL-SIG
HE-SIG-A
HE-LTF
PE
L-STF/L-LTF/L-SIG/RL-SIG
HE-SIG-A
HE-LTF
PE
L-STF/L-LTF/L-SIG/RL-SIG
HE-SIG-A
HE-LTF
PE
L-STF/L-LTF/L-SIG/RL-SIG
HE-SIG-A
HE-LTF
PE
L-STF/L-LTF/L-SIG/RL-SIG
HE-SIG-A
HE-LTF
PE
L-STF/L-LTF/L-SIG/RL-SIG
HE-SIG-A
HE-LTF
PE
L-STF/L-LTF/L-SIG/RL-SIG
HE-SIG-A
HE-LTF
PE
Phy header
Mac header
Common info
user info
PE
Phy header
Mac header
Common info
user info
PE
Phy header
Mac header
Common info
user info
PE
STA 1~18
STA 19~36
STA 37~54
STA 55~72
The polled AID range:
where

## Slide 7: Proposal: Reuse NFRP/NDP for channel status query
We suggest that the NPCH shall be set in the S40/S80/S160.
  Such NPCH selection leads to a low probability of being occupied by OBSS TXOPs occupying the primary channel.
We suggest to reuse the NFRP/NDP to query for the parking channel status of NPCA STAs.
  We need to define a new feedback type for channel status report.
  The RU_TONE_SET_INDEX needs to be redesigned.
    In the baseline, the subcarriers of 80MHz bandwidth are divided into 72 RU_TONE_SET.
    In the proposal, the subcarriers in RU_TONE_SET 37~72 are merged into the RU_TONE_SET 1~36, respectively.
RU_TONE_ SET_INDEX 1~18
RU_TONE_ SET_INDEX 19~36
RU_TONE_ SET_INDEX 37~54
RU_TONE_ SET_INDEX 55~72
RU_TONE_ SET_INDEX 1~18
RU_TONE_ SET_INDEX 19~36
RU_TONE_ SET_INDEX 1~18
RU_TONE_ SET_INDEX 19~36
baseline
proposal
frequency

## Slide 8: The transmission of NDP feedback report
The non-AP STA determines to transmit NDP as follows:
The assigned RU_TONE_SET contains 24 subcarriers, which can be divided into 4 groups:
  1st and 2nd group located in P40, 3rd and 4th group located in S40.
The NDP feedback report
  shall be transmitted through the 1st and 2nd group if the non-AP STA stays on the PCH;
  shall be transmitted through the 3rd and 4th group if the non-AP STA has switched to the NPCH
  shall be transmitted through all the 1st/2nd/3rd/4th group if the non-AP STA determines that both PCH and NPCH are idle.
Further, the non-AP STA determines whether it has pending low-latency UL traffic:
  If yes, the HE-LTF field shall be non-zero in 1st and/or 3rd group, and shall be all zero in 2nd and/or 4th group.
  If no, the HE-LTF field shall be all zero in 1st and/or 3rd group, and shall be non-zero in 2nd and/or 4th group.
P20 (user 1~18)
S20 (user 19~36)
S40_L20 (user 1~18)
S40_H20 (user 19~36)
frequency
P40
S40
RU_TONE_SET_INDEX a:
RU_TONE_SET_INDEX c:
RU_TONE_SET_INDEX b:
RU_TONE_SET_INDEX d:
1st 2nd 3rd 4th

## Slide 9: Example of detection algorithm in AP side
In AP side, the feedback can be determined based on the power detection [8].
The power detection is performed on P40 and S40 respectively.
  P1 = sum(power in 1st group subcarriers);
  P2 = sum(power in 2st group subcarriers);
  P3 = sum(power in 3rd group subcarriers);
  P4 = sum(power in 4th group subcarriers);
 | PCH_LL | PCH_NL | PCH_No_Response
NPCH_LL | PCH: idle; NPCH: idle; Pending LL data: Yes | Unreliable feedback | PCH: busy; NPCH: idle; Pending LL data: Yes
NPCH_NL | Unreliable feedback | PCH: idle; NPCH: idle; Pending LL data: No | PCH: busy; NPCH: idle; Pending LL data: No
NPCH_No_Response | PCH: idle; NPCH: busy; Pending LL data: Yes | PCH: idle; NPCH: busy; Pending LL data: No | PCH: busy; NPCH: busy;
P1 > K*P2  PCH_LL
P2 > K*P1  PCH_NL
Not(P1 > K*P2) & Not(P2 > K*P1)  PCH_No_Response
P3 > K*P4  NPCH_LL
P4 > K*P3  NPCH_NL
Not(P3 > K*P4) & Not(P4 > K*P3)  NPCH_No_Response

## Slide 10: Summary
In this presentation, we propose to extend the existing NFRP/NDP mechanism for NPCA.
  The NDP feedback can be reused to query for the parking channel of non-AP STAs.
  Also, the proposed NDP feedback report indicates whether the non-AP STAs are requesting for UL transmission for its buffered low-latency traffic.

## Slide 11: References
[1] 24/0209-bn Specification Framework for TGbn, Ross Jian Yu (Huawei)
[2] Draft P802.11bn D0.2
[2] 24/0670-bn Different view problems of NPCA, Sanghyun Kim (WILUS)
[3] 24/1125-bn Considerations on switching for NPCA, Dongju Cha (LG Electronics)
[4] 24/1218-bn NPCA - next level discussions, Gaurang Naik (Qualcomm)
[5] 24/1093-bn Special scenarios in Non-Primary Channel Access, Sindhu Verma (Broadcom)
[6] 24/1155-bn Further discussions on NPCA, Sanghyun Kim (WILUS)
[7] 24/1885-bn NPCA Hidden Node Problem, Gwangho Lee, (KNUT)
[8] 17/0044-ax NDP Short Feedback Design, Leo Montreuil (Broadcom)