## Slide 1: Thoughts on Ack Policy in MAP Co-transmission
Date: 2025-4-02
Authors:

## Slide 2: Introduction
802.11bn™/D0.2 have defined Multi-AP coordinated concurrent transmission by coordinated beamforming (Co-BF) and coordinated spatial reuse (Co-SR) mechanisms[1]:
The UHR Co-BF and Co-SR DL transmission have been discussed intensively; however, the acknowledgment procedures remain a open question
In this contribution, we discuss the acknowledgment (Ack) issues in the Co-BF/Co-SR transmission

## Slide 3: Issue on UHR Co-SR Ack
Both DL MU PPDU solicit immediate acknowledgments
  The recipients in different BSS shall respond to associated APs with Ack frame at same time without power control, resulting in RX collisions in AP side.
STA-22
STA-11
AP-1
AP-2
BSS-1
BSS-2
OBSS
BA
Co-SR transmission phase
AP-1
AP-2
Co-SR Trigger
STA-11
BA
DL PPDU-2
BA
STA-22
DL PPDU-1
With Power Control
BA interference
SIFS
SIFS
Without Power Control

## Slide 4: Issue on UHR Co-BF Ack
AP-1
AP-2
Co-BF Invite
STA-11
STA-31
STA-22
STA-42
BA @RU-1
BA @RU-2
BA @RU-1
BA @RU-2
RX Collision
SIFS
Co-BF Response
Co-BF Sync
SIFS
MU PPDU-2
MU PPDU-1
TX(DL)
SIFS
SIFS
Both DL PPDU solicit immediate (implicit) acknowledgments
  These recipients in different BSS may respond Ack frame at same RU, resulting in RX collisions in AP side.
STA-22
STA-11
AP-1
AP-2
BSS-1
BSS-2
OBSS
STA-31
STA-42
Co-BF transmission phase

## Slide 5: Proposal: Ack Policy for MAP Co-transmission Schemes
requesting AP
responding AP
MAP concurrent DL Transmission
Coordinated
Ack
Ack Policy negotiation
Negotiation Req.
Negotiation Resp.
MAPC negotiation
MAPC discovery
Co-transmission phase
In the Multi-AP Coordination (MAPC) negotiation procedure, requesting AP and responding AP negotiate Ack policy for MAP concurrent transmission (Co-BF/Co-SR) to avoid Ack collision or interference.

## Slide 6: MAP Co-transmission Ack Options
  Option 1: Delayed Ack
    Sharing and shared AP solicit explicit delayed acknowledgments
      The Ack Policy set to delayed Ack in all A-MPDU
  Option 2: Sequential Ack
    Sharing and shared AP solicit acknowledgment in a sequence
      Eg, sharing AP trigger shared AP to solicit acknowledgment after receiving Ack
  Option 3: Coordinated Ack
    Sharing and shared AP solicits immediate acknowledgments
      Sharing and shared AP negotiate RU allocation for Ack procedures
      All recipient STAs respond Ack in different RU

## Slide 7: Example: Sequential Ack in Co-BF Transmission
AP-1
AP-2
STA-11
STA-31
STA-22
STA-42
BA
ACK in BSS-1 (OFDMA Ack is optional)
Trig.
MU PPDU-2
MU PPDU-1
SIFS
Ack Policy:
Sequential Ack
BAR
SIFS
SIFS
BAR
SIFS
BA
SIFS
BA
ACK in BSS-2
SIFS
SIFS
BAR
SIFS
BA
BAR
SIFS
  After receiving acknowledgement frame from all receiving STAs, AP-1 send a trigger frame to indicate AP-2 soliciting acknowledgement.
STA-22
STA-11
AP-1
AP-2
BSS-1
BSS-2
OBSS
STA-31
STA-42
Ack Policy Negotiation

## Slide 8: Example: Coordinated Ack in Co-BF Transmission
AP-1
AP-2
STA-11
STA-31
STA-22
STA-42
MU PPDU-2 (Ack @RU-3 @RU-4)
MU PPDU-1 (Ack @RU-1 @RU-2)
Ack Policy:
Coordinated Ack
SIFS
BA @RU-1
BA @RU-2
MU ACK
BA @RU-3
BA @RU-4
Ack Policy Negotiation
STA-11
AP-1
AP-2
BSS-1
BSS-2
OBSS
STA-31
STA-42
The AP-1 and AP-2 negotiate RU allocation to solicit immediate Ack in different RU.
  The AP-1 and AP-2 shall allocate the Ack RU for each receiving STA by including a trigger frame or a frame carrying TRS Control field in each A-MPDU
STA-22

## Slide 9
Summary
In this contribution, we proposed a mechanism to address the Ack issues in UHR MAP concurrent transmission(Co-BF/Co-SR) by negotiating Ack policy:
  Sharing and shared AP solicit delayed Ack
  Sharing and shared AP solicit acknowledgments in a sequence
  Sharing and shared AP solicit immediate acknowledgment in different RU

## Slide 10
Straw Poll 1
Do you agree adding the following text to the SFD:
  Define Ack policy coordination for Multi-AP concurrent transmission (Co-SR/Co-BF )
    The Ack policy coordination is negotiated during the MAPC negotiation procedure
    The details of the Ack policy coordination is TBD

## Slide 11: References
[1] 802.11bn™/D0.2
[2] TGbn Motions List - Part 2