## Slide 1: Transmit and Receive Specifications for New MCS Follow-Up
Date: 2025-04-20
Authors:
Name | Affiliations | Address | Phone | email
Alice Chen | Qualcomm Technologies Inc. |  |  | alicel@qti.qualcomm.com
Lin Yang |  |  |  | 
Daeseok Nam |  |  |  | 
Bin Tian |  |  |  | 

## Slide 2: Introduction
Transmit and receive specification for new MCS in 11bn have been discussed [1-3]
In this presentation, we discuss the following
  For non-ELR new MCS
    Rx minimum sensitivity requirements
    ACR/NACR requirements
  For ELR-MCS
    Tx EVM requirements

## Slide 3: Minimum Sensitivity Proposal for Non-ELR MCSs
It’s natural to have 1dB gap between 2/3 and 3/4 for the same QAM and be consistent across different QAM levels
Table B—Receiver minimum input level sensitivity |  |  |  |  |  | 
Modulation | Rate (R) | Minimum sensitivity (20 MHz PPDU) (dBm) | Minimum sensitivity (40 MHz PPDU) (dBm) | Minimum sensitivity (80 MHz PPDU) (dBm) | Minimum sensitivity (160 MHz PPDU) (dBm) | Minimum sensitivity (320 MHz PPDU) (dBm)
BPSK | 1/2 | -82 | -79 | -76 | -73 | -70
QPSK | 1/2 | -79 | -76 | -73 | -70 | -67
QPSK | 2/3 | -78 | -75 | -72 | -69 | -66
QPSK | 3/4 | -77 | -74 | -71 | -68 | -65
16-QAM | 1/2 | -74 | -71 | -68 | -65 | -62
16-QAM | 2/3 | -71 | -68 | -65 | -62 | -59
16-QAM | 3/4 | -70 | -67 | -64 | -61 | -58
16-QAM | 5/6 | -69 | -66 | -63 | -60 | -57
64-QAM | 2/3 | -66 | -63 | -60 | -57 | -54
64-QAM | 3/4 | -65 | -62 | -59 | -56 | -53
64-QAM | 5/6 | -64 | -61 | -58 | -55 | -52
256-QAM | 2/3 | -60 | -57 | -54 | -51 | -48
256-QAM | 3/4 | -59 | -56 | -53 | -50 | -47
256-QAM | 5/6 | -57 | -54 | -51 | -48 | -45
… | … | … | … | … | … | …

## Slide 4: ACR/NACR Proposal for Non-ELR MCSs
Use same performance trend in the sensitivities
Table C—Minimum required adjacent and nonadjacent channel rejection levels |  |  | 
Modulation | Rate (R) | Adjacent channel rejection (dB) | Nonadjacent channel rejection (dB)
 |  | 20/40/80/160/320 MHz channel | 20/40/80/160/320 MHz channel
BPSK | 1/2 | 16 | 32
QPSK | 1/2 | 13 | 29
QPSK | 2/3 | 12 | 28
QPSK | 3/4 | 11 | 27
16-QAM | 1/2 | 8 | 24
16-QAM | 2/3 | 5 | 21
16-QAM | 3/4 | 4 | 20
16-QAM | 5/6 | 3 | 19
64-QAM | 2/3 | 0 | 16
64-QAM | 3/4 | -1 | 15
64-QAM | 5/6 | -2 | 14
256-QAM | 2/3 | -6 | 10
256-QAM | 3/4 | -7 | 9
256-QAM | 5/6 | -9 | 7
… | … | … | …

## Slide 5: Tx EVM Proposal for ELR MCSs
MCS0 has Tx EVM requirement of -5dB in UHR MU PPDU
  EHT-MCS14-15 follows same Tx EVM requirement as MCS0
For ELR-MCS, propose
  Use same Tx EVM requirement as non-ELR MCS0 for ELR-MCS1
  Use a slightly looser Tx EVM requirement for ELR-MCS0
MCS | Modulation | Coding rate | Duplication | Relative constellation error in a UHR ELR PPDU (dB)
ELR-MCS0 | BPSK | 1/2 | 52-tone RU with four times’ duplication | -4
ELR-MCS1 | QPSK | 1/2 | 52-tone RU with four times’ duplication | -5

## Slide 6: Summary
Use the following receive specifications for non-ELR new MCSs
Use -4dB and -5dB Tx EVM requirement for ELR-MCS0 and ELR-MCS1, respectively
Modulation | Rate (R) | Minimum sensitivity (20 MHz PPDU) (dBm) | Minimum sensitivity (40 MHz PPDU) (dBm) | Minimum sensitivity (80 MHz PPDU) (dBm) | Minimum sensitivity (160 MHz PPDU) (dBm) | Minimum sensitivity (320 MHz PPDU) (dBm)
QPSK | 2/3 | -78 | -75 | -72 | -69 | -66
16-QAM | 2/3 | -71 | -68 | -65 | -62 | -59
16-QAM | 5/6 | -69 | -66 | -63 | -60 | -57
256-QAM | 2/3 | -60 | -57 | -54 | -51 | -48
Modulation | Rate (R) | Adjacent channel rejection (dB) | Nonadjacent channel rejection (dB)
 |  | 20/40/80/160/320 MHz channel | 20/40/80/160/320 MHz channel
QPSK | 2/3 | 12 | 28
16-QAM | 2/3 | 5 | 21
16-QAM | 5/6 | 3 | 19
256-QAM | 2/3 | -6 | 10

## Slide 7: Reference
11-25/354r0, Transmit Constellation Error for Additional MCSs, Genadiy Tsodik, et al.
11-25/98r0, UHR Receiver Minimum Input Sensitivity for ELR MCSs, Juan Fang, et al.
11-25/392r0, Transmit and Receive Specifications for New MCS in 11bn, Alice Chen, et al.