## Slide 1: Information Exchange in the CoBF Transmission Phase Follow-Up
Date: 2025-05-07
Authors:
Name | Affiliations | Address | Phone | email
Alice Chen | Qualcomm Technologies Inc. |  |  | alicel@qti.qualcomm.com
Sameer Vermani |  |  |  | svverman@qti.qualcomm.com
Bin Tian |  |  |  | btian@qti.qualcomm.com
Youhan Kim |  |  |  | youhank@qti.qualcomm.com
Ahmed Elsherif |  |  |  | 

## Slide 2: Introduction
Information exchange between two APs through the following three frames to negotiate parameters and form the common preamble in CoBF transmission was discussed in [1-4]
  CoBF Invite/Sync: sent from the sharing AP to the shared AP
  CoBF Response: sent from the shared AP to the sharing AP
Consensus was reached to include certain contents in these three frames in March
In this presentation, we discuss further details in the information exchange, with the focus on PHY information

## Slide 3: Recap: Contents of Invite/Response/Sync Frames
Invite frame (Motion #327)
Response frame (Motion #328)
Category | 
Control | ‘CoBF Invite’
PHY Common Info | Minimum Number of Data OFDM Symbols
 | Maximum Number of Data OFDM Symbols
 | PHY Version Identifier
 | Bandwidth
 | Punctured Channel Information
 | GI+LTF Size
 | Maximum Total Nss Allowed for shared AP
 | Number of CoBF Users in sharing BSS
Per-User Info in Sharing BSS | STA ID
 | Nss
Category | 
Control | ‘CoBF Acceptance’
PHY Common Info | Suggested Number of Data OFDM Symbols
 | PHY Version Identifier
 | Extra LTF Allowed
 | Number of CoBF Users in shared BSS
Per-User Info in Shared BSS | STA ID
 | MCS
 | Nss
 | 2xLDPC
Sync frame (Motion #311)
Category | 
Control | ‘CoBF Sync’
PHY Common Info | Length
 | PHY Version Identifier
 | Bandwidth
 | Punctured Channel Information
 | BSS Color 1, BSS Color 2
 | TXOP
 | Number of UHR-SIG Symbols
 | GI+LTF Size
 | Number Of UHR-LTF Symbols
 | Number of CoBF Users
Per-User Info in Both BSS | STA ID
 | BSS Color Indication
 | MCS
 | Spatial Configuration
 | 2xLDPC

## Slide 4: Frequency Resource Discussion
Bandwidth and Punctured Channel Information is dictated by the sharing AP and indicated in both the Invite frame and Sync frame
This should be compliant with the static puncturing patterns of the two APs
Suggest that
  When the static puncturing patterns of the two APs are the same, the puncturing information in the invite and sync frames corresponds to that
  If the static puncturing patterns of the two APs are not the same, the sharing AP will need to reduce to a smaller BW in which the two APs have the same puncturing pattern, and the information in the invite and sync frames will correspond to that reduced BW configuration

## Slide 5: GI+LTF Size
The Co-BF PPDU’s GI+LTF support and signaling is as follows:
  Support of following GI+LTF combinations to be mandatory at both AP and STA
    2x LTF +0.8us, 2xLTF+1.6us, 4xLTF+3.2us
  Additionally, 2x LTF+0.8us GI usage for a Co-BF pair is exchanged at the group formation stage
    Each AP conveys if it can use 2x+0.8us GI for this Co-BF group or not
    No further last-minute negotiation before Co-BF transmission
  Invite frame from sharing AP dictates the LTF+GI combination keeping the shared AP’s ability to use 2x LTF+0.8us in mind
[Motion #304, [264] and 321]]
GI+LTF Size is dictated by the sharing AP and indicated in both the Invite frame and Sync frame without negotiation
  The information should be consistent in the two frames

## Slide 6: UHR-SIG Related Info
UHR-SIG MCS
  Suggest to fix it to MCS0
Number of UHR-SIG Symbols
  If UHR-SIG MCS is fixed to MCS0, the Number of UHR-SIG Symbols is a simple function of the Number of CoBF Users
  Suggest to use minimum number of UHR-SIG symbols needed to accommodate the UHR-SIG information
    There is no benefit of having extra UHR-SIG symbols with padding
Number of Non-OFDMA Users | Max Number of info bits per content channel in UHR-SIG | Number of UHR-SIG Symbols (with MCS0)
2 | 52 | 2
3 | 85 | 4
4 | 85 | 4

## Slide 7: Other Info with Fixed Values
Spatial Reuse (SR): Suggest to fix it to ‘PSR_AND_NON_SRG_OBSS_PD_PROHIBITED’
Interference Mitigation (IM): Suggest to fix it to ‘Disable’
LDPC Extra Symbol Segment: Suggest to fix it to 1 (for lower puncturing ratio)
PE Disambiguity
  As in [2-3], with a fixed T_PE=20us, the PE Disambiguity becomes a fixed value of 1 according to the following

## Slide 8: Summary
Bandwidth and Punctured Channel Information should have consistent information in the Invite frame and Sync frame
  The information should be compliant with the static puncturing information of the two APs
GI+LTF Size should have consistent information in the Invite frame and Sync frame
For simplicity
  Disable spatial reuse and interference mitigation
  Fix the following (no info exchange): UHR-SIG MCS, LDPC Extra Symbol Segment and PE Disambiguity
  Use the minimum number of UHR-SIG symbols needed to accommodate the UHR-SIG information

## Slide 9: Reference
11-25/389r2, Information Exchange in the CoBF Transmission Phase, Alice Chen, et al.
11-25/399r1, COBF/COSR Design Follow-up, You-Wei Chen, et al.
11-25/401r0, CoBF PHY design consideration, Juan Fang, et al.
11-25/397r3, Spatial Streams Indication for CoBF TF and PPDU, Junghoon Suh, et al.

## Slide 10: SP1
Do you support to use fixed values for the following fields in the CoBF transmission?
  UHR-SIG MCS is fixed to MCS0
  Spatial Reuse is fixed to ‘PSR_AND_NON_SRG_OBSS_PD_PROHIBITED’
  LDPC Extra Symbol Segment is fixed to 1
  PE Disambiguity is fixed to 1
  Interference Mitigation is fixed to ‘Disable’
Supporting doc: 11-25/842r0, 11-25/389r2, 11-25/399r1, 11-25/401r0

## Slide 11: SP2
Do you support that the Bandwidth and Punctured Channel Information indication in the CoBF Invite and Sync frames are the same with the following rules:
  When the static puncturing patterns of the two APs are the same, the puncturing information in the invite and sync frames corresponds to that
  If the static puncturing patterns of the two APs are not the same, the sharing AP will need to reduce to a smaller BW in which the two APs have the same puncturing pattern, and the information in the invite and sync frames will correspond to that reduced BW configuration
  Note: Indication format is TBD

## Slide 12: SP3
Do you support that the indicated GI+LTF Size (for the COBF transmission) in the CoBF Invite and Sync frames is the same?
  GI+LTF size indication format is TBD

## Slide 13: SP4
Do you support that the Number of UHR-SIG Symbols in CoBF transmission is equal to the minimum number of UHR-SIG symbols needed to accommodate the UHR-SIG information?
  No extra UHR-SIG symbols will be allowed

## Slide 14: appendix
Details