## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: TG4a UWB Modulation and PER Simulation Results
Date Submitted: July 15th, 2005
Source: Gian Mario Maggio (STMicroelectronics)
Contact: Gian Mario Maggio
Voice: +41-22-929-6917, E-Mail: maggio@ieee.org
Abstract: TG4a UWB-PHY modulation format and PER simulation results.
Purpose: To provide preliminary simulation results for PER (packet error rate) performance @1 Mb/s, for time-hopping impulse radio system.
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: TG4a: UWB-PHY Simulation Results
List of Contributors:
- Luca Reggiani (Politecnico di Milano, Italy)
- Gian Mario Maggio, Philippe Rouzet (STMicroelectronics)

## Slide 3: UWB Modulation: TH-IR
Ts
Tc
Tf
+1
-1
Time-Hopping (TH) Impulse Radio (IR)
Flexible receiver:
  Non-coherent (PPM)
  Coherent (PPM + BPSK)
  Extension: Diff. coherent (PPM + DBPSK)

## Slide 4: System Parameters (1/3)
UWB signal characteristics:
Channel separation = 494 MHz
Center frequency = 3.952 GHz
Pulse Repetition Frequency (PRF) = 15.4375 MHz
Over-sampling factor @TX = 8
TX sampling frequency = 3.952 GHz
Chip time (Tc) = 2.02 ns
Frame levels (Nf) = 16
Guard time/frame (Tg) = 14Tc = 28 ns
TH sequence length (LPN) = 8
PN sequence (used in simulations) = [1,-2,3,-4,-2,3,-5,1]
Symbol time (Tg + Nf *Tc) * LPN = 484.8 ns
Packet length = 32*8 bits = 256 bits (uncoded)
Rate (R) = 1 Mbit/s (non-coherent RX); 2 Mbit/s (coherent RX)
Notes: Page <number>
        <footer>
<header>
Jul 28, 2026

## Slide 5: System Parameters (2/3)
Pulse shape:
Raised cosine (roll-off=0.25, B=1/Tc*(1+0.25)=617.5 MHz) [pulseTx = wbaSrrcos(0.25,txOS,8)]
Modulation:
  PPM: “0”  offset = 0; “1  offset = 12 Tc = 24 ns
  BPSK: +1/-1
Channel model(s):
  AWGN
  CM1 (a set of 1000 channel realizations generated from the wbaLDRChan.m Matlab function is used in the simulations)
Convolutional code:
R=1/2
Constraint length = 5 (g0 = 23, g1 = 35)
Hard/soft decoding; 16 states; zero termination
Notes: Page <number>
        <footer>
<header>
Jul 28, 2026

## Slide 6: System Parameters (3/3)
Receiver:
Coherent RX: matched filter + S-RAKE (order: 1,5,10)
Non-coherent RX:
  a) filter + energy detection on Tc + S-RAKE
  b) filter + energy detection on k*Tc (starting from the main peak of the received signal), with:
  k = 1 in AWGN simulations
  k = 6 in CM1 simulations
Ideal Channel acquisition + timing estimation
Notes: Page <number>
        <footer>
<header>
Jul 28, 2026

## Slide 7: Simulation Results (1/5)
PER vs. ES/N0 @1Mb/s (coded, soft detection) in AWGN channel:
NOTE: ES = energy/symbol  EB = ES – 3dB for coherent RX because 1 symbol = 2 bits
Notes: Page <number>
        <footer>
<header>
Jul 28, 2026

## Slide 8: Simulation Results (2/5)
PER vs. ES/N0 @1Mb/s (coded, hard detection) in AWGN channel:
Notes: Page <number>
        <footer>
<header>
Jul 28, 2026

## Slide 9: Simulation Results (3/5)
PER vs. ES/N0 @1Mb/s (coded, soft detection) in CM1 (15.4a) channel; 1-finger RAKE (coherent/non-coherent) or non-coherent (with integration time = PPM/2 = 6*TC):
Notes: Page <number>
        <footer>
<header>
Jul 28, 2026

## Slide 10: Simulation Results (4/5)
PER vs. ES/N0 @1Mb/s (coded, hard detection) in CM1 (15.4a) channel; 1-finger RAKE (coherent/non-coherent) or non-coherent (with integration time = PPM/2 = 6*TC):
Notes: Page <number>
        <footer>
<header>
Jul 28, 2026

## Slide 11: Simulation Results (5/5)
PER vs. ES/N0 @1Mb/s (coded, hard detection) in CM1 (15.4a) channel; 5-fingers RAKE (coherent/non-coherent) or non-coherent (with integration time = PPM/2 = 6*TC):
Notes: Page <number>
        <footer>
<header>
Jul 28, 2026