## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [TG3c Coexistence Models Calculation Bases]
Date Submitted: [07 March 2006]
Source: [Hideto Ikeda] Company [Oki Electric Industry Co., Ltd.]
Address [3-4 Hikarino-oka, Yokosuka-city, Japan 239-0847]
Voice:[+81-46-847-5149] E-Mail:[ikeda637@oki.com]
[Kazuaki Takahashi] Company [Matsushita Electric Industrial Co., ltd]
[Yozo Shoji] Organization [National Institute of Information and Communications Technology,
Japan]
Re : [ Excel spreadsheet is attached for convenient use of interference calculation]
Abstract:[Description of TG3c Coexistence Victim Receiver models calculation base for Selection Criteria document ]
Purpose:[Drafting TG3c Selection Criteria document]
Notice :This document has been prepared to assist the IEEE P802.15. It is offered as a basis for
discussion and is not binding on the contributing individual(s) or organization(s). The material in
this document is subject to change in form and content after further study. The contributor(s)
reserve(s) the right to add, amend or withdraw material contained herein.
Release:The contributor acknowledges and accepts that this contribution becomes the property of IEEE
and may be made publicly available by P802.15.

## Slide 2
Calculation Bases of Coexistence Models of Victim Receiver for TG3c Selection Criteria Document 16 November, 2005
*Co-authors are added
*Description no changes from r2
*Excel spreadsheets are attached

## Slide 3
Coexistence models of Victim receiver (1)
ARIB STD-T69 Japan,
Millimeter-wave Video Transmission Equipment
For Specified Low power Radio Station
(Point to Point system)

## Slide 4
Coexistence models of Victim receiver (2)
ARIB STD-T74 Japan,
Millimeter-wave Ultra High Speed Wireless LAN System
For Specified Low power Radio Station
(Point to Multi-Point system)

## Slide 5
Coexistence models of Victim receiver (3)
ARIB STD-T69/ T74
Typical Victim Receiver Link Budget
Note: ・The mating antennas directions are well aligned each other to get maximum gains.
・The normal receiving input level is targeted to be approximately 10 dB above the receiving
sensitivity value.

## Slide 6
Coexistence models of Victim receiver (4)
ARIB STD-T69/T74
Example of Interference Calculation
Note: ・ The directions of the Interferer antenna and the Victim receiver antenna are different and not
matching each other, and 0dBi antenna gain is supposed in above case.
・ SIR shall be compared in overlapping range of bandwidth between Victim receiver and Interferer
transmitter.
・ In above example, the result of the SIR (A1) does not meet the Required SIR (A2) value,
therefore some countermeasure should be studied by TG-3cWPAN device system for coexistence.

## Slide 7
CONCLUSIONS (1-1)
TG-3c Coexistence requirements for ARIB STD-T69
Selection Criteria Document
Section 4.2.3.2.2 ARIB STD-T69
This model is intended to represent an ARIB STD-T69 device. The following table identifies the relevant parameters of the reference system

## Slide 8
CONCLUSIONS (1-2)
TG-3c Coexistence requirements for ARIB STD-T69
Selection Criteria Document
Section 4.2.3.3.2 ARIB STD-T69 Victim
Minimum Criteria: The interference average power generated by the P802.15.3c transmitter and measured in the relevant bandwidth of the victim receiver should be at least 33 dB (A2: Required SIR) below the standard receiving input level (S9) which is 10dB above the minimum sensitivity level (S11) of the STD-T69 device, when the separation between the P802.15.3c transmitter and victim receiver is 1 meter.
The following table shows example of SIR calculations;
Note: ・ The directions of the Interferer antenna and the Victim receiver antenna are different and not
matching each other, and 0dBi antenna gain is supposed in above case.

## Slide 9
CONCLUSIONS (2-1)
TG-3c Coexistence requirements for ARIB STD-T74
Selection Criteria Document
Section 4.2.3.2.3 ARIB STD-T74
This model is intended to represent an ARIB STD-T74 device. The following table identifies the relevant parameters of the reference system

## Slide 10
CONCLUSIONS (2-2)
TG-3c Coexistence requirements for ARIB STD-T74
Selection Criteria Document
Section 4.2.3.3.3 ARIB STD-T74 Victim
Minimum Criteria: The interference average power generated by the P802.15.3c transmitter and measured in the relevant bandwidth of the victim receiver should be at least 24 dB (A2: Required SIR) below the standard receiving input level (S9) which is 10dB above the minimum sensitivity level (S11) of the STD-T74 device, when the separation between the P802.15.3c transmitter and victim receiver is 1 meter.
The following table shows example of SIR calculations;
Note: ・ The directions of the Interferer antenna and the Victim receiver antenna are different and not
matching each other, and 0dBi antenna gain is supposed in above case.