## Slide 1
Project: IEEE P802.15 WG for Wireless Personal Area Networks (WPANs)
Submission Title: [Merged Proposal for FHSS to TG4g]
Date Submitted: [July, 2009]
Source: [Presenter 1: John Buffington] , Company: [Itron]
[Presenter 2: Bob Mason] , Company: [Elster]
[see page 2 for the complete list of company names, authors, and supporters]
Address: [ ]
Voice: [ ] E-Mail: [ ] Re: [ Response to CFP issued January 22nd 2009, document 15-09-077-00-004g ] Abstract: [This document describes the Merged Proposal for FHSS to TG4g] Purpose: [ Proposal for consideration of inclusion into 802.15.4 PHY draft amendment ]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Authors from 9 affiliated companies/organizations
Objective of this work is to create a baseline FHSS system based on the best technical solution to meet the SUN requirements and plan for the future, without bias to existing systems.
This is a MERGED PROPOSAL from the following authors, representing a combination of equipment suppliers and Silicon vendors.
Elster Electricity [09-302]: Bob Mason, Rodney Hemminger
Itron [09-292]: John Buffington, Daniel Popa, Hartman VanWyk
NICT [09-312]: Fumihide Kojima, Hiroshi Harada
Silicon Laboratories [09-278]: Henk de Ruijter, Ping Xiong, Péter Onódy
The FHSS merged proposal is supported by:
Aclara: Kendall Smith, Mark Wilbur
France Télécom / Orange Labs: Jean Schwoerer
Landis+Gyr: Emmanuel Monnerie
Maxim: Rishi Mohindra
TI: Khanh Tuan Le

## Slide 3: Agenda
Requirements
Details about merged proposal
  TX/RX architecture
  Band plan and channelization
  System Parameters
  Frame format: preamble, header, PSDU
Performance results
  Link budget, sensitivity, system performance in multi-path
  Complexity and power consumption
Summary and conclusions

## Slide 4: Requirements
The network must be comprised of robust, scalable network devices capable of today’s data requirements, but also capable of providing extended data capacity and response times for existing and future data requirements and device types. To meet these criteria, in addition to the items outlined in the PAR, the PHY must support the following:
  Data rates to support basic devices (40kbps) but also data rates to meet future needs (e.g. >300 kbps)
  Ubiquitous network support for battery powered (i.e. gas and water) and full function (i.e. electric) devices. Battery powered devices must interoperate with full function devices.
  Minimal infrastructure requirements (in the majority of cases, nothing required except the utility devices)

## Slide 5: Proposal Details More details in 15-09-0491-00-004g

## Slide 6: Outline of Merged Proposal
Frequency Hopping Spread Spectrum
Three data rates*
  Low: 40kbps (mandatory)
  Medium: 160kpbs (optional)
  High: 320kbps (optional)
Operating frequency range
  400MHz (Japan)
  868MHz (Europe)
  902-928MHz (US)
  950MHz (Japan)
  2,400MHz (Worldwide)
  Other bands as available
GFSK modulation*, 200kHz and 400kHz channels
* Data rate and channel width vary slightly in different regions

## Slide 7: TX/ RX architecture
MAC-PDU
Compute
CRC-32
FEC
(optional)
Data whitening/
scrambling
(optional)
Generate
PHR
Preamble
insertion
RF
MOD
Compute
CRC-32
FEC
(optional)
De-scrambling (optional)
Data
Detection
Synch
RF DMOD
FEC
for PHY header
(optional)
FEC
for PHY header
(optional)
“PHY header processing”
“PHY header processing”

## Slide 8: Band plan
Frequency band | Parameter | Low data rate | Medium data rate | High data rate
426.025-469.4875MHz (Japan) | Channel Spacing | 200 kHz | 200 kHz | 200 kHz
 | Number of Channels | 4~5 | 4~5 | 2(+1?)~2(+2?)
863-870MHz (Europe) | Channel Spacing | 100kHz | 500/600kHz (AFA) | 500/600kHz (AFA)
 | Number of Channels | 52 | 5 | 5
902-928MHz (US) | Channel Spacing | 200/400kHz | 400 kHz | 400 kHz
 | Number of Channels | 64/128* | 64 | 64
950.9-955.7MHz (Japan) | Channel Spacing | 200kHz | 200kHz | 200kHz
 | Number of Channels | 24 | 24 | 12 (+11?)
2,400-2,483.5MHz (Worldwide) | Channel Spacing | 200 kHz | 400 kHz | 400 kHz
 | Number of Channels | 200 | 200 | 200
* For systems using only the low data rate, 128 200kHz channels are available. For systems supporting mid and high data rates, all devices use 64 channels with 400 kHz spacing

## Slide 9: System parameters
Frequency band | Parameter | Low data rate | Medium data rate | High data rate
426.025-469.4875MHz (Japan) 950.9-955.7MHz (Japan) | Data rate | 50kbps | 100kbps | 200/ 400kbps
 | Modulation Technique | GFSK | GFSK | GFSK/ 4GFSK
 | Modulation Index | 1.0 (+/- 25 kHz) | 1.0 (+/-50 kHz) | 1.0 (+/- 100 kHz)/ TBD
 | BT | 0.5 | 0.5 | 0.5
863-870MHz (Europe) | Data rate | 40kbps | 100kbps | 200kbps
 | Modulation Technique | GFSK | GFSK | 4GFSK
 | Modulation Index | 0.75 | 0.9 | 0.3
 | BT | 0.5 | 0.5 | 0.5
902-928MHz (US) 2,400-2,483.5MHz (Worldwide) | Data rate | 40kbps | 160kbps | 320kbps
 | Modulation Technique | GFSK | GFSK | 4GFSK
 | Modulation Index | 2.0 (+/- 40 kHz) | 0.75 | 80 kHz freq sep. (-120, -40, +40, +120 kHz)
 | BT | 0.5 | 0.5 | 0.5

## Slide 10: Simplified PPDU
PPDU consists of:
  Preamble: used for synchronization
  Start-of-Frame Delimiter (SFD): indicates end of preamble and start of packet data, indicates change of data rate
  PHY header (PHR): includes information required to decode data packet
  PHY payload (PSDU)
Doesn’t include optional fields

## Slide 11: PPDU Format
Includes optional fields
DRI and SHR2 fields are only present if the SFD indicates a data rate change prior to transmission of the PHY header (PHR1)
Preamble2 field is only present if Preamble2Len is greater than 0
SFD2 field is only present if SFD2 Present is equal to 1
PHR2 field is only present if EXT = 1
Extended Network ID field is only present if Network Id = 1

## Slide 12: System performance

## Slide 13: Link budget

## Slide 14: Complexity

## Slide 15: Power consumption

## Slide 16: Comparison with other FHSS proposals
Merged proposal
Low data rate* mandatory: 40kbps
Medium/ high data rate* optional: 160/320kbps
GFSK
400kHz channel spacing
* Data rate vary slightly in different regions
Other proposals
100kbps
FSK
250kHz channel
300kHz channel spacing
Advantages of merged proposal
Lower adjacent channel emission for local regulations
Worldwide operation
Proven technology for meter reading and FHSS systems
Lower data rate for battery operation
Higher data rate for future applications
Low and high data rate devices interoperable

## Slide 17: GFSK advantages
Lower adjacent channel emission than FSK complying to local regulations
No linear amplifier needed compared to BPSK/OQPSK
Low complexity in the modem serving low cost endpoints
Proven technology for FHSS regulations
Proven technology for Meter reading

## Slide 18: Conclusions
Merged proposal of equipment suppliers and Silicon vendors
Data rates support
  basic devices (40 kbps)
  future needs (160kbps and 320 kbps)
Support for
  battery powered (i.e. gas and water)
  full function devices (i.e. electric)
Minimal infrastructure requirements (in the majority of cases, nothing required except the utility devices)
Worldwide operation
GFSK modulation