## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [802.15.4f ‘BLINK’ Frame Recommendation to TG4e]
Date Submitted: [Date]
Source: [802.15.4f Task Group document, Adrian Jennings, Billy Verso, George Cavage, Tim Harrington principle authors]
[ Mike McInnis – Submitter]
Address [P.O. Box 3707, MC 7M-CA, Seattle, Washington, USA 98124]
E-Mail:[michael.d.mcinnis@boeing.com]
Re: []
Abstract: [IEEE 802.15.4f ‘BLINK’ Frame Recommendation to TG4e]
Purpose: [Work with the 802.15.4e TG on required 802.15.4f MAC enhancements in support of new 802.15.4f TG PHYs]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: ‘BLINK’ Frame Recommendation submitted to TG4e from TG4f
Source: IEEE 802.15.4f TG
Submitter: Mike McInnis 802.15.4f Chair

## Slide 3
TG4f ‘Blink’ Frame Recommendation
Establish a new ‘Blink’ frame type for Active RFID
  Such that when a non-RFID device receives this frame type it immediately discards it (after frame control and before addressing bits)
  No association required, No ACK required
An RFID blink frame may include an IEEE 64 bit source address or omit it.
An RFID blink frame may also omit or include PAN ID.
The proposed addressing mode for the blink frame is supported by;
  Addressing modes in 802.15 may already have a value of 00 (no address).
  Addressing mode 01 which is currently reserved in 802.15.4, is utilized to mean 64 bits without PAN ID.
The blink frame will accommodate any alternate ID in the payload.
Recommend that the new Blink frame be assigned a frame type value of 100, 101, 110 (ie. Non-extended mode).
802.15.4f TG
Slide 3
November 2009