## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Analysis of Preamble Length in Non-Coherent UWB Systems]
Date Submitted: [9 Mar 2010]
Source: [Adrian Jennings] Company [Time Domain]
Address [330 Wynn Drive, Suite 300, Huntsville, AL. 35805. USA]
Voice:[+1 256 759 4708], FAX: [+1 256 922 0387], E-Mail:[adrian.jennings@timedomain.com]
Re: [Preamble length for proposed UWB RFID PHY in 802.15 TG4f]
Abstract: [An analysis of acquisition performance of a non-coherent UWB system is presented. Different length preambles are compared.]
Purpose: [Guidance in defining preamble structure of the UWB RFID PHY]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Analysis of Preamble Length in Non-Coherent UWB Systems
Adrian Jennings
adrian.jennings@timedomain.com
+1 256 759 4708

## Slide 3: Background
The current baseline draft for 802.15.4f (document # IEEE 802.15-09-0804-05-004f) contains a number of TBDs, including preamble length
This document addresses the Base Mode preamble for the UWB PHY
Three questions require answers
  What is the minimum preamble length?
  What is the maximum preamble length?
  How will the variability in length be managed?

## Slide 4: Performance Considerations
Minimum preamble length
  Desired to minimize packet length
  Must deliver useful performance
Maximum preamble length
  Desired to maximize performance in difficult channels
  Must not be so large as to significantly impact tag throughput
Managing variability
  Continuous variability between extremes allows for most flexibility
  Small number of pre-defined lengths adds clarity and implementation ease

## Slide 5: Minimum Preamble Length

## Slide 6: Minimum Preamble Length Data
Current draft standard states 32 as minimum preamble length
There has been a proposal to reduce that number to 16
So the question is:
  “Compared to the performance with a preamble of 32, how much worse is the performance if the preamble is reduced to 16?”

## Slide 7: Experimental Setup
Data was collected using a non-coherent UWB system in an outdoor test range
Preamble length was set to 32
Measurements were taken at evenly distributed range bins
At each range bin, data was collected during a consistent time interval (i.e. the same number of packets were sent per range bin)
Data recorded
  The number of packets successfully received in each range bin
  The number of preamble pulses actually used for each successful packet

## Slide 8: Preamble Pulses Used – All Ranges
Note:
Data from all ranges included
Non-linear vertical axis

## Slide 9: Packets Dropped as F(Preamble Length)
Note:
Data from all ranges included

## Slide 10: Packets Dropped as F(Range)

## Slide 11: Packets Dropped as F(Range) - Rotated

## Slide 12: Packets Dropped by Length 16 Preamble as F(Range)
2s

## Slide 13: Conclusion
The majority of links were close using a preamble length of 16
Time Domain therefore recommends a minimum preamble length of 16
However, this answer is implementation specific, and other parties who are concerned about a shortened preamble are encouraged to provide a similar analysis