## Slide 1: UWB Standards and PHYs - Discussion
RFID/TG4f
OOK and BPM/BPSK (4a) Coherent Rx
OOK Non-Coherent RFID Rx
OOK Coherent RFID Rx
OOK Base/Enhanced Mode RFID Tx
OOK Long Range Mode RFID Tx
Michael McLaughlin (Decawave), Dalibor Pokrajac (GuardRFID), Adrian Jennings (Time Domain), Andy Ward (Ubisense), Tim Harrington (ZES)
4a UWB Tag
Optional, already defined (4a)
Mandatory
Already defined (4a)
To be discussed
Action:
Mandatory going forward pending:
Quantification of added complexity for non-coherent receiver: xtal tolerance, acquisition engine.
Then, what techniques could help the non-coherent receiver? Inserted 1:1 SFD at end of LR mode preamble? Whitening the packet for enough 1’s to maintain timing?
Change picture to reflect one receiver type since the standard does not define implementation, and if blue and green lines are black then the receivers (non-coherent, coherent) can be shown in a single box.

## Slide 2: General Discussion
Are the cross cases (purple, blue, green) linked?
  Either both mandatory or both optional?
What are the practical use cases for the blue/green links?
  What is the value?

## Slide 3: Debating the purple line….
Mandatory
  Pros
    Enables coherent receiver to additionally detect Base/Enhanced Mode tags
    Better interoperability / more complete standard
  Cons
    More machinery in 4a receiver (purpose of non-coherent is simplicity) Is this out of our scope?
    or much more complicated tag, counter to intent to make simple tag
Optional
  4a designer may choose to add functionality to receiver

## Slide 4: 4a* Discussion -
Substantially similar to 4a, but part of 4f - TBD
Modifications - TBD
  Band plan uses 4a channels 6, 7, 10 at 1.3 GHz bandwidth
  New channels denoted 6*, 7*, 10* ??????
    Same center frequencies as equivalent 4a bands????
    Wider bandwidth ????
  Support for OOK demodulation
  PRF as defined on slide 5