## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [UWB Enhanced Mode Proposal]
Date Submitted: [18 Mar, 2010]
Source: [Adrian Jennings] Company [Time Domain]
Address [330 Wynn Drive, Suite 300, Huntsville, AL. 35805. USA]
Voice:[+1 256 759 4708], FAX: [+1 256 922 0387], E-Mail:[adrian.jennings@timedomain.com]
Re: [Simple FEC scheme for UWB RFID PHY]
Abstract: [This document describes a simple triple-voting error correction scheme for the UWB RFID PHY]
Purpose: [To resolve outstanding issues on the current baseline proposal]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: UWB Enhanced Mode Proposal
Adrian Jennings
adrian.jennings@timedomain.com
+1 256 759 4708

## Slide 3: Encoding Scheme
The entire packet is repeated n times, with each packet following 0.815ms after the end of the previous packet
The PHY Header contains a 3 bit subsequence count, which indicates the number of packets to follow in the burst sequence. A non encoded packet uses the value 0.
Each packet contains the same data payload and sequence count from the MAC
Only packets with a subsequence count of 0 can append an LEI

## Slide 4: Example
For triple voting
  Subsequence count (SSC) starts at 2
  Packet 1 contains SSC 2, sequence count xxxx
  Packet 2 contains SSC 1, sequence count xxxx
  Packet 3 contains SSC 0, sequence count xxxx, and may append an LEI
The demodulation engine aggregates packets with the same sequence count
The location engine aggregates packets with same sequence and subsequence counts