## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: TG4e Closing Report for LA Jan 2010
Date Submitted: 21 January 2010
Source: Pat Kinney Company: Kinney Consulting LLC
Voice:+1.847.960.3715, FAX: +1.630.524.9054, E-Mail:pat.kinney@ieee.org
Re: TG4e Closing Report for January 2010Session
Abstract: Closing Report for the TG4e Session
Purpose: Amendments to IEEE 802.15.4 MAC
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: TG4e PAR Scope of Proposed Standard
The intention of this amendment is to enhance and add functionality to the 802.15.4-2006 MAC to a) better support the industrial markets and b) permit compatibility with modifications being proposed within the Chinese WPAN.
Specifically, the MAC enhancements are limited to:
TDMA: to provide a) determinism, b) enhanced utilization of bandwidth
Channel Hopping: to provide additional robustness in high interfering environments and enhance coexistence with other wireless networks
GTS: to increase its flexibility such as a) supporting peer to peer, b) the length of the slot, and c) number of slots
CSMA: to improve throughput and reduce energy consumption
Security: to add support for additional options such as asymmetrical keys
Low latency: to reduce end to end delivery time such as needed for control applications

## Slide 3: Purpose of Proposed Standard
This functionality facilitates Industrial applications (such as addressed by HART 7 and the ISA100 proposed standards), and those enhancements defined by the proposed Chinese WPAN standard that aren't included in TG4c. This amendment addresses coexistence with wireless protocols such as 802.11, 802.15.1, 802.15.3, and 802.15.4.

## Slide 4: Meeting Goals
Finalize any remaining technical issues
  Specifically resolve FCF format
Review all comments pertaining to draft
Prepare draft for WG letter ballot
  Formatted as per IEEE-SA Styles manual
Approve draft for Letter Ballot

## Slide 5: TG4e Meetings This Week
Mtg | Monday | Tuesday | Wed | Thursday
AM1 |  | FCF discussion TSCH & Low Energy reports |  | FCF merger review and decision Draft Review: Annex M, Section 5
AM2 | Opening Logistics, Factory Automation, Channel Diversity, Blink | EGTS report FCF discussion FCF decision |  | Draft Review: Section 6
PM1 | FCF Presentations, FCF discussion |  |  | Draft Review: Section 6
PM2 | Joint Meeting w/4f, 4g |  |  | Approve draft for WG LB, closing logistics

## Slide 6: 802.15.4 MAC Pictorial
nonbeacon-enabled PAN
beacon-enabled PAN
E-GTS
TDMA
Contention Access
Contention-Free
Contention-Free
Factory Automation
ISA, HCF
ZigBee, 802.15.5
Overhead Reduction/Security
Low Energy
Channel Diversity
Blink frames (RFID)

## Slide 7: TG4e Schedule
Editing complete
Task Group Review (21 day) 20 Feb 2010
TG Comment Resolution 15 Mar 2010
Letter Ballot Starts (40 day) 5 Apr 2010
Letter Ballot Closes 15 May 2010
Resolve comments & reballot 24 Jun 2010
Resolve comments & final reballot 26 Aug 2010
Sponsor Ballot Nov 2010
Comment resolution & reballot Dec 2010
IEEE RevCom approval Mar 2011

## Slide 8: TG4e Motion to approve draft standard and request WG for letter ballot
“That the 802.15 TG4e approves the draft amendment P802-15-4e-D1_Draft_Amendment.pdf, to be constructed from the preliminary draft amendment 15-09-0604-06-004e-ieeestd802-15-4e-d0-x and the technical direction from the comment resolution document 15-10-0160-04-004e-Preliminary_Draft_Comments, and in doing so approves taking it to the 802.15 WG to seek approval to go to Letter Ballot.”
Moved by Ludwig Winkel
Seconded Ghulam Bhatti
TG4e Motion to Accept Draft by Task Group Passed Unanimously

## Slide 9: 802.15 WG Motion
Move that the 802.15 WG approve the start of a WG Letter Ballot requesting approval to forward document P802-15-4e-D1_Draft_Amendment.pdf, edited in accordance with comment spreadsheet 15-10-0160-04-004e and preliminary draft amendment 15-09-0604-06-004e-ieeestd802-15-4e-d0-x, to Sponsor Ballot pending the completion and inclusion of the edits in the draft.
Moved by Pat Kinney

## Slide 10: Conference Calls
No Task Group Calls are scheduled
Editor calls will occur as needed