## Slide 1
Euntae Won
Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: CSK related Comment Resolution Input Summary
Date Submitted: 17. May 2010
Source: [Jaeseung Son, Taehan Bae,Sridhar Rajagopal, Atsuya Yokoi, E.T. Won]
Contact:
Voice:
E-Mail: js1007.son@samsung.com
Re:
Abstract:
Purpose: addresses comments pending on input from Samsung for comment resolution
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.
Notes: 1

## Slide 2
Samsung response about CID 877,884,885
17. May 2010

## Slide 3: Assumptions
CSK signal is generated by 3 color light sources in 7 color bands that are defined in TG7 standard draft.
The 3 tops of CSK constellation triangle are decided by the center wave length of the 3 color bands on xy color coordinates. (page 3-4)
Symbol points of CSK constellation are defined by the symbol allocation design rules. (page5-7)
Data allocations are shown in page 8-10.

## Slide 4: xy color coordinates values for each color band
Color Code | color | Band (nm) | Center (nm) | (x , y)
000 | pB | 380-450 | 415 | (0.18, 0.01)
001 | B,BG | 450-510 | 480 | (0.09, 0.13)
010 | G | 510-560 | 535 | (0.19, 0.78)
011 | yG,gY | 560-600 | 580 | (0.51, 0.49)
100 | rO | 600-650 | 625 | (0.70, 0.30)
101 | R | 650-710 | 680 | (0.72, 0.28)
110 | R | 710-780 | 745 | (0.73, 0.27)
111 | Reserved | - | - | -
Notes: This slides shows ‘What is CMC?’.
This block diagram is the CMC system configuration.
First, transmit data is coded by the color coding block into xy values according to the xy color coordinate.
This picture shows the CIE1931 xy color coordinate with the example for CMC symbol positions.
All visible colors in the color palette defined by xy values.
And the numbers around the color palette show the wave lengths at each single tone colors.
And R,G,B figures shows the center wave length of the actual RGB LED devices.
In this case, 4 Symbol points are placed in the RGB tri angle.
That means this system can send 2 bits data information per symbol.
Next, these xy values are transformed into RGB values.
The relation between xy and RGB is showed by thses equations (according to “CIE1931 RGB color space”).
Those coefficients are defined by the RGB wave length. In this case RGB wave length are these (R:700nm, G:546.1nm, B:435.8nm).
In the receiver side, xy values are calculated from received RGB values.
And xy values are decoded into the received data.
In this system,
CMC symbols are provided as the visible colors which are made by RGB light sources.
And, the information is transmitted as the intensity ratio among RGB. Not as the each RGB absolute values like WDM.
CIE (Commission internationale de l'éclairage)
In 1931, CIE defined color standard as ‘CIE1931 RGB color space’.
3 primary colors in CIE1931 are R:700nm, G:546.1nm, B:435.8nm.

## Slide 5: Center of color bands on xy color coordinates
110
101
100
011
010
001
000
Notes: This slides shows ‘What is CMC?’.
This block diagram is the CMC system configuration.
First, transmit data is coded by the color coding block into xy values according to the xy color coordinate.
This picture shows the CIE1931 xy color coordinate with the example for CMC symbol positions.
All visible colors in the color palette defined by xy values.
And the numbers around the color palette show the wave lengths at each single tone colors.
And R,G,B figures shows the center wave length of the actual RGB LED devices.
In this case, 4 Symbol points are placed in the RGB tri angle.
That means this system can send 2 bits data information per symbol.
Next, these xy values are transformed into RGB values.
The relation between xy and RGB is showed by thses equations (according to “CIE1931 RGB color space”).
Those coefficients are defined by the RGB wave length. In this case RGB wave length are these (R:700nm, G:546.1nm, B:435.8nm).
In the receiver side, xy values are calculated from received RGB values.
And xy values are decoded into the received data.
In this system,
CMC symbols are provided as the visible colors which are made by RGB light sources.
And, the information is transmitted as the intensity ratio among RGB. Not as the each RGB absolute values like WDM.
CIE (Commission internationale de l'éclairage)
In 1931, CIE defined color standard as ‘CIE1931 RGB color space’.
3 primary colors in CIE1931 are R:700nm, G:546.1nm, B:435.8nm.

## Slide 6: 4CSK symbol allocation design rule
I
J
K
Gravity center of △IJK
3 bands’ decide tops of a CSK
Triangle (I, J, K).

## Slide 7: 8CSK symbol allocation design rule
I
J
K
Points divide sides in the ratio 1:2.
(2 points)
3 bands’ decide tops of a CSK
Triangle (I, J, K).
a
b
c
d
Midpoint of the side IJ
Line ba and line cd meet at right angles with line KI.
Points divide lines in the ratio 1:2.
(2 points)
Midpoint of the side KI

## Slide 8: 16CSK symbol allocation design rule
I
J
K
Gravity center of △IJK
3 bands’ decide tops of a CSK
Triangle (I, J, K).
Gravity center of each small △
(6 points)
Points divide sides in one third
(6 points)

## Slide 9: 4CSK data allocation
[0 0]
[0 1]
[1 0]
[1 1]
2bits / Symbol

## Slide 10: 8CSK data allocation
[0 0 0]
[0 1 0]
[1 0 0]
[1 1 1]
[0 0 1]
[0 1 1]
[10 1]
[1 1 0]
3bits / Symbol

## Slide 11: 16CSK data allocation
[0 0 0 0]
[0 1 0 1]
[1 0 1 0]
[1 1 1 1]
[0 0 1 0]
[0 0 0 1]
[0 0 1 1]
[0 1 0 0]
[1 0 0 0]
[0 1 1 0]
[0 1 1 1]
[1 1 0 0]
[1 0 0 1]
[1 0 1 1]
[1 1 1 0]
[1 1 0 1]
4bits / Symbol

## Slide 12: CSK constellations
CSK constellation is decided by the combination of the 3 color bands.
The performance of CSK depends on the form of the CSK constellation triangle.
The system can not select the combination which can not make a triangle on the xy color coordinates, like as (110-101-100) or (100-011-010).
Some color band combination examples and their xy coordinates’ values are shown in page12-23.

## Slide 13: Color band combination for CSK (110-010-000)
110
101
100
011
010
001
000
Band i
Band j
Band k
Color band combination (1)
Notes: This slides shows ‘What is CMC?’.
This block diagram is the CMC system configuration.
First, transmit data is coded by the color coding block into xy values according to the xy color coordinate.
This picture shows the CIE1931 xy color coordinate with the example for CMC symbol positions.
All visible colors in the color palette defined by xy values.
And the numbers around the color palette show the wave lengths at each single tone colors.
And R,G,B figures shows the center wave length of the actual RGB LED devices.
In this case, 4 Symbol points are placed in the RGB tri angle.
That means this system can send 2 bits data information per symbol.
Next, these xy values are transformed into RGB values.
The relation between xy and RGB is showed by thses equations (according to “CIE1931 RGB color space”).
Those coefficients are defined by the RGB wave length. In this case RGB wave length are these (R:700nm, G:546.1nm, B:435.8nm).
In the receiver side, xy values are calculated from received RGB values.
And xy values are decoded into the received data.
In this system,
CMC symbols are provided as the visible colors which are made by RGB light sources.
And, the information is transmitted as the intensity ratio among RGB. Not as the each RGB absolute values like WDM.
CIE (Commission internationale de l'éclairage)
In 1931, CIE defined color standard as ‘CIE1931 RGB color space’.
3 primary colors in CIE1931 are R:700nm, G:546.1nm, B:435.8nm.

## Slide 14: 4CSK xy coordinates values (110-010-000)
*** CSK constellation ***
xy coordinates of color band i, j, k
(xi yi) = (0.730 0.270)
(xj yj) = (0.190 0.780)
(xk yk) = (0.180 0.010)
Symbol data allocation on xy coordinates
[Data] --> (xp yp)
[0 0] --> (0.190 0.780)
[0 1] --> (0.367 0.353)
[1 0] --> (0.180 0.010)
[1 1] --> (0.730 0.270)

## Slide 15: 8CSK xy coordinates values (110-010-000)
*** CSK constellation ***
xy coordinates of color band i, j, k
(xi yi) = (0.730 0.270)
(xj yj) = (0.190 0.780)
(xk yk) = (0.180 0.010)
Symbol data allocation on xy coordinates
[Data] --> (xp yp)
[0 0 0] --> (0.190 0.780)
[0 0 1] --> (0.187 0.523)
[0 1 0] --> (0.370 0.610)
[0 1 1] --> (0.519 0.383)
[1 0 0] --> (0.180 0.010)
[1 0 1] --> (0.244 0.253)
[1 1 0] --> (0.455 0.140)
[1 1 1] --> (0.730 0.270)

## Slide 16: 16CSK xy coordinates values (110-010-000)
*** CSK constellation ***
xy coordinates of color band i, j, k
(xi yi) = (0.730 0.270)
(xj yj) = (0.190 0.780)
(xk yk) = (0.180 0.010)
Symbol data allocation on xy coordinates
[Data] --> (xp yp)
[0 0 0 0] --> (0.190 0.780)
[0 0 0 1] --> (0.249 0.638)
[0 0 1 0] --> (0.187 0.523)
[0 0 1 1] --> (0.370 0.610)
[0 1 0 0] --> (0.246 0.381)
[0 1 0 1] --> (0.367 0.353)
[0 1 1 0] --> (0.429 0.468)
[0 1 1 1] --> (0.426 0.211)
[1 0 0 0] --> (0.183 0.267)
[1 0 0 1] --> (0.242 0.124)
[1 0 1 0] --> (0.180 0.010)
[1 0 1 1] --> (0.363 0.097)
[1 1 0 0] --> (0.550 0.440)
[1 1 0 1] --> (0.609 0.298)
[1 1 1 0] --> (0.547 0.183)
[1 1 1 1] --> (0.730 0.270)

## Slide 17: Color band combination for CSK (100-010-001)
110
101
100
011
010
001
000
Band i
Band j
Band k
Color band combination (2)
Notes: This slides shows ‘What is CMC?’.
This block diagram is the CMC system configuration.
First, transmit data is coded by the color coding block into xy values according to the xy color coordinate.
This picture shows the CIE1931 xy color coordinate with the example for CMC symbol positions.
All visible colors in the color palette defined by xy values.
And the numbers around the color palette show the wave lengths at each single tone colors.
And R,G,B figures shows the center wave length of the actual RGB LED devices.
In this case, 4 Symbol points are placed in the RGB tri angle.
That means this system can send 2 bits data information per symbol.
Next, these xy values are transformed into RGB values.
The relation between xy and RGB is showed by thses equations (according to “CIE1931 RGB color space”).
Those coefficients are defined by the RGB wave length. In this case RGB wave length are these (R:700nm, G:546.1nm, B:435.8nm).
In the receiver side, xy values are calculated from received RGB values.
And xy values are decoded into the received data.
In this system,
CMC symbols are provided as the visible colors which are made by RGB light sources.
And, the information is transmitted as the intensity ratio among RGB. Not as the each RGB absolute values like WDM.
CIE (Commission internationale de l'éclairage)
In 1931, CIE defined color standard as ‘CIE1931 RGB color space’.
3 primary colors in CIE1931 are R:700nm, G:546.1nm, B:435.8nm.

## Slide 18: 4CSK xy coordinates values (100-010-001)
*** CSK constellation ***
xy coordinates of color band i, j, k
(xi yi) = (0.700 0.300)
(xj yj) = (0.190 0.780)
(xk yk) = (0.090 0.130)
Symbol data allocation on xy coordinates
[Data] --> (xp yp)
[0 0] --> (0.190 0.780)
[0 1] --> (0.327 0.403)
[1 0] --> (0.090 0.130)
[1 1] --> (0.700 0.300)

## Slide 19: 8CSK xy coordinates values (100-010-001)
*** CSK constellation ***
xy coordinates of color band i, j, k
(xi yi) = (0.700 0.300)
(xj yj) = (0.190 0.780)
(xk yk) = (0.090 0.130)
Symbol data allocation on xy coordinates
[Data] --> (xp yp)
[0 0 0] --> (0.190 0.780)
[0 0 1] --> (0.157 0.563)
[0 1 0] --> (0.360 0.620)
[0 1 1] --> (0.491 0.414)
[1 0 0] --> (0.090 0.130)
[1 0 1] --> (0.186 0.329)
[1 1 0] --> (0.395 0.215)
[1 1 1] --> (0.700 0.300)

## Slide 20: 16CSK xy coordinates values (100-010-001)
*** CSK constellation ***
xy coordinates of color band i, j, k
(xi yi) = (0.700 0.300)
(xj yj) = (0.190 0.780)
(xk yk) = (0.090 0.130)
Symbol data allocation on xy coordinates
[Data] --> (xp yp)
[0 0 0 0] --> (0.190 0.780)
[0 0 0 1] --> (0.236 0.654)
[0 0 1 0] --> (0.157 0.563)
[0 0 1 1] --> (0.360 0.620)
[0 1 0 0] --> (0.202 0.438)
[0 1 0 1] --> (0.327 0.403)
[0 1 1 0] --> (0.406 0.494)
[0 1 1 1] --> (0.372 0.278)
[1 0 0 0] --> (0.123 0.347)
[1 0 0 1] --> (0.169 0.221)
[1 0 1 0] --> (0.090 0.130)
[1 0 1 1] --> (0.293 0.187)
[1 1 0 0] --> (0.530 0.460)
[1 1 0 1] --> (0.576 0.334)
[1 1 1 0] --> (0.497 0.243)
[1 1 1 1] --> (0.700 0.300)

## Slide 21: Color band combination for CSK (011-010-001)
110
101
100
011
010
001
000
Band i
Band j
Band k
Color band combination (3)
Notes: This slides shows ‘What is CMC?’.
This block diagram is the CMC system configuration.
First, transmit data is coded by the color coding block into xy values according to the xy color coordinate.
This picture shows the CIE1931 xy color coordinate with the example for CMC symbol positions.
All visible colors in the color palette defined by xy values.
And the numbers around the color palette show the wave lengths at each single tone colors.
And R,G,B figures shows the center wave length of the actual RGB LED devices.
In this case, 4 Symbol points are placed in the RGB tri angle.
That means this system can send 2 bits data information per symbol.
Next, these xy values are transformed into RGB values.
The relation between xy and RGB is showed by thses equations (according to “CIE1931 RGB color space”).
Those coefficients are defined by the RGB wave length. In this case RGB wave length are these (R:700nm, G:546.1nm, B:435.8nm).
In the receiver side, xy values are calculated from received RGB values.
And xy values are decoded into the received data.
In this system,
CMC symbols are provided as the visible colors which are made by RGB light sources.
And, the information is transmitted as the intensity ratio among RGB. Not as the each RGB absolute values like WDM.
CIE (Commission internationale de l'éclairage)
In 1931, CIE defined color standard as ‘CIE1931 RGB color space’.
3 primary colors in CIE1931 are R:700nm, G:546.1nm, B:435.8nm.

## Slide 22: 4CSK xy coordinates values (011-010-001)
*** CSK constellation ***
xy coordinates of color band i, j, k
(xi yi) = (0.510 0.490)
(xj yj) = (0.190 0.780)
(xk yk) = (0.090 0.130)
Symbol data allocation on xy coordinates
[Data] --> (xp yp)
[0 0] --> (0.190 0.780)
[0 1] --> (0.263 0.467)
[1 0] --> (0.090 0.130)
[1 1] --> (0.510 0.490)

## Slide 23: 8CSK xy coordinates values (011-010-001)
*** CSK constellation ***
xy coordinates of color band i, j, k
(xi yi) = (0.510 0.490)
(xj yj) = (0.190 0.780)
(xk yk) = (0.090 0.130)
Symbol data allocation on xy coordinates
[Data] --> (xp yp)
[0 0 0] --> (0.190 0.780)
[0 0 1] --> (0.157 0.563)
[0 1 0] --> (0.297 0.683)
[0 1 1] --> (0.374 0.531)
[1 0 0] --> (0.090 0.130)
[1 0 1] --> (0.164 0.351)
[1 1 0] --> (0.300 0.310)
[1 1 1] --> (0.510 0.490)

## Slide 24: 16CSK xy coordinates values (011-010-001)
*** CSK constellation ***
xy coordinates of color band i, j, k
(xi yi) = (0.510 0.490)
(xj yj) = (0.190 0.780)
(xk yk) = (0.090 0.130)
Symbol data allocation on xy coordinates
[Data] --> (xp yp)
[0 0 0 0] --> (0.190 0.780)
[0 0 0 1] --> (0.214 0.676)
[0 0 1 0] --> (0.157 0.563)
[0 0 1 1] --> (0.297 0.683)
[0 1 0 0] --> (0.181 0.459)
[0 1 0 1] --> (0.263 0.467)
[0 1 1 0] --> (0.321 0.579)
[0 1 1 1] --> (0.288 0.362)
[1 0 0 0] --> (0.123 0.347)
[1 0 0 1] --> (0.148 0.242)
[1 0 1 0] --> (0.090 0.130)
[1 0 1 1] --> (0.230 0.250)
[1 1 0 0] --> (0.403 0.587)
[1 1 0 1] --> (0.428 0.482)
[1 1 1 0] --> (0.370 0.370)
[1 1 1 1] --> (0.510 0.490)