## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [470MHz Narrow Band DSSS Proposal for MR-O-QPSK]
Date Submitted: [5 July, 2009]
Source: [X Wang, Y X Fu, J Shen, J F Luo, X Tao, Haituo Liu, L Li]
Company: [SIMIT, Vinno, Huawei]
Address: [NO.865 Changning Road, Shanghai, 200050, China]
Voice:[+86 21 6251 1070 ], FAX:[+86 21 6213 2314],
E-Mail:[ wilsonwangxiang@gmail.com, fxy@mail.sim.ac.cn]
Re: [IEEE 802.15.4g group]
Abstract: According to the regular limitation of frequency in China Smart Grid. A proposal of MR-PHY layer on 470MHz to meet the requirement and characteristic.
Purpose: Presented to the 802.15.4g SUN Task Group for consideration
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: 470MHz Narrow Band DSSS Proposal for MR-O-QPSK

## Slide 3: 470-510MHz Regular Limit in China
Max TX Power = 50mW (e.r.p)
The occupied BW: no larger than 200 kHz
Frequency tolerance: 100×10-6
Max TX Time: no larger than 5s

## Slide 4: Why DSSS
MR-FSK and OFDM in 470MHz
Large Transmit Distance
  DSSS obtain larger transmit range due to process gain
Target Low Data Rate
  Low data rate is obtained by different spread code with BW unchanged
  Simplify design of analog front end

## Slide 5: Consideration
Bands: 470-510MHz
Channel spacing: 200KHz
Chip rate: 100Kcps
Data rate: 6.25~50Kbps
Clock offset tolerance: ±20PPM
FEC: (2,1,7) convolution code
Shape: Raised cosine pulse shape with roll-off factor = 0.8

## Slide 6: Further Work
Appropriate spread code
  Clock offset tolerance
  Simple Implement
Suitable preamble design

## Slide 7: Thank you