## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [LB50 comment resolution related to subclause 5.6.1 to 5.6.4]
Date Submitted: [June, 2010]
Source: [Dae Ho Kim, Tae-Gyu Kang, Sang-Kyu Lim, Il Soon Jang, You Jin Kim] Company [ETRI]
Address [138 Gajeongno, Yuseong-gu, Daejeon, 305-700]
Voice:[+82-42-860-5648], FAX: [+82-42-860-5218], E-Mail:[dhkim7256@etri.re.kr]
Re: [Response to LB50 comments]
Abstract: [This document describes a LB50 comment resolution related to suclause 5.6.1 to 5.6.4]
Purpose: [Proposal to resolve LB50 comments ]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: LB50 comment resolution related to subclause 5.6.1 to 5.6.4
Dae Ho Kim
dhkim7256@etri.re.kr
ETRI

## Slide 3: CID 123
Resolution/Instruction to editor
  We need a more discussion
    My suggestion is that the random access is better than slotted random access.
CID | Name | Clause | Subclause | Page | Line | Comment | Suggested Remedy
123 | Michael Bahr | 5 | 5.6.1 | 11 | 37-45 | While it is useful to have the 3 topologies as mentioned at the beginning of clause 5 (P2P, star, broadcast), I do not see the need for a superframe definition, at least not right now. The current definition is not flexible enough for todays applications. For instance, only beacon intervals that are powers of 2 are possible (2^0, 2^1,...,2^14). exactly 16 slots are available where one is actually assigned to the beacon. Only 7 guaranteed time slots are possible within the available 15 time slots. | * Remove the current superframe specification from the VLC draft. * Use a scheme more similar to IEEE 802.11 (without all the thousand bytes) that simply announces the coordinator in the beacon, so that devices learn about the coordinator. * Leave hooks for adding a flexible superframe structure later, after analysis of the requirements of todays applications. * remove the specification of slotted random access and use random access. * change the beacon specification (remove everything except some beacon interval) Some specific actions: * remove line 18 on page 4 ("Optional allocation of guaranteed time sltos (GTSs)") * remove GTS from clause 4 * remove clause 5.6.1

## Slide 4: CID 133
Resolution/Instruction to editor
  Accept, do as suggested remedy
CID | Name | Clause | Subclause | Page | Line | Comment | Suggested Remedy
133 | James Gilb | 5 | 5.6.1 | 11 | 45 | The draft refers to "slotted random access" but four distinct methods are used, random access, slotted random access and random access with CCA. and slotted random access with CCA. The correct terms for these are aloha, slotted aloha, CSMA/CA, and slotted CSMA/CA (technically pure aloha doesn't use a backoff, but the one you have is close enough in terms of performance characteristics). | Use the correct terms in the draft. In this location, you are referring to all four, so it should just be "random access method, as described in 7.6.1.5"

## Slide 5: CID 137
Resolution/Instruction to editor
  This section is overview.
    Line 31 on page 12 describes as “More information on the superframe can be found in 7.6.1.1”.
    More detail information is introduced at clause 7.6.1.1
  Reject
CID | Name | Clause | Subclause | Page | Line | Comment | Suggested Remedy
137 | Soo-Young Chang | 5 | 5.6.1 | 12 | 1 | Need to specify the detailed information on slots such as the number of slots in a frame and slot size in Figures 7 and 8. | Need to put detailed information to specify slots and a frame.

## Slide 6: CID 139
Resolution/Instruction to editor
  Figure 8 is the same as the thing in IEEE 802.15.4 standard
  Accept, do as suggested remedy
CID | Name | Clause | Subclause | Page | Line | Comment | Suggested Remedy
139 | Clint Chaplin | 5 | 5.6.1 | 12 | 36 | (SY) Figure 8 does not actually show any GTSs, even though the figure text is about GTSs | Show GTSs in the figure

## Slide 7: CID 140
Resolution/Instruction to editor
  Accept in principle
    do as suggested remedy or modify the text
    My suggestion is that do as suggested remedy
CID | Name | Clause | Subclause | Page | Line | Comment | Suggested Remedy
140 | James Gilb | 5 | 5.6.1 | 12 | 27 | "However, a sufficient ... join the network." is not true. There may or may not be sufficient time, it is not possible to know. | Delete the sentence "However, a sufficient ... join th network."

## Slide 8: CID 141
Resolution/Instruction to editor
  On line 32 in page 138 of 7.2.2.1,
    The maximum number of GTS descriptors shall be limited to seven.
  Accept in principle, remain a related sentence and add a new sentence as “More detailed information about the maximum number of GTS can be found in 7.6.1.1.”
CID | Name | Clause | Subclause | Page | Line | Comment | Suggested Remedy
141 | R. Roberts | 5.6.1 |  | 12 | 27 | The offending sentence is … The coordinator may allocate up a number of these GTSs, and a GTS may occupy more than one slot period. | 15.4 said the coordinator my allocate up to seven of these GTSs. Did we really intent to say "a number of these" or is this a typo?

## Slide 9: CID 142
Resolution/Instruction to editor
  Device discovery is explained in 7.6.2.4.
    It is the almost same function with network discovery.
  Accept in principle,
    change the word “network discovery” into “device discovery”
    add the reference about device discovery(7.6.2.4).
CID | Name | Clause | Subclause | Page | Line | Comment | Suggested Remedy
142 | Soo-Young Chang | 5 | 5.6.2 | 13 | 3 | Some schemes for network discovery needs to be introduced. | Need to explain some schemes for network discovery.

## Slide 10: CID 143, 148 and 154
Resolution/Instruction to editor
  CID 149 has already resolved these comments.
  Accept, modify the figures to indicate the last ACK is optional
    Figure 10, 11 and 12
CID | Name | Clause | Subclause | Page | Line | Comment | Suggested Remedy
143 | David Cypher | 5 | 5.6.3 | 13 | 49 | The text in the paragraph preceding Figure 10 states an optional acknowledgment frame, while the figure shows no option. | Correct inconsistency, 1) add "(if requested)", if this is the correction or 2) remove the work optional from the text, if this is the correction.
148 | David Cypher | 5 | 5.6.3.1 | 14 | 29 | The text in the paragraph preceding Figure 11 states an optional acknowledgment frame, while the figure shows no option. | Correct inconsistency, 1) add "(if requested)", if this is the correction or 2) remove the work optional from the text, if this is the correction.
154 | David Cypher | 5 | 5.6.3.1 | 15 | 12 | The text in the paragraph preceding Figure 12 states an optional acknowledgment frame, while the figure shows no option. | Correct inconsistency, 1) add "(if requested)", if this is the correction or 2) remove the work optional from the text, if this is the correction.

## Slide 11: CID 145, 151b
Resolution/Instruction to editor
  CID 151 has already resolved these comments.
  Reject, see CID 151
CID | Name | Clause | Subclause | Page | Line | Comment | Suggested Remedy
145 | James Gilb | 5 | 5.6.3 | 13 | 7 | This subclause covers technical details which are described in Clause 7. There is no reason to describe this in an overview. | Delete subclause 5.6.3.
151b | James Gilb | 5 | 5.6.3.1 | 14 | 1 | The subclause depth is wrong here, 5.6.3.1 and 5.6.3.2 should be at the same depth as 5.6.3. Luckily, the easy solution is to simply delete all three of these subclauses as they are not needed. | Either delete 5.6.3, 5.6.3.1and 5.6.3.2 (the best answer) or fix the subclause depth to be consistent.

## Slide 12: CID 146, 152
Resolution/Instruction to editor
  We don’t know exactly what the comments about figures 11 and 12 mean.
  All frame can occupy multiple slots according to frame size
    related clause 7.6.1
  Reject
CID | Name | Clause | Subclause | Page | Line | Comment | Suggested Remedy
146 | Soo-Young Chang | 5 | 5.6.3.1 | 14 | 13 | In figure 11, 1. All frames occupies one slot of the same size while they have different sizes. It results in inefficiency in throughput. 2. When using random access, the performance is low with fixed size slots. | Need to modify the scheme or structure.
152 | Soo-Young Chang | 5 | 5.6.3.1 | 15 | 1 | In figure 12, 1. All frames occupies one slot of the same size while they have different sizes. It results in inefficiency in throughput. 2. When using random access, the performance is low with fixed size slots. | Need to modify the scheme or structure.

## Slide 13: CID 147
Resolution/Instruction to editor
  Related paragraph is a communication to a coodinator in a nonbeacon-enabled WPAN associated with Figure 12.
  Network device can not know whether data is pended or not because nonbeacon-enabled WPAN has no beacon. So data request is transmitted at an application-defined rate.
  Reject
CID | Name | Clause | Subclause | Page | Line | Comment | Suggested Remedy
147 | Soo-Young Chang | 5 | 5.6.3.1 | 14 | 38 | The condition of "If a data frame is pending" is not needed because "Data request" is sent due to its recognition of pending data. | Need to delete "If a data frame is pending".

## Slide 14: CID 151a
Resolution/Instruction to editor
  see CID 14a, 14b and CID 2
    We don’t know whether CIDs 14a, 14b and 2 has been resolved.
CID | Name | Clause | Subclause | Page | Line | Comment | Suggested Remedy
151a | Larry Taylor | 5 | 5.6.3.2 | 14 | 19 | VLC sphere of influence is not a defined term. Use "operating space" or a term defined and used consistently for this concept | 

## Slide 15: CID 162
Resolution/Instruction to editor
  only one description about MAC and PHY mixed frame simultaneously
  Reject
    If accepted, skip from CID 163 to 179
CID | Name | Clause | Subclause | Page | Line | Comment | Suggested Remedy
162 | James Gilb | 5 | 5.6.4.1 | 15 | 42 | The entire subclause needs to be deleted because it repeats normative information found in other subclauses. This is supposed to be an overview, not a repeat of the normative figures in the other subclauses | Delete Subclause 5.6.4.1 through 5.6.4.5

## Slide 16: CID 164, 167
Resolution/Instruction to editor
  The figures allow us to know the frame information easier
  If there is no problem we’d better to remain the figures 13 through 17
  We need to adjust the sync between the figures
  Reject
CID | Name | Clause | Subclause | Page | Line | Comment | Suggested Remedy
164 | James Gilb | 5 | 5.6.4.1 | 15 | 50 | The PHY frame format is repeated in all 5 subsections. This will lead to mistakes. It should not be in a picture that shows the MAC frame format, after all, the PHY simply gets an MSDU and wraps it the same way regardless of the MAC frame format. Including this picture with the MAC frame is a mistake. | Delete the PHY layer picture from all of the MAC frame format pictures in 5.6.4. If there is a need for a picture of the PHY frame format, use a separate picture. However, there isn't a need for the PY frame format figure in an overview, so simply deleting it is the best answer.
167 | James Gilb | 5 | 5.6.4.1 | 16 | 3 | This figure is an excellent example of why normative information shall not be repeated in a specification. The PHR is shown as 1 octet in length, yet in Clause 6 it is defined to be 3 octets in length. Because the information is repeated not just once, but in 4 figures, there are now four corrections to make. | Delete Figures 13, 14, 15 16 and 17 as they repeat normative information which will results (and indeed has resulted) in technical errors in the draft.

## Slide 17: CID 155, 161
Resolution/Instruction to editor
  CID 158 has been already resolved
  at CID 155
    ACK frame type is only one with no payload.
    see page 17, line 4
  Accept in principle
    frame types: beacon, data, ACK, command, visibility and color
    According to the doc. 10/0348/r0, the color frame has been added
CID | Name | Clause | Subclause | Page | Line | Comment | Suggested Remedy
155 | David Cypher | 5 | 5.6.4 | 15 | 39 | the text states four frame types, and covers five subclauses, but read the rest of the document there are six. | There are too many inconsistencies to provide a solution. Are there two ack frames (one with no payload and one with payload)? As but one example.
161 | Sridhar Rajagopal | 5.6.4 |  | 15 |  | missing frame types | add visibility frame, add dimming, color stabilization

## Slide 18: CID 160
Resolution/Instruction to editor
  The first sentence in 5.6.1 describes as “This standard allows the optional use of a superframe structure.”
  Supferframe structure is optional.
    If GTS concept is not flexible enough for any applications, we can choose the use of GTS.
  Reject
CID | Name | Clause | Subclause | Page | Line | Comment | Suggested Remedy
160 | Michael Bahr | 5 | 5.6.4.1 | 15 | 42-22 | (see comment on 5.6.1) GTS concept is not flexible enough for todays applications. | * remove "superframe specification, GTS fields," from line 46 on page 15 * remove fields Superframe Specification and GTS Fields from figure 13

## Slide 19: CID 165, 166, 169 and 170
Resolution/Instruction to editor
  PHR format in figure 13 through 16 is wrong.
  Need to harmonize the packet format of Figure 13, 14, 15 and 16 with Figure 21, 65, 73, 76 and 81.
  Accept, do as suggested remedy
CID | Name | Clause | Subclause | Page | Line | Comment | Suggested Remedy
165 | Khanh Tuan Le | 5 | 5.6.4.1 | 16 | 1 to 14 | The frame format is different from the general packet format in section 6.4.1 page 39. | Harmonize the packet format.
166 | Khanh Tuan Le | 5 | 5.6.4.2 | 16 | 30 to 40 | The frame format is different from the general packet format in section 6.4.1 page 39. | Harmonize the packet format.
169 | Khanh Tuan Le | 5 | 5.6.4.3 | 17 | 14 to 24 | The frame format is different from the general packet format in section 6.4.1 page 39. | Harmonize the packet format.
170 | Khanh Tuan Le | 5 | 5.6.4.4 | 17 | 38 to 48 | The frame format is different from the general packet format in section 6.4.1 page 39. | Harmonize the packet format.

## Slide 20: CID 168, 172
Resolution/Instruction to editor
  These CIDs relate to CID 163
  CID 163 has been already resolved
  But we need to discuss the suggested remedy of CID 163
    see slide 22
CID | Name | Clause | Subclause | Page | Line | Comment | Suggested Remedy
168 | James Gilb | 5 | 5.6.4.2 | 16 | 44 | The sentences "The MAC payload ... form the MAC data frame (i.e., MPDU)."repeat normative information and so need to be deleted. The Figure shows the fields and the correct order. | Delete the sentences "The MAC payload ... form the MAC data frame (i.e., MPDU)."
172 | James Gilb | 5 | 5.6.4.4 | 17 | 30 | The sentences "The MAC payload ... form the MAC command frame (i.e., MPDU)."repeat normative information and so need to be deleted. The Figure shows the fields and the correct order. | Delete the sentences "The MAC payload ... form the MAC command frame (i.e., MPDU)."

## Slide 21: CID 171
Resolution/Instruction to editor
  This CID relates to CID 163 and is similar to CIDs 168 and 172
  But we need to discuss the suggested remedy of CID 163
    see slide 22
CID | Name | Clause | Subclause | Page | Line | Comment | Suggested Remedy
171 | James Gilb | 5 | 5.6.4.3 | 17 | 4 | The sentences "The MAC acknowledgment ... form the MAC acknowledgment frame (i.e., MPDU)."repeat normative information and so need to be deleted. The Figure shows the fields and the correct order. | Delete the sentences "The MAC acknowledgment frame ... form the MAC acknowledgment frame (i.e., MPDU)."

## Slide 22: CID 192
Resolution/Instruction to editor
  this CID is similar to CIDs 163, 168, 171 and 172
  But if we accept these suggested remedies, we’d better to delete subcluse 5.6.4.1 to 5.6.4.5 because no sentence is remained.
    See CID 162 (slide 15)
  My suggestion is a reject of CID 163, 168, 171, 172 and 192
    We can know more information through these subclauses
CID | Name | Clause | Subclause | Page | Line | Comment | Suggested Remedy
192 | James Gilb | 5 | 5.6.4.1 | 19 | 19 | The sentence "The MAC beacon frame ... PHY packet (i.e., PPDU)." repeats normative information that is better covered in clause 6. In addition, it is repeated in three other subclauses in this clause. The information is not relevant to an overview and should be deleted. | Delete the sentences "The MAC beacon frame ... PHY packet (i.e., PPDU)." here and the copies of the paragraph in 5.6.4.2, page 16, line 49, 5.6.4.3, page 17, line 8 and 5.6.4.4, page 17, line 51.

## Slide 23: CID 173, 174 and 178
Resolution/Instruction to editor
  Need to put more explanation about frame
  CID 173, 178: Accept, do as suggested remedy
  CID 174: Accept. But, we need to modify Figure 17 rather than a new figure
CID | Name | Clause | Subclause | Page | Line | Comment | Suggested Remedy
173 | Billy Verso, (affiliation DecaWave) | 5 | 5.6.4.5 | 18 | 3 to 12 | Figure 17—Visible/Dimming Frame, frame format seems to be special in that the optional data follows the FCS. It would be good to explain why this is done (i.e. as opposed to defining a MAC command frame.) | Add description to explain this special function.
174 | Soo-Young Chang | 5 | 5.6.4.5 | 18 | 1 | This section needs more detailed explanations on the frame. Figure 17 should be redrawn and PHY Header should be renamed. | Need to put more explanation on this section and a new figure for Figure 17.
178 | Sridhar Rajagopal | 5.6.4.5 |  | 18 |  | update text | update text to reflect use for dimming and VPM support (and also, for color stabilization)

## Slide 24: CID 179
Resolution/Instruction to editor
  Visibility frame is in subclause 7.5
    need to unify the names of visibility frame or visible/dimming frame to one name
  Reject
CID | Name | Clause | Subclause | Page | Line | Comment | Suggested Remedy
179 | James Gilb | 5 | 5.6.4.4 | 18 | 1 | There is no Visible/Dimming frame in the draft. There are some MAC commands that enable these functions, but the format of MAC commands is covered in subclause 7.3. | Delete subclause 5.6.4.5.