## Slide 1
<September 2010>
<Seung-Hoon Park>, <Samsung Electronics>
Slide <number>
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Resolution of TG6 comments: S7-303]
Date Submitted: [22 September, 2010]
Source: [Seung-Hoon Park, Ranjeet Kumar Patro, Sridhar Rajagopal] Company [Samsung Electronics]
Address [416, Maetan-3Dong, Yeongtong-Gu, Suwon-Si, Gyeonggi-Do, 443-742, Korea]
Voice:[+82-10-9349-9845], FAX: [+82-31-279-2441], E-Mail:[shannon.park@samsung.com]
Re: [Proposed Resolution of D0 Comments S7-303]
Abstract: [Comment resolution for letter ballot 55 for S7-303]
Purpose: [Propose Resolution of D0 Comment S7-303]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.
Notes: doc.: IEEE 802.15-<doc#1>
<September 2010>
        <Seung-Hoon Park>, <Samsung Electronics>
Page <number>

## Slide 2: Proposed Resolution of D0 Comment S7-303
<September 2010>
Slide <number>
<Seung-Hoon Park>, <Samsung Electronics>
Comments relative to
Distributed Time Sharing by Active co-channel usage advertisement

## Slide 3: D0 Comment S7-303
<September 2010>
Slide <number>
Comment: "by tracking the overflow of total used capacity only when inter-piconet message exchange is possible" --> need more details.
Commentators proposed resolution: "In passive channel scan, existing coordinator shall try to locate beacon or B2 message in a channel. And prospective coordinator shall enable its receiver for at least mPassiveScanDuration duration waiting for B2."
Must be satisfied:
<Seung-Hoon Park>, <Samsung Electronics>
Notes: doc.: IEEE 802.15-<doc#>
<month year>
        <Seung-Hoon Park>, <Samsung Electronics>
Page <number>

## Slide 4: Proposed Resolution
<September 2010>
Slide <number>
Accepted in principle.
The coexistence method using B2 frame exchange related to the comment will be provided in the separate sub-clause.
It was proposed originally named by Distributed Time Sharing and the name changed to Active co-channel usage advertisement during MAC ad-hoc meeting in London.
<Seung-Hoon Park>, <Samsung Electronics>
Notes: doc.: IEEE 802.15-<doc#>
<month year>
        <Seung-Hoon Park>, <Samsung Electronics>
Page <number>

## Slide 5
<September 2010>
<Seung-Hoon Park>, <Samsung Electronics>
Slide <number>
Note [1]: Refers to multiple body area networks (BANs) on the same body/person.
Coexistence Mechanisms | 10-50 MHz HBC/EFC[1] | MICS Band | 868 MHz Band | 902-928 MHz Band | 2.36 GHz MBANS Band | 2.4 GHz ISM Band | UWB Band | 
Regulatory Rules | *TBD* | LBT channel selection, communication session occupancy | LBT channel selection & occupancy | None if low power, non spread spectrum power levels | *pending* possible duty cycle limit on aggregate transmissions, etc. | None if low power, non spread spectrum power levels | LDC or DAA for 3.1 to 4.8 GHz | 6 -10.6 GHz Different bands in regulations
Scan for channel selection | S, SD, D | S, SD | S, SD | S, SD | S, SD | S, SD | S, SD | S, SD
Active piconet time sharing | S, SD, D | S | S | S | S | S, SD | S, SD | S, SD
Active co-channel usage advertisement | S, SD, D | None | S | S | S | S, SD | S, SD | S, SD
Beacon Shifting | Not applicable | D Limited / No applicability given LBT restrictions | SD, D | SD, D | SD, D | SD, D | D | D
Channel Hopping | Not applicable | D | SD, D | SD, D | SD, D | SD, D | SD, D | SD, D
Non-medical traffic reduction, Load control per traffic class | Not applicable | Not applicable – only medical traffic in this PHY by regulations | S, SD, D | S, SD, D | Not applicable – only medical traffic in this PHY by regulations | S, SD, D | S, SD, D | S, SD, D
Notes: doc.: IEEE 802.15-<doc#>
<month year>
        <Seung-Hoon Park>, <Samsung Electronics>
Page <number>

## Slide 6: Related Sentences from Draft 01
<September 2010>
<Seung-Hoon Park>, <Samsung Electronics>
Slide <number>
P112, L42-45, in D01
  The BAN descriptor field in B2 message contains coordinator address, length of contention access period in current superframe, beacon period, offset to next superframe start time and minimum reservation period and priority of the piconet.
In B2 message in D01, for consistency
  offset to next superframe start time
   Offset to Start Time
  minimum reservation period
   Reserved slots
Notes: doc.: IEEE 802.15-<doc#>
<month year>
        <Seung-Hoon Park>, <Samsung Electronics>
Page <number>

## Slide 7: Related Sentences from Draft 01
<September 2010>
<Seung-Hoon Park>, <Samsung Electronics>
Slide <number>
P113, L6-8, in D01
  Upon receiving coexistence request frame, existing coordinator shall respond with coexistence assignment frame to the prospective coordinator, by providing exclusive time duration or rejecting the coexistence assignment request, to the prospective coordinator.
In B2 message in D01, for consistency
  exclusive time duration  Reserved slots
Notes: doc.: IEEE 802.15-<doc#>
<month year>
        <Seung-Hoon Park>, <Samsung Electronics>
Page <number>

## Slide 8: Related Sentences from Draft 01
<September 2010>
<Seung-Hoon Park>, <Samsung Electronics>
Slide <number>
P113, L14-17, in D01
Next Superframe Start Time and Minimum Reservation Period Length in B2 may be used to share time resource within piconets, after the end of coexistence initialization phase. Next B2 will always come after Minimum Reservation Period Length, so neighboring coordinator which listens B2 can predict the timing of next B2. This helps to avoid for coordinator to wait B2 at listening mode all the time.
In B2 message in D01, for consistency
  Next Superframe Start Time
   Offset to Start Time
  Minimum Reservation Period Length
   Reserved slots
Notes: doc.: IEEE 802.15-<doc#>
<month year>
        <Seung-Hoon Park>, <Samsung Electronics>
Page <number>

## Slide 9: Operation of Active co-channel usage advertisement
<month year>
<Seung-Hoon Park>, <Samsung Electronics>
Slide <number>
Hub 2 detects the interference and stops the operation of channel access in BAN 2.
Hub 2 waits the possible Beacon or B2. message, and receives B2 from Hub 1 after some time.
Hub 2 sends B2 message during CAP of BAN 1.
Hub 2 may adjust beacon period and the allocation size.
Hub 2 may broadcast the changed beacon period by beacon or B2.
Notes: doc.: IEEE 802.15-<doc#>
<month year>
        <author>, <company>
Page <number>

## Slide 10: Operation of Active co-channel usage advertisement
<month year>
<Seung-Hoon Park>, <Samsung Electronics>
Slide <number>
“Offset to Start Time” and “Reserved slots” in B2 helps Hub2 calculating the timing of next B2.
Hub 1 and Hub 2 may wakeup and listen B2 frame even in inactive period by the predicted timing of each B2.
Notes: doc.: IEEE 802.15-<doc#>
<month year>
        <author>, <company>
Page <number>

## Slide 11: Features
This is nearly same operation to Active Superframe Interleaving.
Superframe period does not need to be identical among the collocated BANS.
No request & response. Just receiving broadcast message, B2.
Not precise coordination. Coarse time sharing.
Pros
  Resource sharing ratio can be adjusted according to the traffic load and traffic class priority of BANs.
  Coexistence for more than 2 BANs can be resolved by receiving multiple B2 messages for CAP duration.
Support for allocation reduction
  The total capacity of the collocated BANs can be calculated by coexistence information such as beacon period, reservation slots, or etc. (S7-303)
<September 2010>
Slide <number>
<Seung-Hoon Park>, <Samsung Electronics>

## Slide 12: Requirements
The concept of Active/Inactive period is required
  Active/Inactive superframe is not flexible to support various traffic load and QoS constraints.
  The case that active period is larger than inactive period can not be supported by active/inactive superframe mechanism.
Following fields is required in B2 frame
  CAP length
  Offset to Start Time
  Reserved Slot
<September 2010>
<Seung-Hoon Park>, <Samsung Electronics>
Slide <number>

## Slide 13: Field Definition
CAP length
  The CAP Length field is set to the length of contention access phase immediately after the B2 frame in slot allocation unit.
  CAP length is set to the value more than minCAP which is decided considering operation on CAP for control messages or coexistence messages.
<September 2010>
<Seung-Hoon Park>, <Samsung Electronics>
Slide <number>

## Slide 14: Field Definition
  Offset to Start Time
  This field is set to the length of period in slot allocation unit immediately after the B2 frame until the start of the active superframe to be advertised.
<September 2010>
<Seung-Hoon Park>, <Samsung Electronics>
Slide <number>

## Slide 15: Field Definition
  Reserved Slot
  This field is set to the length of period in slot allocation unit immediately after the time designated by the Offset to start time until the B2 frame start of the active superframe to be advertised.
<September 2010>
<Seung-Hoon Park>, <Samsung Electronics>
Slide <number>

## Slide 16: Proposed Edited Text
<September 2010>
<Seung-Hoon Park>, <Samsung Electronics>
Slide <number>
Notes: doc.: IEEE 802.15-<doc#>
<month year>
        <Seung-Hoon Park>, <Samsung Electronics>
Page <number>

## Slide 17: For co-operation
When Hub 2 want a time sharing coexistence mechanism,
If beacon period between BAN 1 and BAN 2 can be adjusted to be identical
  Use Active Superframe Interleaving
Else
  Use Active Co-channel Usage Advertisement
<September 2010>
Slide <number>
<Seung-Hoon Park>, <Samsung Electronics>

## Slide 18: Proposed Resolution
<September 2010>
<Seung-Hoon Park>, <Samsung Electronics>
Slide <number>
This proposal was based on
  Distributed TDMA Scheduling [DCN321-01]
  MAC and Security Baseline Proposal ¨C Normative Text.doc [DCN196-02]
  samsung-mac-proposal-documentation [DCN 344-03]
    7.2.1.4 Occasional collision detection and avoidance during slot allocation
  Active co-channel usage advertisement is defined in Table at 7.11
Notes: doc.: IEEE 802.15-<doc#>
<month year>
        <Seung-Hoon Park>, <Samsung Electronics>
Page <number>

## Slide 19: Proposed Resolution
<September 2010>
<Seung-Hoon Park>, <Samsung Electronics>
Slide <number>
Original concept in DCN 344-03
Notes: doc.: IEEE 802.15-<doc#>
<month year>
        <Seung-Hoon Park>, <Samsung Electronics>
Page <number>