## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Resolutions to MR-FSK Comments on MPM management scheme issues]
Date Submitted: [13 September 2010]
Source: [Daniel Popa, Hartman Van Wyk, Roberto Aiello, John Buffington]
Company [ITRON],
Address [France],
E-Mail:[daniel.popa@itron.com, hartman.vanwyk@itron.com]
Re: [ 802.15.4g Comment Resolution for LB51.]
Abstract: []
Purpose: [LB51 Comment Resolution]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2
Comments ID:
728, 749, 750, 1160

## Slide 3
Comments ID: 749, 750
CID # 750: ECC REC 70-03 require channel spacing < 100 kHz for narrowband modulation and wideband modulation other
than FHSS and DSSS
Requested resolution: Change channel spacing to 100 kHz for the common signaling mode.
Response: ECC REC 70-03 allows for channel spacing larger than 100kHz.
Proposed resolution: Reject.
CID #749: ECC REC 70-03 require channel spacing < 100 kHz for narrowband modulation and wideband modulation other than
FHSS and DSSS
D. Popa et al <Itron>

## Slide 4
Comments ID: 728, 1160
CID #728: The channel spacing for the mandatory data rate (50 kbps) in 915 MHz and 2.4 GHz bands should not be restricted to only 200 kHz. Switching from the MR-FSK mandatory 50 kbps / 200 kHz channel spacing to MR-FSK 150 ,200 kbps / 400 kHz, as well as when switching from the MR-FSK 50 kpbs / 200 kHz to MR-O-QPSK or OFDM adds useless design burden and might increase
the power consumption.
CID #1160: The channel spacing for the mandatory data rate (50 kbps) in 915 MHz and 2.4 GHz bands should not be
restricted to only 200 kHz. Switching from the MR-FSK mandatory 50 kbps / 200 kHz channel spacing to MR-FSK 150 , 200 kbps / 400 kHz, as well as when switching from the MR-FSK 50 kpbs / 200 kHz to MR-O-QPSK or OFDM adds useless design burden and might increase the power consumption.
Requested resolution: Add a new PIB attribute phyChannelSpacingCSM (integer value) that takes the following values: phyChannelSpacingCSM = 0 indicates the mandatory mode for MR-FSK uses 200 kHz channel spacing;
phyChannelSpacingCSM = 1 indicates the mandatory mode for MR-FSK uses 400 kHz channel spacing.
Response: Adding a new PIB attribute will challenge the interoperability goal because devices might not share the same context. Instead, a simpler solution consists in allowing MPM messages to be exchanged only on odd channel numbers. This is an additional benefit for FHSS, as it decreases the convergence time for the synchronization of unassociated devices.
Proposed resolution: Accept in principle. See slide 6 of document 15-10-0771-04-004g for resolution.
D. Popa et al <Itron>

## Slide 5: MPM messages
Exchanging MPM messages on odd channels doubles the probability of success and decreases the acquisition time for FH systems
Notes:
  A PHY capable to communicate in every channel can also communicate in a subset of channels
  This resolution does not add any additional requirements to the existing PHY
Channels
(200 kHz
0
1
2
3
4
5
6
7
8
Channels
(400 kHz
N-1
Odd channels
(200kHz)
D. Popa et al <Itron>

## Slide 6
Insert the following text
For a MR-FSK frequency hopping systems, MPM management scheme shall use only odd channel numbers.
D. Popa et al <Itron>