## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: TG4e Closing Report for Waikoloa Sep 2010
Date Submitted: 16 September 2010
Source: Pat Kinney Company: Kinney Consulting LLC
Voice:+1.847.960.3715, FAX: +1.630.524.9054, E-Mail:pat.kinney@ieee.org
Re: TG4e Closing Report for September 2010 Session
Abstract: Closing Report for the TG4e Session
Purpose: Amendments to IEEE 802.15.4 MAC
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: TG4e PAR Scope of Proposed Standard
The intention of this amendment is to enhance and add functionality to the 802.15.4-2006 MAC to a) better support the industrial markets and b) permit compatibility with modifications being proposed within the Chinese WPAN.
Specifically, the MAC enhancements are limited to:
TDMA: to provide a) determinism, b) enhanced utilization of bandwidth
Channel Hopping: to provide additional robustness in high interfering environments and enhance coexistence with other wireless networks
GTS: to increase its flexibility such as a) supporting peer to peer, b) the length of the slot, and c) number of slots
CSMA: to improve throughput and reduce energy consumption
Security: to add support for additional options such as asymmetrical keys
Low latency: to reduce end to end delivery time such as needed for control applications

## Slide 3: Purpose of Proposed Standard
This functionality facilitates Industrial applications (such as addressed by HART 7 and the ISA100 proposed standards), and those enhancements defined by the proposed Chinese WPAN standard that aren't included in TG4c. This amendment addresses coexistence with wireless protocols such as 802.11, 802.15.1, 802.15.3, and 802.15.4.

## Slide 4: Meeting Goals
Complete Letter Ballot 53 comment resolution
TG approval of comment resolutions and instruct editor(s) to modify draft document to incorporate changes as per comment resolution document
Request WG for a letter ballot of draft

## Slide 5: TG4e Meetings This Week
Mtg | Monday | Tuesday | Wed | Thursday
AM1 |  |  |  | 
AM2 | Opening Mtg Comment Review/Resolution | Comment Resolution | Comment Resolution | Comment resolution
PM1 | Comment Resolution | Comment Resolution | Comment Resolution | Comment resolution
PM2 | Comment Resolution | Comment Resolution | Comment Resolution | Comment resolution, closing logistics

## Slide 6: TG4e Accomplishments in Waikoloa
Approved revised multipurpose frame format capable of extensibility with selectable elided fields and information elements
Approved Enhanced Beacon Request and Enhanced Beacon capable of extensibility and serving needs such as informative exchange between devices
Completed resolution of LB53 comments marked as technical by commenter
Approved release of revised draft to letter ballot upon completion of editing by TG4e editors

## Slide 7: TG4e Schedule
Editing complete
TG4e Editor completion 8 Oct 2010
Letter Ballot Starts (30 day) 8 Oct 2010
Letter Ballot Closes 7 Nov 2010
Resolve comments & reballot Jan 2011
Sponsor Ballot Mar 2011
Comment resolution & reballot May 2011
IEEE RevCom approval Sep 2011

## Slide 8: TG4e Motion to approve draft standard and request WG for letter ballot
“That the 802.15 TG4e empowers the TG4e editors to revise P802-15-4e-d1_Draft_Amendment in accordance with the technical direction from the comment resolution document 15-10-0321-10-004e resulting in a revised draft amendment P802-15-4e-D2_Draft_Amendment.pdf, and in doing so approves taking it to the 802.15 WG to seek approval to go to Letter Ballot.”
Moved by Tim Godfrey
Seconded Myung Lee
TG4e Motion to Accept Draft by Task Group Passed Unanimously

## Slide 9: 802.15 WG Motion
Move that the 802.15 WG approve the start a WG Letter Ballot requesting approval to forward the P802.15.4e Draft D2 [d2P802-15-4e_Draft_Standard.pdf] to Sponsor Ballot pending the completion and inclusion of remaining edits to D1 [d1P802-15-4e_Draft_Standard.pdf] as per 15-10-0321-10 in the draft
Moved by Pat Kinney
Seconded by

## Slide 10: Conference Calls
No Task Group Calls are scheduled
Editor calls will occur as needed