## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Proposal for Resolution of Comments 946-947– LB59]
Date Submitted: [10 November 2010]
Source: [Roberto Aiello] [Larry Taylor]
Company: [Itron] [DTC]
E-Mail:[aiello@ieee.com][larry.taylor@acm.org]
Re: [LB#59 Comment resolution]
Abstract: [Suggested comment resolutions to MPM/CSM comments]
Purpose: [LB#59]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Proposed resolution for comments
CIDs # 946, 947
CID#s 923, 925, 1024, 1116
CIDs # 608, 941

## Slide 3
CID #946: Clause 5, Sub-Clause 5.5.5a
  Comment: Test states: "A SUN device implements at least one of the following PHYs: the MR-FSK PHY, the MR-OFDM PHY, or the MR-O-QPSK PHY". However, MPM is mandatory for MR-FSK and should be stated
  Proposed Change: correct text to reflect that MPM is mandatory
  Proposed Resolution ACCEPT IN PRINCIPLE
  See slide 7

## Slide 4
CID #947: Clause 5, Sub-Clause 5.5.5a
  Comment: MPM is to be used for Interoperatibility especially for the discovery and Join portions of networks
  Proposed Change: add text
  Proposed Resolution ACCEPT IN PRINCIPLE
  See slide 7

## Slide 5
CID #608: Clause 5, Sub-Clause 5.5.5a
  Comment: The text "facilitates negotiation among potential coordinators with different PHYs before these coordinators start their respective networks" is incorrect. CoEx Beacons are stated to be transmitted by Coordinators, not potential coordinators. A network must be operating before it can be detected using the MPM process.
  Proposed Change: Correct the description to say an operating network can be detected by a potential coordinator before that coordinator starts its network.
  Proposed Resolution ACCEPT IN PRINCIPLE
  See slide 7

## Slide 6
CID #941: Clause 5, Sub-Clause 5.5.5a
  Comment: It is not clear if a SUN compliant device needs to implement MPM
  Proposed Change: Add: A SUN device implements MPM
  Proposed Resolution ACCEPT IN PRINCIPLE
  See slide 7

## Slide 7: Proposed text
A SUN device supports implements at least one of the following PHYs: the MR-FSK PHY, the MR-OFDM PHY, or the MR-O-QPSK PHY. Given that three PHYs are defined within the application space, it is possible that multiple, different SUN PHYs may be operating in the same location and within the same frequency band. In order to mitigate interference, a multi-PHY management (MPM) scheme is specified to enable inter-PHY coexistence. For this purpose, the MPM scheme facilitates interoperability and negotiation among potential coordinators with different PHYs before these coordinators start their respective networks, by permitting a potential coordinator to detect an operating network during its discovery phase using By employing a common communication bridge known as the common signaling mode (CSM) appropriate to the band being used as defined in Table 6a.

## Slide 8
CID #923: Clause 7, Sub-Clause 7.5.8a
  Comment: text mandates that all devices compliant to SUN standard shall transmit and receive CSM and support coex-beacons even though devices operating in licensed bands do not need this mechanism since coexistence is secured via a license
  Proposed Change: either delete MPM or make it optional
  Proposed Resolution ACCEPT IN PRINCIPLE
    Only devices in regulatory domains with multiple specified PHYs (see Table 6a) are required to support the MPM. Other frequency bands are not subject to this rule. No change required.

## Slide 9
CID #925: Clause 6, Sub-Clause 6.1a
  Comment: subclause states "SUN device acting as a coordinator shall be able to transmit and receive in CSM" therefore all coordinators are mandated to be CSM capable when it is clear that this is not appropriate for all bands.
  Proposed Change: either delete MPM or make it optional
  Proposed Resolution ACCEPT IN PRINCIPLE
  See resolution for CID #923

## Slide 10
CID #1024: Annex D, Sub-Clause D.7.3.1
  Comment: MPM is mandatory according to the text
  Proposed Change: remove "capability to"
  Proposed Resolution ACCEPT
  Remove “capability to transmit and receive” from text

## Slide 11
CID #1166: Clause, Sub-Clause 6.1a
  Comment: "a coordinator shall be able to transmit and receive in CSM" does it mean it doesn't have to as long as it has the ability?
  Proposed Change: Change to "shall transmit and receive".
  Proposed Resolution ACCEPT IN PRINCIPLE
  Replace text with: “A SUN device acting as a coordinator, with a duty cycle greater than 1%, shall support CSM”

## Slide 12
CID #954: Clause, Sub-Clause 6.1a
  Comment: For a given band, a SUN device shall implement at least the mode of operation #1 (and mode of operation #2 for certain bands) of the MR-FSK PHY. The implementation of other MR-FSK PHY modes as well as all MR-OFDM and MR-OQPSK PHY modes are optional.
  Proposed Change: Change the sentence and clearly specify the MR-FSK modes that shall be implemented by a 4g devices for each band.
  Proposed Resolution ACCEPT in Principle
  Replace last sentence in paragraph (page 13, line 11): “A SUN device shall implement at least one of the SUN PHYs” with “A SUN device shall support the MR-FSK PHY”