## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title:[Summary of FCS group of comments]
Date Submitted: [Jan 18, 2011]
Source:[Ben Rolfe]
Company [BCA]
Address []
Voice: [+4.408.395.7207], FAX: [None], E-Mail: [ben @ blindcreek.com]
Re:[]
Abstract:[Summarizes the FCS group of comments from TTG4g LB59 as presented during the January 2011 ad hoc meeting]
Purpose:[support LB59 Comment resolution]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Summary
Comments examined: 171 301 436 695 730 1097
In the “importation” process of copying description from other 802 standards (802.15.3 and 802.11) a couple lines got left behind, which is the cause of most of these comments

## Slide 3: CID # 171
Correctly identifies the missing text
Accept and correct as indicated (restore lines inadvertently left out):
With this resolution, description is
  Complete
  Correct
  Consistent with how IEEE CRC-32 is specified in other 802 standards

## Slide 4: CID #730
Comment:
(a) Description is awkward and (b) would like a test vector (example )
Proposed Resolution: Accept in Principle
(a)The description (when corrected per CID#171 is identical to several 802 standards that use the same CRC and have been successfully implemented many millions (billions?) of times. It is not recommended we tread new ground, the risk seems great and reward minimal
(b) Agree a test vector would be helpful; suggest commenter work with commenter of CID#1097 to provide for inclusion in an informative annex.
Discussed with Commenter: Accepts resolution (a) as adequate if corrections applied per CID#171.
Recommended resolution: Correct text per CID #171.

## Slide 5: CID # 301
Comment identifies edge case – 802.15.4 ACK content (MHR = FCF + Seq Num = 3 octets)
What happens with less than 32 bits run through CRC 32? If result predictable, no action needed…othewise:
Suggested change:
  Add a generalized rule to pad value for < 4 octet MAC frame when using CRC32 (Pad doesn’t need to go over the air)

## Slide 6: CID # 301
New text (add to end of 7.2.1.9)
if the MPDU length is < 4 octets, upon transmission the FCS computation will assume padding the MPDU with zero value octets to exactly 4 octets MPDU length; upon reception when the MPDU length < 4 the received MPDU will be padded with zero value octets to exactly 4 octets MPDU length prior to computing the FCS for validation
Or technically equivalent text as determined by the editors.

## Slide 7: CID # 436
FCS Length field of the FSK PHR
  Commenter suggests a table to show more clearly the meaning of the field value.
Propose resolution: AP, Add a table:
Commenter reviewed and is satisfied
FCS used in PSDU | FCS Length field Value
32-bit FCS | 0
16-bit FCS | 1

## Slide 8: CID #695
Comment: Really need to signal FCS length in PHR?
Recommended resolution: Reject
Explanation:
  2 octet FCS sufficient for short frames and very low data rates, to be decided by the sending device
  Configuration via PIB by network management entity may suffice in some cases but not all and not precluded by current draft;
  OTA signaling useful in some network scenarios

## Slide 9: CID #1097
Commenter would like an example (test vector)
Comment # 730 also asks for a test vector
Proposed resolution: reject comment “The group does not believe a test vector is necessary as the description is adequate for implementation. “