## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title:[Summary of proposed resolutions – Comments assigned to “Rolfe”]
Date Submitted: [Jan 19, 2011]
Source:[Ben Rolfe]
Company [BCA]
Address []
Voice: [+4.408.395.7207], FAX: [None], E-Mail: [ben @ blindcreek.com]
Re:[]
Abstract:[Summarizes the Resolutions for comments to “Rolfe” per 0852r14 ]
Purpose:[support LB59 Comment resolution]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Summary
Delayed ACK: 59,470,502,623,681,889
Frame Format: 70
PIB: 73 76 237 822
Time: 214 328 336 380 682 737 739 887 920

## Slide 3: CID # 70
Proposed resolution: A
Note that in 802.15.4i roll-up field definitions are not repeated; the defintion of PSDU is given once in 10.1 and referenced in other PHY claues because all PPDU formats have the same definition of PSDU. Thus this sub-clause will be removed when aligned with the roll-up.

## Slide 4: Delayed ACK: 59,470,502,623,681,889
Resolution: Align with new ACKs in 15.4e:
The required ACK format (with addressing) is included in 4e draft already so use that form;
Asynchronous acknowledgment will be specified in 4e draft to use CSMA
Remove description of frame form 4g:
  All text in subclause 7.2.2.3
  Figure 91 and 91a
  Remove 7.2.2.3.1. This is to be included in 4e draft with definition of asynchronous acknowledgment.
Change references to “delayed acknowledgement” to “enhanced acknowledgement”.
7.5.6.4.2: Delete second sentence. Delete edits to 7.5.6.4.2 (“otherwise” not needed anymore). This information is being folded into 4e.
Change capabilities: bit name is “supports enhanced ack”, to “requires asynchronous ack” :
  If destination has indicated REQUIRES AA, only send AA; if capabilities has not been exchanged, use AA ;

## Slide 5: Enhanced ACK (EAck): CIDS 641, 686
Can use the addressing modes from the general frame control
Payload in IE’s - no “ack control” byte
Can use security
CCA optional (enabled via PIB)
macSecAckWaitDuration: The maximum time to wait for the PHY header of an enhanced acknowledgment frame to arrive following a transmitted data frame. Default setting of 864 μs. (table 86i) Note: MAC PIB attribute (r/w) may be set by a higher layer and should account for frame processing, latency, and back-off delays.
Enhanced ACK payloads are ignored if not understood by incoming frame originator but the frame is considered acknowledged.

## Slide 6: PIB: 73 76 237 822
# 73:
Clarify valid range of phyCurrentSUNPageEntry
AP
Valid range is correctly specified (as a range). Add reference to Figure 22a in attribute description.

## Slide 7: PIB: 73 76 237 822
# 76:
Improve description of phySUNPageEntriesSupported
Accept.

## Slide 8: PIB: 73 76 237 822
# 237:
Improve description of phySUNPageEntriesSupported
Accept.

## Slide 9: PIB: CID # 822
Comment: "Only one bit" is confusing. It is a bitmap and more than one bit may be set in the bitmap. [refers to phyCurrentSUNPageEntry ]
Accept in Principle: revise description consistent with P802.15.4i-D04 convention for specifying a collection.
Description becomes:
“For channel page 7 or 8, indicates the current PHY mode. For channel page 7, the current mode is one of the standard-defined modes. For channel page 8, the value is the index into phySUNGenericPHYDescriptors. See table 22a.”